## Slide 1: Modeling Basic Operations and Inputs
Chapter 4
Last revision June 7, 2003

## Slide 2: What We’ll Do ...
Model 4-1: Electronic assembly/test system
  Modeling approaches
  New Arena modules (Decide, Record)
Model 4-2: Enhanced electronic assembly/test
  Resource Schedules, States, and Failures
  Frequency outputs
  More on utilizations
Model 4-3: Enhancing the animation
  Queues, Entity Pictures, Resource Pictures
  Adding Plots and Variables

## Slide 3: What We’ll Do ... (cont’d.)
Model 4-4: Adding entity travel times
  Modify with Stations, Transfers, Routes, animation of entity movement
Input analysis
  Specifying input distributions, parameters
  Deterministic vs. random input
  Collecting and using data
  Fitting input distributions via the Input Analyzer
  No data?
  Nonstationary arrival processes
  Multivariate and correlated input data

## Slide 4: Electronic Assembly/Test System (Model 4-1)
Produce two different sealed elect. units (A, B)
Arriving parts: cast metal cases machined to accept the electronic parts
Part A, Part B – separate prep areas
Both go to Sealer for assembly, testing – then to Shipping (out) if OK, or else to Rework
Rework – Salvaged (and Shipped), or Scrapped

## Slide 5: Part A
Interarrivals: expo (5) minutes
From arrival point, proceed immediately to Part A Prep area
  Process = (machine + deburr + clean) ~ tria (1,4,8) minutes
Go immediately to Sealer
  Process = (assemble + test) ~ tria (1,3,4) min.
  91% pass, go to Shipped; Else go to Rework
Rework: (re-process + testing) ~ expo (45)
  80% pass, go to Salvaged; Else go to Scrapped

## Slide 6: Part B
Interarrivals: batches of 4, expo (30) min.
Upon arrival, batch separates into 4 individual parts
From arrival point, proceed immediately to Part B Prep area
  Process = (machine + deburr +clean) ~ tria (3,5,10)
Go to Sealer
  Process = (assemble + test) ~ weib (2.5, 5.3) min. , different from Part A, though at same station
  91% pass, go to Shipped; Else go to Rework
Rework: (re-process + test) = expo (45) min.
  80% pass, go to Salvaged; Else go to Scrapped

## Slide 7: Run Conditions, Output
Start empty & idle, run for four 8-hour shifts (1,920 minutes)
Collect statistics for each work area on
  Resource utilization
  Number in queue
  Time in queue
For each exit point (Shipped, Salvaged, Scrapped), collect total time in system (a.k.a. cycle time)

## Slide 8: Developing a Modeling Approach
Define pieces of model, modules, data structures, control logic
Appropriate level of detail – judgment call
Often multiple ways to model, represent logic
This model:
  Entities are the individual parts (two types)
  Separate Create modules for two part types
  Separate Process modules for each Prep area
  Process modules for Sealer and Rework, each followed by a Decide module (2-way by Chance)
  Depart modules for Shipped, Salvaged, Scrapped
  Attribute Sealer Time assigned after Creates in Assign modules (parts have different times at the Sealer)
  Record modules just before Departs for time in system

## Slide 9: Building the Model
New model window
Attach Basic Process panel (if needed)
Place modules
  Create (x 2)
  Assign (x 2)
  Process (x 4)
  Decide (x 2)
  Record (x 3)
  Dispose (x 3)
Right click — repeat last action (place module)
Auto-Connect, or manually connect via
Alternate strategy – place one module at a time, fill it out completely

## Slide 10: Part A Create Module
Name: Part A Arrive
Entity Type: Part A
Time Between Arrivals
  Type: Random (Expo)
    Pull-down list with options
  Value: 5
  Units: Minutes
    Pull-down list with options
Default what’s not mentioned above
Once these entries are made, they are placed on the list for names of that type (Module Name, Entity Type, etc.) and will appear on future pull-down lists for that type of name.

## Slide 11: Part B Create Module
Name: Part B Arrive
Entity Type: Part B
Time Between Arrivals
  Type: Random (Expo)
    Pull-down list with options
  Value: 30
  Units: Minutes
    Pull-down list with options
Entities per Arrival: 4

## Slide 12: Part A Attributes Assign Module
Name: Assign Part A Sealer and Arrive Time
Add button:
  Type: Attribute
  Attribute Name: Sealer Time
  New Value: TRIA(1, 3, 4)
Add button:
  Type: Attribute
  Attribute Name: Arrive Time
  New Value: TNOW (to compute time in system on exit)
TNOW is the internal Arena variable name for the simulation clock; see
Help > Arena Help > Contents >
Variables, Functions, and Distributions > Date and Time Variables

## Slide 13: Part B Attributes Assign Module
Name: Assign Part B Sealer and Arrive Time
Add button:
  Type: Attribute
  Attribute Name: Sealer Time
  New Value: WEIB(2.5, 5.3)
Add button:
  Type: Attribute
  Attribute Name: Arrive Time
  New Value: TNOW
Names for things in Arena
– Default names usually suggested
– Names placed on appropriate pull-down lists for future reference
– All names in a model must be unique (even across different kinds of objects)

## Slide 14: Process Module Actions
Delay
  Entity just sits here for the specified time; no Resource involved, so multiple entities could be undergoing this Delay simultaneously
Seize Delay
  Entity must first Seize the specified number of units of a Resource (possibility for Queueing if they’re not available), then undergoes the Delay … assume that the entity will Release the Resource units at another downstream module
Seize Delay Release
  Like Seize Delay, but entity releases Resource units after Delay (what we want in this model)
Delay Release
  Assumes entity had already Seized Resource units at another upstream module, now Delays and Releases Resource units

## Slide 15: Prep A Process Module
Name: Prep A Process
Action: Seize Delay Release
Resources subdialog (Add button):
  Type: Resource (a pull-down option)
  Resource Name: Prep A
  Quantity: 1 (default)
Delay Type: Triangular
Units: Minutes
Minimum: 1
Value (Most Likely): 4
Maximum: 8
If several Resources were named (Add button), entity would have to Seize them all before the Delay could start.

## Slide 16: Prep B Process Module
Name: Prep B Process
Action: Seize Delay Release
Resources subdialog (Add button):
  Type: Resource (a pull-down option)
  Resource Name: Prep B
  Quantity: 1 (default)
Delay Type: Triangular
Units: Minutes
Minimum: 3
Value (Most Likely): 5
Maximum: 10

## Slide 17: Sealer Process Module
Name: Sealer Process
Action: Seize Delay Release
Resources subdialog (Add button):
  Type: Resource (a pull-down option)
  Resource Name: Sealer
  Quantity: 1 (default)
Delay Type: Expression
Units: Minutes
Expression: Sealer Time
Recall – Sealer Time attribute was defined upstream for both Parts A and B … now its value is being used … allows for different distributions for A and B.

## Slide 18: Sealer Inspection-Result Decide Module
Decide module provides branch points
  By Condition (entity Attributes, global Variables)
  By Chance (multi-sided, possibly-biased hypercoin flip)
Name: Failed Sealer Inspection
Type: 2-way by Chance (default)
Percent True: 9
Different exit points for True, False results – connect appropriately downstream
Note it’s percent true, not probability of true … so “9” means probability of 0.09
We arbitrarily decided “true” meant part failed inspection … could have reversed (but would change numerical results ... why? ... does this upset you? ... why?)
This is a rich, deep, versatile module … explore its Help button

## Slide 19: Rework Process Module
Name: Rework Process
Action: Seize Delay Release
Resources subdialog (Add button):
  Type: Resource (a pull-down option)
  Resource Name: Rework
  Quantity: 1 (default)
Delay Type: Expression
Units: Minutes
Expression: EXPO(45)
Had to use the general Expression choice for Delay Type since what we want (EXPO) is not directly on the Delay Type pull-down list.

## Slide 20: Rework Inspection-Result Decide Module
Name: Failed Rework Inspection
Type: 2-way by Chance (default)
Percent True: 20
We arbitrarily decided “true” meant part failed inspection

## Slide 21: Record Modules
Arena collects and reports many output statistics by default, but sometimes not all you want
We want time in system (average, max) of parts sorted out by their exit point (Shipped, Salvaged, Scrapped)
  It’s this sorting that Arena doesn’t do by default ... it would automatically sort by Entity Type if we had Entities checked in Run > Setup > Project Parameters (which we don’t)
Record module can be placed in the flowchart to collect and report various kinds of statistics from within the model run as entities pass through it
For Tally-type output performance measures (see Chapter 3)

## Slide 22: Shipped Parts Record Module
Name: Record Shipped Parts
Type: Time Interval
  This option records the length of time that elapsed up to now (TNOW) from when an entity attribute was marked with a time “stamp” upstream ... Attribute Name is below ...
  There are several other options for Type … explore via Record module’s Help button!
Attribute Name: Arrive Time
  Was defined upstream as the clock value in the Assign modules instantly after each entity was Created
Tally Name: Record Shipped Parts
  Determines the label in the reports
Other two Record modules –
just like this except for Name and Tally Name.

## Slide 23: Dispose Modules
Three separate exit points for three separate part disposition (Shipped, Salvaged, Scrapped)
Could have directed all three exit types to a single Dispose module
  But having separate ones produces animation counts of the three dispositions
Also, having separate Dispose modules allows for differentially checking the boxes to Record Entity Statistics
  Produces flow statistics separated by entity type (if Entities Statistics Collection is checked in Run > Setup > Project Parameters), not by final disposition of part … so we did need our Record modules and Arrive Time attribute

## Slide 24: Run > Setup for Run Control
Without this, model would run forever – no defaults for termination rule
  That’s part of modeling, and generally affects results!
Project Parameters tab:
  Fill in Project Title, Analyst Name
  Defaults for Statistics Collection, but we cleared the check box for Entities – not needed for what we want (we installed our own Record modules), and would slow execution
Replication Parameters tab:
  Replication length: 32, accept Hours default for Time Units
  Base Time Units: Minutes for inputs without Time Units option, internal arithmetic, and units on output reports

## Slide 25: Different Part A, B Entity Pictures
Entity data module (just single-click on it in Project Bar, edit via spreadsheet only)
Row for each Entity Type (Part A, Part B)
Pull down Initial Picture pull-down menu, select different pictures for each Entity Type
  Edit > Entity Pictures to see, change the list of pictures that’s presented here … more later

## Slide 26: Running the Model
Check (if desired)
  Find button to help find errors
Go (will automatically pre-Check if needed)
  Some graphics don’t show during run … will return when you End your run … control via View > Layers
  Status Bar shows run progress – replication number, simulation time, simulation status
Animation speed – increase (>), decrease (<)
Pause ( ) or Esc key; to resume
Run > Step ( ) to debug
Run > Fast-Forward ( ) to turn off animation
  Run > Run Control > Batch Run (No Animation) is fastest

## Slide 27: Viewing the Results
Counters during animation for modules
  Create, Dispose, Decide – incremented when entity leaves
  Process – number of entities currently in the module
Asked at end if you want to see reports
  What you get depends on Run > Setup > Project Parameters
    Looks like the Rework area is a bottleneck ... more later
  Navigate through report with browsing arrows, tree at left
  Tally, Time-Persistent, and Counter statistics
  Avg, Min, Max, and 95% Confidence Interval half-widths
    Confidence intervals are for steady-state expectations … more later
    May not be produced if run is not long enough for reliable stats
Generally difficult/unreliable to draw conclusions from just one run … more later

## Slide 28: Model 4-2: The Enhanced Electronic Assembly and Test System
A Story
  Original model shown to production manager
  Pointed out that this is only the first shift of a two-shift day — on second shift there are two operators at Rework (the bottleneck station) … 16-hour days
  Pointed out that the Sealer fails sometimes
    Uptimes ~ exponential, mean 2 hours
    Repair times ~ exponential, mean 4 minutes
  Wants to buy racks to hold rework queue
    A rack holds 10 parts
    How many racks should be bought?
  Run for 10 days
Need: Resource Schedules, Resource States, Resource Failures

## Slide 29: Change Run Conditions
Redefine a “day” to be 16 hours – Run > Setup > Replication Parameters
Change Replication Length to 10 (of these) days

## Slide 30: Schedules
Vary Capacity (number of units) of a resource over time
In Resource Data module (spreadsheet view)
  For Rework Resource, change Type from Fixed Capacity to Based on Schedule
  Two new columns – Schedule Name and Schedule Rule
  Type in a schedule name (Rework Schedule)
  Select a Schedule Rule – details of capacity decrease if the Resource is allocated to an entity
    Ignore – Capacity goes down immediately for stat collection, but work goes on until finished … “break” could be shorter or gone
    Wait – Capacity decrease waits until entity releases Resource, and “break” will be full but maybe start/end late
    Preempt – Processing is interrupted, resumed at end of “break”

## Slide 31: Schedules (cont’d.)
Define the actual Schedule the Resource will follow – Schedule data module (spreadsheet)
  Row already there since we defined Rework Schedule
  Format Type is Duration for entries based on time past simulation beginning
  Type is Capacity, for Resource schedule (more later on Arrival Type)
  Click in Durations column, get Graphical Schedule Editor
    X-axis is time, Y-axis is Resource Capacity
    Click and drag to define the graph
    Options button to control axis scaling, time slots in editor, whether schedule loops or stays at a final level forever
    Can use Graphical Schedule Editor only if time durations are integers, and there are no Variables or Expressions involved

## Slide 32: Schedules (cont’d.)
  Alternatively, right-click in the row, select Edit via Dialog
    Enter schedule Name
    Enter pairs for Capacity, Duration … as many pairs as needed
      If all durations are specified, schedule repeats forever
      If any duration is empty, it defaults to infinity
    Can involve Variables, Expressions
  Another alternative – right-click in the row, select Edit via Spreadsheet
    Enter capacity Value, Duration pairs

## Slide 33: Resource Failures
Usually used to model unplanned, random downtimes
Can start definition in Resource or Failure module (Advanced Process panel) … we’ll start in Failure
Attach Advanced Process panel if needed, single-click on Failure, get spreadsheet view
To create new Failure, double-click – add new row
Name the Failure
Type – Time-based, Count-based (we’ll do Time)
Specify Up, Down Time, with Units

## Slide 34: Resource Failures (cont’d.)
Attach this Failure to the correct Resource
  Resource module, Failures column, Sealer row – click
  Get pop-up Failures window, pick Failure Name Sealer Failure from pull-down list
  Choose Failure Rule from Wait, Ignore, Preempt (as in Schedules)
Can have multiple Failures (separate names)
Can re-use defined Failures for multiple Resources (operate independently)

## Slide 35: Frequencies
Record time-persistent occurrence frequency of variable, expression, or resource state
  Use here to record % of time rework queue is of length 0, (0, 10], (10, 20], … to give info on number of racks needed
Statistic data module (Advanced Process panel)
  Five Types of statistics, of which Frequencies is one
  Specify Name (Rework Queue Stats), Frequency Type (Value)
  Specify Expression to track and categorize
    Right-click in field to get to Expression Builder
  Report Label (Rework Queue Stats)
  Pop-up secondary spreadsheet for Categories (browse file)

## Slide 36: Frequencies (cont’d.)
Add another Frequency (in Statistic module) to give a finer description of the Sealer states
  Will produce statistics on proportion of time Sealer is in each of its three possible states – Busy, Idle, and Failed
Frequencies are not part of default Category Overview report – open Frequencies report from Project Bar (get a separate window for them)

## Slide 37: Results of Model 4-2
Differ from those of Model 4-1 since this is a longer run, modeling assumptions are different
  All of which causes underlying random-number stream to be used differently (Chapter 12)
Prep A/B didn’t change (other than run length and random variation) … need statistical analysis of simulation output (Chapters 6, 7, 12)
Sealer is more congested (it now fails)
Rework is less congested (50% higher staffing)
Frequencies report suggests one rack suffices about 95% of the time, two racks all the time
  See text for discussion of Standard, Restricted Percents

## Slide 38: Utilizations – Some Fine Points
Two utilizations reported for each Resource
  Instantaneous Utilization is the time-average of the ratio of the number of units that are busy to the number of units that are scheduled
    By definition, counts periods when zero units are scheduled as zero-utilization periods
  Scheduled Utilization is the average number busy divided by the average number available
    No division-by-zero problem, assuming there were ever any units of the Resource scheduled at all (if not, it shouldn’t be in the model)
Identical for fixed-capacity Resource
Can differ for Resources on a variable Schedule
  If Resource capacity varies among several different positive values, it’s better to use Scheduled Utilization
  See text for discussion of issues and even finer points

## Slide 39: Model 4-3: Enhancing the Animation
Get “Spartan” generic default animation for some things (queues, connector-animation movement)
  Usually sufficient for verification, validation
Often want to customize, enhance it a bit
  More realism, impact
Can pull animation away from model logic in model window
  Useful for big models, complex animation
  Set up Named Views for model logic, animation, or close-ups of parts of animation
Animation objects are connected to model logic
  Identifiers, physical location (Shift-drag to decouple)

## Slide 40: Changing Animation Queues
Lengthen (click, drag, maybe hold shift) to “hold” more entities
  Simulation logic, results still OK even if animated queue overflows
Rotate to re-orient for realism
Change the “form” of the queue from Line (the default) to Point — fixed places for entities
  Double-click on the queue
  Select Type to be Point
  Click Points… button
  Successively click Add for points, then OK
  Drag them around on screen
  Check Rotate box to show entities turning

## Slide 41: Changing the Entity Pictures
Earlier – used Entity data module to assign different Initial Pictures to different Entity Types
Now – customize the list, or alter the pictures in it
  Edit > Entity Pictures
  Left column – names, pictures currently on the list
  Right column –picture libraries (.plb filename extension)
  Add a hand-drawn picture – Add button on left, name it in Value field at top, double-click on blank depressed button, then artwork (or paste in a copied graphics image)
    New name won’t appear in Entity data module until you type it there
  Edit an existing picture – double-click, artwork
  Copy a picture over from picture library

## Slide 42: Adding Resource Pictures
Animate a Resource – Resource button in animate toolbar – get Resource Picture Placement window
Left column – default pictures for different Resource states
  Attach logically to a Resource by Identifier pull-down list
  Double-click to edit the artwork by hand, or paste in previously copied graphics images
  Seize area – where seizing entity will “reside”
  Multiple seize areas for multi-capacity Resources
Right column – picture libraries (.plb files) – can copy over to selected (depressed) state pictures
Accept window, cross hairs, click to place
  Resize, reposition later

## Slide 43: Adding Variables and Plots
Variable animation – just show a value of something as a number, watch it change
  Variable object from Animate toolbar
  Double-click, specify Expression to be shown (Expression Builder), and cosmetics
  Resize, reposition later
Dynamic animated plots – discussed in Chapter 3
Other animation objects from Animate toolbar
  Clock (TNOW), variety of formats
  Level (thermometer) animation
  Others discussed later

## Slide 44: Model 4-4: The Electronic Assembly and Test System with Part Transfers
Generalize Model 4-3
All part transfers now take 2 minutes (not instant) … want to model and animate
  Includes:
    Arriving parts to prep areas
    Departing parts to appropriate exit
    All internal part transfers
  Regardless of distance ... will fix this (unrealistic) assumption in Chapter 8

## Slide 45: New Arena Constructs
Station – location where some process occurs
  Arrivals, manufacturing cells, departures
  Each Station given a unique name
  Can serve as an entry point for a section of model logic
  Station marker represents a logical station in the flowchart/animation
Station Transfer – entities move between Stations without direct connection
  Several different types – we’ll use Routes here, which allow for positive transfer time, but no other delays like “room” on the transitway or transporters
  Route paths represent Routes in the flowchart/animation

## Slide 46: Adding the Route Logic – From Arrival
Stations and Station Transfers affect both the model logic and the animation
Start with Model 4-3 … change to Model 4-4
For incoming parts (A and B) delete connection from Assign modules to “Prep” Process modules
  Replace with Station/Route module pairs
    Station module (Advanced Transfer panel) – define entity’s current location
      Module Name vs. Station Name
    Route module (Advanced Transfer panel) – send entity out
      Route Time, Destination Station
  No direct connections exiting from the Route modules – Route module’s Destination Station Name defines that

## Slide 47: Adding the Remaining Route Logic
Add Station modules for entry to each Prep area
  Station names are Prep A Station, Prep B Station, and are the destination stations for Routes after arrivals
Process modules for Prep A, Prep B unchanged
After prep, entities connected to Route module to send to next station (sealer)
  Don’t need a separate Station module for outgoing side
Similar changes for rest of model
  Station modules for incoming parts into sealer, rework, each of three Record modules (entity exit points)
  Route modules for outgoing parts out of sealer inspection, rework inspection (two for each Decide module – pass/fail)
Could run model now, get correct results … but no animation of transfers …

## Slide 48: Why Not Just Add Delays?
Simpler approach than the above to getting the two-minute transfer times:
  Insert a Process module with Action = Delay for 2 minutes on each relevant connection
  Alternatively, use Delay module from Advanced Process panel
Actually this would work fine from modeling, numerical-output viewpoints
But it would not allow animation of part transfers, so we’ll proceed with the Stations and Routes

## Slide 49: Altering the Animation – Station Markers, Routes
Add animation for Stations and Routes
Station button , Animate Transfer toolbar
  Attach Identifier to it from pull-down list of station names
  Get cross hairs, place (click) marker in animation
  Can place several station markers for the same logical station (to represent incoming, outgoing sides)
  Can drag station markers around later
Route button from Animate Transfer toolbar
  Options for appearance of entities as they travel the route
  Get cross hairs; click in origin, destination Station Markers
    Intermediate clicks for corners along the route
  Can drag around endpoints, corners later

## Slide 50: Altering the Animation – Entity Pictures
Part B arrivals are in batches of four parts/batch
  But constant travel time to Prep B implies they travel “on top of each other” so it looks like just one part B
  Try – change Route time from 2 to EXPO(2), see separation along the route
Create illusion to animate the batch
  Assign module just after Part B Arrive
  Add assignment of Entity Picture to Picture.Batch B
  Edit > Entity Pictures to draw the new picture
    Copy Picture.Part B and rename it Picture.Batch B
    Double-click on picture, use Picture Editor to get four circles
  When batch arrives to Prep B, change to single circle
    Add Assign module after Prep B Arrival Station

## Slide 51: Input Analysis: Specifying Model Parameters, Distributions
Structural modeling: what we’ve done so far
  Logical aspects — entities, resources, paths, etc.
Quantitative modeling
  Numerical, distributional specifications
  Like structural modeling, need to observe system’s operation, take data if possible
Notes: <number>
<footer>
<header>
<date/time>

## Slide 52: Deterministic vs. Random Inputs
Deterministic: nonrandom, fixed values
  Number of units of a resource
  Entity transfer time (?)
  Interarrival, processing times (?)
Random (a.k.a. stochastic): model as a distribution, “draw” or “generate” values from to drive simulation
  Transfer, Interarrival, Processing times
  What distribution? What distributional parameters?
  Causes simulation output to be random, too
Don’t just assume randomness away — validity
Notes: <number>
<footer>
<header>
<date/time>

## Slide 53: Collecting Data
Generally hard, expensive, frustrating, boring
  System might not exist
  Data available on the wrong things — might have to change model according to what’s available
  Incomplete, “dirty” data
  Too much data (!)
Sensitivity of outputs to uncertainty in inputs
Match model detail to quality of data
Cost — should be budgeted in project
Capture variability in data — model validity
Garbage In, Garbage Out (GIGO)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 54: Using Data: Alternatives and Issues
Use data “directly” in simulation
  Read actual observed values to drive the model inputs (interarrivals, service times, part types, …)
    Arena ReadWrite module ... see Model 10-2
  All values will be “legal” and realistic
  But can never go outside your observed data
  May not have enough data for long or many runs
  Computationally slow (reading disk files)
Or, fit probability distribution to data
  “Draw” or “generate” synthetic observations from this distribution to drive the model inputs
  We’ve done it this way so far
  Can go beyond observed data (good and bad)
  May not get a good “fit” to data — validity?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 55: Fitting Distributions to Data with the Arena Input Analyzer
Assume:
  Have sample data: Independent and Identically Distributed (IID) list of observed values from the actual physical system
  Want to select or fit a probability distribution for use in generating inputs for the simulation model
Arena Input Analyzer
  Separate application, also accessible via Tools menu in Arena
  Fits distributions, gives valid Arena expression for generation to paste directly into simulation model
Notes: <number>
<footer>
<header>
<date/time>

## Slide 56: Fitting Distributions to Data with the Arena Input Analyzer (cont’d.)
Fitting = deciding on distribution form (exponential, gamma, empirical, etc.) and estimating its parameters
  Several different methods (Maximum likelihood, moment matching, least squares, …)
  Assess goodness of fit via hypothesis tests
    H0: fitted distribution adequately represents the data
    Get p value for test (small = poor fit)
Fitted “theoretical” vs. empirical distribution
Continuous vs. discrete data, distribution
“Best” fit from among several distributions
Notes: <number>
<footer>
<header>
<date/time>

## Slide 57: Data Files for the Input Analyzer
Create the data file (editor, word processor, spreadsheet, ...)
  Must be plain ASCII text (save as text or export)
  Data values separated by white space (blanks, tabs, linefeeds)
  Otherwise free format
Open data file from within Input Analyzer
  File > New or
  File > Data File > Use Existing or
  Get histogram, basic summary of data
  To see data file: Window > Input Data
Can generate “fake” data file to play around
  File > Data File > Generate New
Notes: <number>
<footer>
<header>
<date/time>

## Slide 58: The Fit Menu
Fits distributions, does goodness-of-fit tests
Fit a specific distribution form
  Plots density over histogram for visual “test”
  Gives exact expression to Copy and Paste (Ctrl+C, Ctrl+V) over into simulation model
  May include “offset” depending on distribution
  Gives results of goodness-of-fit tests
    Chi square, Kolmogorov-Smirnov tests
    Most important part: p-value, always between 0 and 1:
      Probability of getting a data set that’s more inconsistent with the fitted distribution than the data set you actually have, if the the fitted distribution is truly “the truth”
      “Small” p (< 0.05 or so): poor fit (try again or give up)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 59: The Fit Menu (cont’d.)
Fit all of Arena’s (theoretical) distributions at once
  Fit > Fit All or
  Returns the minimum square-error distribution
    Square error = sum of squared discrepancies between histogram frequencies and fitted-distribution frequencies
    Can depend on histogram intervals chosen: different intervals can lead to different “best” distribution
  Could still be a poor fit, though (check p value)
  To see all distributions, ranked: Window > Fit All Summary or
Notes: <number>
<footer>
<header>
<date/time>

## Slide 60: The Fit Menu (cont’d.)
“Fit” Empirical distribution (continuous or discrete): Fit > Empirical
  Can interpret results as a Discrete or Continuous distribution
    Discrete: get pairs (Cumulative Probability, Value)
    Continuous: Arena will linearly interpolate within the data range according to these pairs (so you can never generate values outside the range, which might be good or bad)
  Empirical distribution can be used when “theoretical” distributions fit poorly, or intentionally
Notes: <number>
<footer>
<header>
<date/time>

## Slide 61: Some Issues in Fitting Input Distributions
Not an exact science — no “right” answer
Consider theoretical vs. empirical
Consider range of distribution
  Infinite both ways (e.g., normal)
  Positive (e.g., exponential, gamma)
  Bounded (e.g., beta, uniform)
Consider ease of parameter manipulation to affect means, variances
Simulation model sensitivity analysis
Outliers, multimodal data
  Maybe split data set (see textbook for details)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 62: No Data?
Happens more often than you’d like
No good solution; some (bad) options:
  Interview “experts”
    Min, Max: Uniform
    Avg., % error or absolute error: Uniform
    Min, Mode, Max: Triangular
      Mode can be different from Mean — allows asymmetry
  Interarrivals — independent, stationary
    Exponential— still need some value for mean
  Number of “random” events in an interval: Poisson
  Sum of independent “pieces”: normal
  Product of independent “pieces”: lognormal
Notes: <number>
<footer>
<header>
<date/time>

## Slide 63: Cautions on Using Normal Distributions
Probably most familiar distribution – normal “bell curve” used widely in statistical inference
But it has infinite tails in both directions … in particular, has an infinite left tail so can always (theoretically) generate negative values
  Many simulation input quantities (e.g., time durations) must be positive to make sense – Arena truncates negatives to 0
If mean  is big relative to standard deviation , then P(negative) value is small … one in a million
But in simulation, one in a million can happen
Moral – avoid normal distribution as input model

## Slide 64: Nonstationary Arrival Processes
External events (often arrivals) whose rate varies over time
  Lunchtime at fast-food restaurants
  Rush-hour traffic in cities
  Telephone call centers
  Seasonal demands for a manufactured product
It can be critical to model this nonstationarity for model validity
  Ignoring peaks, valleys can mask important behavior
  Can miss rush hours, etc.
Good model: Nonstationary Poisson process
Notes: <number>
<footer>
<header>
<date/time>

## Slide 65: Nonstationary Arrival Processes (cont’d.)
Two issues:
  How to specify/estimate the rate function
  How to generate from it properly during the simulation
Several ways to estimate rate function — we’ll just do the piecewise-constant method
  Divide time frame of simulation into subintervals of time over which you think rate is fairly flat
  Compute observed rate within each subinterval
  In Arena, must convert to expected number of arrivals per hour on subintervals of time that need not be of one-hour length
    Want expected 45 arrivals in a half hour; specify rate = 90 per hour
Example: Model 5-2 in Chapter 5
Notes: <number>
<footer>
<header>
<date/time>

## Slide 66: Multivariate and Correlated Input Data
Usually we assume that all generated random observations across a simulation are independent (though from possibly different distributions)
Sometimes this isn’t true:
  A “difficult” part requires long processing in both the Prep and Sealer operations
  This is positive correlation
Ignoring such relations can invalidate model
See textbook for ideas, references
Notes: <number>
<footer>
<header>
<date/time>