## Slide 1: Entity Transfer
Chapter 8
Last revision June 9, 2003

## Slide 2: What We’ll Do ...
Types of Entity Transfers
Model 8-1: Resource-Constrained Transfers
Models 8-2, 8-3: Transporters
Conveyors
  Model 8-4: Non-accumulating
  Model 8-5: Accumulating

## Slide 3: Types of Entity Transfers So Far
Connect
  Zero-delay
  Connection graphic vs. module Labels (no graphic)
Route
  Non-zero-delay — constant, r.v., expression
  Stations, animated Routes
  Fixed routes vs. entity-dependent Sequences
Connect and Route both assume:
  No limit on number in transit at a time
  Entities have their own feet

## Slide 4: New Types of Entity Transfers
Resource-constrained transfers
  Limit total number of entities in transit at a time
  Entities still have their own feet
  Telecommunications (number of packets), logistics (number of vehicles)
Material-handling devices
  Transporters – fork lifts, trucks, carts, wheelchairs
    Usually place limits on numbers, capabilities of transporters
    Like a Resource, except moveable
  Conveyors
    Belts, hook lines, escalators
    Usually limit space on conveyor, speed
    Non-accumulating vs. accumulating

## Slide 5: Model 8-1: Small Manufacturing System with Resource-Constrained Transfers
Original system (Model 7-1)
  Assumed all transfer times = 2 minutes … keep (for now)
  Parts have their own feet … keep (for now)
  No limit on number of parts in transit at a time … dump
    Now – no more than 2 parts can be in motion at a given time
    If other parts are ready to go, they must wait until there’s room to go
Model via existing constructs — think creatively
  Model “space” on the “road” as a Resource
  Limit the number of Units of this Resource
  Entity must Seize unit of “space” resource before beginning trip, Release it at end of trip

## Slide 6: Two Ways to Model Resource-Constrained Transfers
Both use a new Transfer Resource representing space on the transitways
  Capacity set to 2 in Resource data module
Maybe the most obvious way (but won’t do) …
  Before each Route module insert a Seize module to Seize one unit of Transfer (queue, priority details … see text)
  After each Station module (except Order Release) insert a Release module to free up one unit of Transfer

## Slide 7: Two Ways to Model Resource-Constrained Transfers (cont’d.)
Different way (will do, to illustrate new modules, set up for transporters and conveyors) …
  Replace Route modules with Leave modules (Advanced Transfer panel)
    Transfer Out: Seize unit of Transfer resource before leaving station
      Resource, Resource Set, particular member of a Resource Set
      Can specify priorities
    Also contains the Route operation
    Get individual queues, with animation, for parts waiting to go
  Replace Station modules with Enter modules (Advanced Transfer panel)
    Defines the Station
    Option of an unload Delay time (0 for this model)
    Transfer In: Release Transfer resource
Effect – slight increase in cycle times in system

## Slide 8: Transporter Concepts
Carts, fork lifts, trucks, wheelchairs, people, …
When entity is ready to go somewhere, it needs to be “picked up” and moved
Use Transporters — “moveable” resources
Activities: Request, Transport, Free
  Transporter Selection Rule: If > 1 transporter is available when Requesting
  When freed and > 1 entity is waiting: Priorities, closest one
Two types of Transporters
  Free-Path (we’ll do)
    Travel time depends only on velocity, distance
    Ignore “traffic jams” and their resulting delays
  Guided (won’t do)
    AGVs, intersections, etc.

## Slide 9: The Small Manufacturing System with Transporters
Have two carts to transport parts
  A cart can carry one part at a time
  Carts move at 50 feet/minute
    Will need to specify accurate distances between Stations
  It takes 0.25 minute to load part on a cart, 0.25 minute to unload it from a cart
Modify Model 8-1 to Model 8-2

## Slide 10: The Small Manufacturing System with Transporters (cont’d.)
Create Transporter in Transporter data module (Advanced transfer panel)
  Name = Cart, Capacity = 2, Velocity = 50
  Default the Distance Set (later), Units = Per Minute, Initial Positions
    Mind the units – consistency here, in Distance Set (later)
Animation picture for Cart Transporter
  Transporter button , Animate Transfer toolbar
  Identifier = Cart, pictures for Idle, Busy, Inactive states
  Draw or copy from .plb picture libraries
  Ride point (details in book)
  Drop it anywhere in flowchart view (hidden during run)

## Slide 11: The Small Manufacturing System with Transporters (cont’d.)
Request a Cart – modify existing Leave modules
  Delay = 0.25 Minute for load time
  Transfer Out = Request Transporter
  Transporter Name = Cart
  Selection Rule = Smallest Distance
    Applies when > 1 transporter is available
    Others: Cyclic, Random, Preferred Order, Largest Distance (???)
  Save Attribute = Cart # (remember which cart … for later)
  Connect Type = Transport
    Move Time disappears … determined by Velocity, Distances (later)
  Station Type = Sequence
Instead of Leave: Request-Delay-Transport
  More complex, more flexible – book has details, examples

## Slide 12: The Small Manufacturing System with Transporters (cont’d.)
Free the Cart – modify existing Enter modules
  Delay = 0.25 Minute for unload time
  Transfer In = Free Transporter
  Transporter Name = Cart
  Unit Number = Cart # attribute of part entity
Instead of Enter: Station-Delay-Free
  More complex, more flexible – book has details, examples

## Slide 13: Distances for Transporters
Define contents of Distance Set Cart.Distance
Distances (in feet) moved by parts:
  Blank cells: part movements that don’t occur
Enter these data in Distance data module (Advanced Transfer panel)
  Name = Cart.Distance
  Stations button, add 11 rows with Beginning Station, Ending Station, Distance for above data
  Direction is implied; could be asymmetric
Units!!
Units!!
Why are there 25 rows??

## Slide 14: Animating Transporter Movement
Add distances to animation
Delete all the old Route Path animation objects
  But leave the Station animations
Add animated transporter distances with Distance button , Animate Transfer toolbar
  Dialog, placement similar to Route Paths
  Identifier = Cart.Distance
  Click in Beginning Station marker, intermediate clicks, Ending Station marker
  Options for Rotate, Flip
  Grid, Snap to help place animated transporter distances

## Slide 15: Parking Areas for Transporters
Animate transporters when they’re free
Parking button , Animate Transfer toolbar
  Like a Queue animation – Point vs. Line, Shift, Rotate
  Cursor becomes cross hairs, click near lower left of Station marker to start, click for first Point or head of Line
  More clicks for more Points (double-click to end), or second click to end Line
  Want enough points/space for all transporters (2 here)
  Repeat for all Stations where Transporters could be freed

## Slide 16: More Distances — Empty Transporters
Above Distances incomplete — only for part movements along their sequences
Transporters must also move when empty (deadheading)
  In general, n(n - 1) distances need definition for network with n nodes
  Some not possible — Order Release to Exit System
14 more distances to define in Distances data module (not grayed):

## Slide 17: Model 8-3: Refining the Animation for Transporters
As it stands, Part Entities disappear from animation when waiting to be picked up by a Cart Transporter
  Model logic OK … get right answers … animation is flawed
Solution – Storage for entity to reside in, be animated, while it waits for something (here, a Cart Transporter)
  Can get statistics on numbers in Storages
But Storages not available with modules from Advanced Transfer panel
  Use lower-level SIMAN modules from Blocks panel … see book for specific details

## Slide 18: Conveyors
Replace Transporters with a conveyor
Loop conveyor to follow main path, clockwise
Six entrance/exit points
  Load, Unload takes 0.25 minute
  Each part is 4 feet per side, but want 6 feet of conveyor space for clearance on corners
Speed = 20 feet/minute
Distances:
Units!!

## Slide 19: Conveyor Concepts
Entity to be conveyed must wait for space
Conveyor consists of cells
  Equal size, constantly moving – think of a narrow escalator
Entities might require multiple contiguous cells
Must define cell size; tradeoff involved:
  Small cells: accurate model but slow execution
  Large cells: just the opposite!
Entities Access space, Convey, and Exit
Conveyor = series of linear Segments
  Each segment starts and ends at a Station
  Link to form loops, diverge points, converge points

## Slide 20: Types of Conveyors
Both travel in a single, irreversible direction
Nonaccumulating: belt, bucket line, escalator
  Spacing between entities on it doesn’t change
  Entire conveyor stops for entity Access/Exit if Load/Unload time is > 0
Accumulating: rollers, freeway
  Conveyor never stops moving
  If entity on it stops to Exit, other entities behind it are blocked and bunch up (entities ahead of it keep moving)
  When blockage ends, blocked entities go on but maybe not all at once (spacing requirements)

## Slide 21: Model 8-4: Small Manufacturing System with Nonaccumulating Conveyors
Modify Model 8-1 (resource-constrained transfer)
Define new Variables Load Time and Unload Time, each with initial value 0.25
Delete all the Route Paths
Define Conveyor via Conveyor data module, Advanced Transfer panel
  Conveyer = Loop Conveyor
  Segment Name = Loop Conveyor.Segment
  Type = Non-Accumulating
  Velocity = 20 (feet), Units = Per Minute
  Cell Size = 3 (feet)
  Max Cells Occupied = 2 (cells per entity)
Units!!
Units!!

## Slide 22: Leave, Enter Modules for Conveyor
Change each Leave module
  Delay = Load Time, Units = Minutes
  Transfer Out = Access Conveyor
  Conveyor Name = Loop Conveyor
  # of Cells = 2
  Connect Type = Convey
Change each Enter module
  Delay = Unload Time, Units = Minutes
  Transfer In = Exit Conveyor
  Conveyor Name = Loop Conveyor

## Slide 23: Conveyor Segments
Define one-way lengths (in feet) of segments
Segment data module, Advanced Transfer panel
  Name = Loop Conveyor.Segment
  Beginning Station = Order Release
  Next Stations button
    Name Next Station in correct sequence
    Give distance (in feet) to this next station
Segment animation
  Put Station markers in front of each Resource picture
  Segment button , Animate Transfer toolbar
  Dialog, crosshairs, clicking just like Distances for Transporters
    Except here, have to place only 6 Segment animations

## Slide 24: Conveyor Statistics
Run > Setup > Project Parameters to check Conveyor Statistics
Get percent of time blocked (stopped)
Utilization statistic is average percent of space occupied on conveyor (not percent of time that a part was on the conveyor)
To see conveyor stop (it’s nonaccumulating) more clearly, change Load Time and Unload Time to much greater values than 0.25
  Could do this during run with VBA (Chapter 10), or Run Controller – see text for details – but makes output statistics nearly impossible to interpret

## Slide 25: Model 8-5: Change Conveyors to Accumulating
Conveyor module
  Change Conveyor Type to Accumulating
  Accumulation Length = 4 (in feet), amount of space the accumulated parts need on the conveyor
Running, see very little accumulation in animation
  To see more, increase Load Time and Unload Time