## Slide 1: Continuous and Combined Discrete/ Continuous Models
Chapter 11
Last revision July 21, 2003

## Slide 2: What We’ll Do ...
What is a continuous system?
Simple linear continuous systems
Combined discrete/continuous systems
Non-linear and complex systems

## Slide 3: Continuous Systems
Discrete systems – State changes occur at isolated points in time called events
Continuous systems – State changes may occur continuously over time
  Flow of fluids and fluid-like materials
  Temperature changes
  Chemical operations
  Biological processes

## Slide 4: Continuous Systems
Simple systems (linear)
  Rate of change is constant between events
  Future value can be calculated from starting value and rate
  Can step directly to calculated event
Complex systems (non-linear)
  Rate of change may depend on other continuous processes
  Specialized approaches used to capture change
  Approximates continuous change by making a series of small steps between the usual discrete events

## Slide 5: Continuous Systems
Example of simple continuous system filling a tank smoothly over time

## Slide 6: Continuous Systems
Basic constructs: Levels & Rates from Elements Panel
A Level is the value that is changing over time
A Rate determines the rate of change of the level
Both are similar to Variables in that they can be assigned a new value at any time.
Levels may also change as time advances if the value of the associated Rate is non-zero.
A Level and a Rate should be used as a pair
  (e.g. If you have 4 Levels you should have 4 Rates)

## Slide 7: Simple Continuous Systems
Continuous Element specifies integration parameters:
  Number of Dif Equations – In simple systems, leave at default of number of Rate/Level pairs.
  Number of State Equations – Ignore in simple systems.
  Minimum step size – The minimum time advance between integration steps. Use 0.0 in simple systems.
  Maximum step size – The maximum time advance between integration steps. Use a high value (100) in simple systems.
  Save Point Interval – The maximum time between save points for recording continuous statistics (CSTATS).
  Method – Use Euler linear algorithm for simple systems.

## Slide 8: Simple Continuous Systems
Discrete control loop to empty and refill a tank

## Slide 9: Combined Discrete/Continuous
Detect Module from Blocks panel “watches” for and helps predict events.
Watches for value of a variable to cross a threshold value (e.g. a tank level reaching its maximum value)
Similar to Create Module in that an entity is created when crossing occurs.

## Slide 10: Combined Discrete/Continuous
Fill and empty logic using Detect modules

## Slide 11: Complex Systems
Non-linear systems require special algorithms like Runge-Kutta-Fehlberg (RKF).
Step sizes must be set carefully.
Smaller step size will generate more accurate results because Arena will calculate continuous-change variables more often.
Larger step size will run faster, but your error tolerances will need to be set higher.
Many situations (like a gravity fed tank) are actually non-linear, but can be accurately approximated with faster, linear methods.