## Slide 1: Asynchronous Transfer Mode
LAN
WAN

## Slide 2: Circuit Switching
Bandwidth allocated in fixed, inflexible increments
Applications get only fixed allocation of bandwidth
No Congestion Control or Bandwidth Sharing
Slow call establishment
Guaranteed throughput

## Slide 3: Packet Switching
Bandwidth is shared between all users
LAN applications contend for link access
No call establishment
No guaranteed performance
Full bandwidth available after link access
Performance is protocol sensitive

## Slide 4: LAN vs ATM
A LAN uses broadcast communications over a connectionless network service
A LAN uses variable length packets
ATM uses virtual circuit communications over a connection oriented network service
ATM uses fixed length packets called cells
  Cell length is 53 bytes
  Fixed cells length permits packet-based and stream based traffic to co-exist.

## Slide 5: Why was ATM Needed?
Need bandwidth allocated by design, not accident
Need Quality of Service management for multimedia applications
Need manageable delay, delay variation and packet loss for some applications
  Video conferencing
  Collaborative workgroup computing

## Slide 6: What is ATM?
ATM means Asynchronous Transfer Mode
Switched, connection oriented virtual circuit network technology
Supports voice, video, data, and image transmissions over the same link
Supports quality of service parameters
Multiple supported link speeds
  25 Mbps, 155 Mbps, 622 Mbps
  OC-3, OC-12, OC-48, OC-192

## Slide 7: Why Use ATM?
Supports voice, data, video, image, and multimedia over the same network with highly efficient bandwidth utilization
Common Internetworking technology for implementation in private and public networks
Connection oriented service using cell switching
Improved performance through streamlined error and flow control management
Notes: Switched network rather than a shared network allows for scalability.
Each switch added to the network actually increases bandwidth of the network.
There are trials in place in the US, and more extensively in Europe where ATM is used for the wide area network

## Slide 8: How ATM Works
All data is converted into 53 byte cells prior to transmission
  Cells streams can be multiplexed together
Switching is simplified because only cells are supported
  Hardware switching permits lower processing overhead
ATM benefits from both circuit and packet switching technologies

## Slide 9: Early ATM Evolution
1995
1997
UNI 3.0/3.1
1996
RFC 1577
LAN Emulation
Static Routing
622 Mbps PHY
ATM Layer Access Definition (API)
Congestion Control
P-NNI Routing
UNI 4.0
ABR
Multiprotocol Support

## Slide 10: How ATM Eliminates Delays
Fixed length cells
Variable length packets
F1
F1
F2
F3
F2
F1
F1
F1
F3
F3
F2
F3
F2

## Slide 11: ATM and the OSI RM
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
ATM Adaptation Layer
(AAL)
(Convergence SubLayer)
(Segmentation and Reassembly)
ATM Layer
(VPI & VCI Translation)
(Cell Header Generate/Extract)
Physical Layer
(Transmission Convergence)
(Physical Medium)

## Slide 12: ATM Network Environments
Service Provider
Enterprise WAN
Campus
PNNI
Public UNI
Public UNI
PNNI

## Slide 13: ATM Connections
VCI
VCI
VCI
VCI
VCI
VCI
VPI
VPI
VPI
Transmission
Path
PVC
or
SVC

## Slide 14: VP and VC Characteristics
Supports quality of service
Provides switched and semipermenant connections
Provides cell sequencing integrity
Supports traffic parameter negotiation
Permits usage monitoring
Provides restricted channels (VP only)

## Slide 15: ATM Virtual Path
Contains a bundle of virtual channels
Provides a simplified architecture
Increases performance and reliability
Reduces processing and connection time
Enhances services

## Slide 16: ATM Virtual Channel
Provides user to user connections
  PVCs or SVCs
Allows variable data rates
Uses fixed cell size
Provides full duplex connection
Supports user to network signaling
Supports network to network signaling
  Network management
  User messages

## Slide 17: Virtual Connections
Permanent Virtual Circuit (PVC)
  Dedicated physical lines.
  Connectivity is statically configured in the switches and endstations.
Switched Virtual Circuit (SVC)
  Created dynamically for each transmission.
  Similar to a voice telephone network.

## Slide 18: Permanent Virtual Connections
Manual configuration
Connections active for long periods of time
VPI/VCI tables required in all locations
Network
Management System
Switch
Switch
VPI/VCI
VPI/VCI
VPI/VCI
VPI/VCI

## Slide 19: Switched Virtual Connections
VPI/VCI = 0/5, Switch and terminal exchange signaling messages on this channel
VPI/VCI = 0/16, Interim Local Management Interface
VPI/VCIs: 0/0-31 are reserved
Signaling Channel:
VPI/VCI = 0/5
Switch
Signaling Channel:
VPI/VCI = 0/5

## Slide 20: ATM Network Interfaces
Private ATM Network
ATM
Switch
Router
with
ATM
Interface
UNI
UNI
PNNI
UNI
Public ATM Network
NNI
Public UNI
ATM
Switch
Public UNI
ATM
Switch
ATM
Switch
AT&T

AT&T

Router
with
ATM
Interface

## Slide 21: ATM Network Interfaces
User Network Interface (UNI)
  ATM switch to router interface
  ATM switch to workstation interface
Network to Network Interface (NNI)
  ATM switch to switch interfaces
  Private-NNI (PNNI)
  Public NNI

## Slide 22: UNI and NNI
User-to-Network Interface (UNI)
Network-to-Network Interface (NNI)
Integrated Interswitch Protocol (IISP)
Switch
Switch
NNI / IISP
UNI
UNI
UNI

## Slide 23: UNI and NNI
UNI 3.0 and 3.1 are not interoperable
  UNI 3.0 developed by ATM Forum
  UNI 3.1 aligned with ITU-T standard
Both have same functionality
UNI 4.0 is backward compatible with UNI 3.1
IISP provides static ATM routing
PNNI provides dynamic ATM routing
  PNNI replaced IISP

## Slide 24: ILMI
ATM Forum standard for network management
  Monitors transfers between switch and nodes
  Reports CRC error rates
  Tracks performance dips
  Provides address registration
    Used during station attachment to the ATM network
    Used during LANE initialization

## Slide 25: ATM Addressing
Byte 1 - Authority & Format Identifier
  Identifies address format
Bytes 2-13 - Network Prefix
  3 Formats - (DCC, ICD, E.164)
Bytes 14-19 - End Station Identifier
  Equivalent to MAC address
Byte 20 - Selector
  Not used by network
Network Prefix
ESI
Sel
AFI

## Slide 26: ATM Cell Characteristics
53 byte cell
  5 byte header
  48 byte payload
Header types
  User to network (UNI)
  Network to network (NNI)

## Slide 27: ATM Cell Structure
BYTE
8 7 6 5
4 3 2 1
BIT
1
2
3
4
5
6
...
53
Generic Flow Control
Virtual Path Identifier
Virtual Path Identifier
Virtual Channel Identifier
Virtual Channel Identifier
Virtual Channel Identifier
Payload Type
CLP
Header Error Control
Cell Payload
48 bytes
NNI - Generic Flow Control not used, field extends
size of Virtual Path Identifier to 12 bits.

## Slide 28: Payload Type Field
Bit 1
  0 = user
  1 = network (in band)
User bit 2
  0 = no congestion
  1 = congestion
User bit 3
  ATM user to ATM user (AAU)

## Slide 29: ATM Adaptation Layer
Adapts protocol frames to ATM cells
  PCM, LAPF, TCP/IP, etc. ….
Provides segmentation & reassembly
Supports timing and flow control
  Transmission errors
  Lost and mis-inserted cells

## Slide 30: ATM Adaptation Layer
AAL provides 4 different packet-to-cell conversions required for different data types
AAL performs Segmentation and Reassembly
  Normally done in hardware
AAL maintains cell sequencing
AAL 1 and AAL 5 are most widely supported

## Slide 31: ATM Adaptation Layer
AAL 1 - Supports isochronous traffic (CBR) for voice or video traffic
AAL 2 - Supports Variable Bit Rate data that requires transfer of timing between end points
AAL 3/4 - Connection or connectless VBR data traffic. Supports short, high bursty data generated at irregular intervals
AAL 5 - Most efficient way to support data traffic

## Slide 32: ATM Quality of Service Classes
Constant Bit Rate - guaranteed bandwidth for connection duration
Variable Bit Rate - guaranteed bandwidth for connection duration with a peak maximum burst size
Available Bit Rate - uses all bandwidth that is available at any instant
Unspecified Bit Rate - best effort delivery with no guarantee

## Slide 33: RFC 1483
Defines multiprotocol encapsulation for network traffic over AAL 5
  Routed Encapsulation
    Non-VC Multiplexing - protocol families share a VC
    LLC/SNAP Header identifies Protocol Type
    Used in RFC 1577
  Bridged Encapsulation
    Non-VC Multiplexing used for “Bridging over ATM”
      Used by pre-LANE products
    VC-Multiplexing - Protocol families on separate VCs
      Used by LANE products

## Slide 34: RFC 1577
Classical IP and ARP over ATM
  Defines the ATM address resolution protocol to map IP addresses to ATM addresses within a logical IP subnet.
  A group of IP Hosts on the same subnet are connected to a single ATM Network called a Logical IP Subnet
  ATM Address Resolution Server
  No Broadcasts
  No Routing

## Slide 35: ATM Forum LAN Emulation
A Media Access Control, MAC layer specification, known as LANE 1.0, that allows the ATM fabric to emulate a logical Ethernet or Token Ring segment.
Definitions:
  LAN Emulation User Network Interface - Referred to as “LANE 1.0”. It defines the interface between a legacy LAN attached device and the ATM network.
  LAN Emulation Services - They serve the following functions: initialization , address registration / resolution, and data forwarding. They consist of the LECS, LES, and BUS.

## Slide 36: ATM Forum LAN Emulation
Definitions (continued):
  LAN Emulation Configuration Server, LECS - Maintains the configuration information for each emulated LAN.
  LAN Emulation Server, LES - Performs the MAC-to-ATM address resolution functions in an emulated LAN.
  Broadcast Unknown Server, BUS - Performs the multicast server function and broadcasts packets to multiple LECs.
  LAN Emulation Client, LEC - Multiple LECs connect to the LANE services. Client functionalities are typically implemented on adapters, routers, and ATM-to-LAN edge devices.

## Slide 37: LAN Emulation
AAL 5 segments data frames into cells
ATM LAN Edge Device implements Proxy LANE Client and MAC Layer LANE
Proxy client forwards unregistered MAC addresses
Legacy LAN Host requires no changes
LANE emulates a bridged LAN segment

## Slide 38: LANE Protocol Stack
Application
NDIS/ODI Driver
LAN Emulation
AAL5
ATM
Physical
ATM
Physical
Physical
LAN
Emulation
AAL5
ATM
Physical
Application
MAC
Physical
NDIS/ODI
Driver
Physical
MAC
Bridging
Software
ATM Host
LAN Host
ATM LEC
“Edge Device”
ATM Switch

## Slide 39: LANE Network Configuration
Ethernet Network
LANE Clients
Proxy LEC
“Edge Devices”
Switch
PNNI
LANE Clients
LEC
UNI
Switch
Switch
Switch
Bridge
Bridge
Bridge
Token Ring
Network
Ethernet Network
LANE Servers
LECS, LES, BUS

## Slide 40: ATM Based LANs
Support multiple service classes
Support isochronous traffic
Scale to higher speeds
Permit dynamic performance level assignment

## Slide 41: ATM Based WANs
Reduce WAN bandwidth cost
  30% bandwidth savings
    Voice compression
    Silence and/or repetitive pattern suppression
    Dynamic bandwidth allocation
  50–70% reduction in management costs

## Slide 42: ATM Based WANs
Improve performance
  50% performance improvement
  Reduce downtime
    Use highly redundant systems
    Provide rapid reroute around failed trunks
  Goal 99.99% uptime
Typical costs
  One time installation cost
  Monthly facility access and network port cost
  Costs are speed dependant