## Slide 1: Chapter 2
Business Information
Wall
Street
Journal

## Slide 2: Measuring Data
Digital
  Bit - binary digit
  Numeric value of 0 or 1
Analog
  Hertz - cycles per second
Computer
  Byte = 8 bits
  Octet

## Slide 3: Prefix Notation
kilo = 103 or 210 -- Kb, Kbps, KB, KHz
  Kb - kilobit (1024)
  Kbps - kilobit per second (data rate, speed)
  KB - kilobyte
  KHz - kilohertz (1000)
mega = 106 or 220 - Mb, Mbps, MB, MHz
giga = 109 or 230 - Gb, Gbps, GB, GHz
tera = 1012 or 240 - Tb, Tbps, TB, THz

## Slide 4: Scientific Notation
Numberbase 10 x 10power
  Example: 5 x 10a * 7 x 10b = 35 x 10(a+b)
Logarithms: log1010a = a
Numberbase 2 x 2power
  Example: (0,1) x 2c

## Slide 5: Wordsize and Outcomes

## Slide 6: Analog Sound/Audio
Telephone - 3,000 Hz = 3KHz
Teleconference - 7,000 Hz = 7KHz
High fidelity - 15,000 Hz = 15KHz
  range of human ear
CD - 20,000 Hz = 20KHz

## Slide 7: Digital Voice
Analog sound is sampled
Voice - 8,000 samples per sec (smp/sec)
Amplitude - 8 bits = 256 levels
Data rate = 8000 smp/sec * 8 bits/smp = 64,000 bps or 64 Kbps

## Slide 8: Digital CD
44,100 samples per channel
2 channels
Amplitude = 16 bits = 65,536 levels
Data rate = 44,100 x 16 x 2 = 1,411,200 bps = 1,411 Kbps = 1.4 Mbps
CD capacity = 600 MB = 5 Gb
Playing time = 5 Gb/1.4 Mbps = 3,566 seconds ~ 1 hour

## Slide 9: Text & Numbers (data)
Text characters
  ASCII (7 or 8 bits) = 128 or 256 characters
  EBCDIC (8 bits) = 256 characters
  Unicode (16 bits) = 65,536 char
    Standard is ISO 10646
Numeric
  Integers - 16 or 32 bits (2 or 4 bytes)
  Floating point - 32 or 64 bits (4 or 8 bytes)

## Slide 10: Transaction Processing
Response time
  Time required for a system to react to a given input
Transaction time
  System response time
  User response time
Data processing costs
  Computer processing power
  Transmission capacity

## Slide 11: Images
Rectangular grid
  Rows times columns
  Number of cells = r x c
Pixel (pel) = picture element
Pixel wordsize = number of colors
Drawing approach
  Bit maps
  PostscriptTM

## Slide 12: Laser Image
Image size = 5in x 3in = 15 sq in
Printer resolution = 300 dots per inch (dpi)
  Dot density = 90,000 dots/sq in
Data volume = (dots/sq in) x (sq in) x (bits/dot) = bits
  Data volume = 90,000 x 15 x 1 = 1,350,000 = 1.35 Mb

## Slide 13: Medical Applications

## Slide 14: Data Rate Requirements