## Slide 1
Digital Transmission & Multiplexing

## Slide 2
End-to-End Connectivity

## Slide 3
Digital Transmission
Analog -- continuous values
Digital -- discrete values
Data communications usage
  Data
  Signaling
  Transmission

## Slide 4
Digital Transmission
Analog Signals
Frequency
Amplitude
Phase
Bandwidth

## Slide 5
Digital Transmission
Digital Signals
Frequency
Amplitude
Bandwidth

## Slide 6
Benefits of Digitization
Improved Signal Quality
  Regeneration vs. Amplification
  Error correction
  Better signal to noise ratio (SNR)
Easier to Multiplex
  TDM vs. FDM
Easier to Integrate Voice and Data
  Higher quality conferencing

## Slide 7
Benefits of Digitization
Uses Digital Circuitry
  Faster processing
  Less expensive
  More accurate signal representation
  Provides greater voltage tolerances
  Easier to test
Facilitates Security
  Encryption

## Slide 8
Digital Transmission
Modulation Types
Amplitude
Frequency
Phase
Pulse Code
Signaling Methods
Direct Current
Dual Tone
In-band
Out-of-band
Common Channel

## Slide 9
Digital Transmission
Pulse Code Modulation
  64000 bps
  8000 samples/second, digitized 8 bits
Adaptive Differential Pulse Code Modulation
  32000 bps
  8000 samples/second, digitized 4 bits

## Slide 10
Digitizing Errors
Time
Signal Amplitude

## Slide 11
North American PCM Standard
Output Y(X)
Input X
Formula:
Y(X) = ln(1-u*X)/ln(1-u)
u = 255
Mu Law (u)
- 8 KHz Sampling Rate
- 256 Quantization Levels
- 8 bits/Quantization Level
- 64 Kbps Digitization Rate

## Slide 12
Digital Transmission
Digital Carrier Systems (T-1)
  Circuit speed = 1.544 Mbps
  23 channels for data
  Each channel uses 7 bits for data + 1 bit for control
  8000 frames per second
  Data rate = 56000 bps
  24th channel used for frame synchronization
  DS-1 frame format

## Slide 13
Digital Transmission
Digital Subscriber (Local) Loops
Using twisted pair
  Simplest solution is 2 pair for full duplex operation
  Installed base is 1 pair
  Need full duplex capability

## Slide 14
ISDN 4-Wire Local Loop
ISDN NT1
ISDN
Central Office
Switch
Rx
Tx
Tx
Rx

## Slide 15
Digital Transmission
  Problems with full duplex operation on single pair
    Modems -- difficult to achieve 144 Kbps using current technology
    Direct transmission -- problems with echos through a hybrid

## Slide 16
Digital Transmission
Overcoming echo problems
  Time-Compression Multiplexing
    Actual transmitted bit rate ~ 350 Kbps
    Difficult to achieve on installed twisted pair
  Echo Cancellation
    Transmit at 192 Kbps (144 Kbps aggregate data rate
    Requires complex digital signal processing circuitry

## Slide 17
Digital Transmission
Using fiber optics
  Needed to support high data rates provided by broadband ISDN
  Subscriber interface, simple direct link
    Active star topology
    Use two-fiber or wavelength-division multiplexing (WDM)
    Allows gradual network evolution
    Subscriber unaware of distribution network details

## Slide 18
Digital Transmission
  Subscriber interface, multiple-access logic
    Passive star topology
    Signal split at remote nodes
    All subscribers receive same signal
    Use dense WDM or TDM
    Requires complex equipment at subscriber
  TDM currently less expensive that WDM
  DecreasingWDM cost will make technology competitive

## Slide 19
Multiplexing
Frequency Division Multiplexing
SynchronousTime Division Multiplexing
Statistical Time Division Multiplexing

## Slide 20
Multiplexing
SynchronousTime Division

## Slide 21
Multiplexing
Statistical Time Division

## Slide 22
Multiplexing
Statistical Time Division

## Slide 23
Multiplexing
Statistical Time Division

## Slide 24
Multiplexing
Digital Carrier Systems (DS-1)
  Time Division Multiplexing
  Pulse Code Modulation for Voice
  24 channels per frame
  8000 frames per second
  193 bits per frame
  Every 6th frame uses 7 bit PCM + 1 bit Signaling
  Circuit speed = 1.544 Mbps