## Slide 1: Frame Relay
Encompasses:
An Interface Specification
A Signaling Protocol
A Network Service

## Slide 2: What is Frame Relay?
A standards based next generation packet switching technology
  Reduces protocol functionality at user-network interface
  Supports higher bandwidth, throughput, reliability and lower delay
  Provides minimal error checking

## Slide 3: Frame Relay Interface
Frame Relay
Network
LEC Interface
V.35
DLCI = 12
V.35
DLCI = 14
Frame Relay Service
Frame Relay
Signaling Protocol
Frame Relay
Signaling Protocol
Frame Relay
Interface to
Frame Relay
Network
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Frame Relay Signaling
Benefits of frame relay as signaling protocol
  In band CPE management
  In-band link management
  Protocol
    Highly flexible
    Transparent to upper layer protocols
  Improved performance
  Flexible bandwidth allocation
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Frame Relay Network Access
Benefits of using frame relay for network access
  Equipment savings
  Local loop savings
  Maximize link efficiency
  “True” international standard
    ANSI
    ITU-T
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Frame Relay Network Service
Benefits of frame relay as network service
  Prevents technology discontinuity
  Lowers WAN costs
    Circuit savings
  Provides managed service
    Bridge for LAN-to-LAN connectivity
    Dynamic architecture
    Guaranteed availability
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Why Frame Relay?
X.25 Approach to Packet Switching
  Call setup carried on same virtual circuit as data
  Layer 3 provides logical channel multiplexing
  Layer 2 and 3 provide flow and error control
  Designed for low data rates (64 Kbps or less)
Frame Relay Approach to Packet Switching
  Call setup carried on separate logical connection from data
  Layer 2 provides multiplexing and switching
  Layer 2 does not provide flow and error control
  Streamlined version of X.25 for high data rates (> 2 Mbps)

## Slide 8: Frame Relay vs. X.25
Differences
  No flow or error control
  High bandwidth access circuit
    1.544 Mbps (T-1) is most common
    Fractional T-1 is available
    44.7 Mbps (T-3) is available
  Multiplex channel
    Data link connections
  Only uses PVC’s
Similarities
  Packet switched
  Logical connection
  Connection oriented
  Preservation of frame order
  Variable payload

## Slide 9: Frame Relay vs X.25
X.25 and Frame Relay Protocol Stacks

## Slide 10: The Bursty Data Problem
Multiple serial lines:
  Increased hardware costs
  Fixed bandwidth
  Possible bandwidth bottlenecks
  Delay issues
  Fairness issues
Notes: Frame relay can potentially solve the problems that today’s bursty data are encountering. Connecting LAN networks across the wide area provides an example. One typically adds routers to each LAN, and then connects the routers using dedicated leased lines or perhaps TDM channels.
Because bandwidth is expensive, and the bandwidth is dedicated solely to the router (other devices cannot use the bandwidth unneeded by the router); these lines are relatively low speed.
This design in bandwidth inefficient. Routers typically only use the bandwidth 10% of the time. The other 90%, the bandwidth is wasted.
This design is also a severe restriction on performance. The 10% of the time when the bandwidth is needed, it is not enough. The typical LAN operates at a speed of 10 or 16 Mbps; the low speed lines between the routers are a bottleneck.
When information is sent to a workstation across the WAN, it must often go across intermediate routers. These routers must perform switching. This adds to their processing load and typically adds at least 20 to 50 msec of delay to our data. Increased delay, for most applications, translates to reduced throughput.
To avoid intermediate routers, one could install lines to every remote routers. However, now one is buying more bandwidth that is wasted 90% of the time; one must buy many serial line cards for the routers; and one must buy a higher capacity router that can accommodate

## Slide 11: The Service Access Problem
ANSI and ITU-T interface specification
Bandwidth sharing
Hardware and line savings
Software upgrade
Low delay, fairness, and predictability possible
Frame Relay Interface supports multiple virtual circuits
Notes: Frame relay is an interface specification that StrataCom, DEC, Northern Telecom, and Cisco developed based upon earlier work done by the CCITT for ISDN. The work by the ‘Gang of Four’ has since been standardized by ANSI and the CCITT.
The interface specifies how a user device, such as the routers, deliver information to a WAN for transmission. The standards only specify the interface. Different architectures can provide the frame relay service, but each at a different Cost of Service and a different Quality of Service.
Frame relay offers the potential to share bandwidth needs among a large number of users. Bandwidth that is unneeded by one user can be reallocated to others that are bursting at this instant. If the frame relay service is offered by a PTT, those other users are most likely tens or hundreds of other frame relay customers. If the frame relay network is a private WAN, then the other users may be idle frame relay connections and, with some architectures

## Slide 12: Customer Benefits
Cost competitive national or global networking
  Single physical interface
  Multiple virtual circuits
  High transmission rate, throughput and reliability
  Usage triggered bandwidth
  Predictable response and delay
  Fairness
Supported on most routers and FEPs
Notes: Any standards compliant frame relay service can potentially offer the benefits of the frame relay interface. However, to receive the benefits on the right, a close look at the underlying platform is required.

## Slide 13: Frame Relay Costs
Access port costs
Hardware costs
  CSU/DSU costs
PVC costs
CIR costs

## Slide 14: Frame Relay Terminology
DLCI 21
DLCI 23
DLCI 22
DLCI 31
DLCI 32
DLCI 33
Frame Relay
Switch
SDLC
FRAD
Router
Router
Frame Relay Switch
Maps DLCIs to form a PVC
Controls each PVC’s CIR, Bc, Be
Congestion Notification: FECN, BECN
Provides Accounting and Monitoring
Network hops = network latency
Definitions
DLCI: Data Link Connection Identifier
CIR : Committed Information Rate
Bc : Committed burst in bits
Be : Excess Burst in bits
FECN: Forward Explicit Congestion Notify
BECN: Backward Explicit Congestion Notify
DE: Discard Eligible

## Slide 15: Controlling Standards
ANSI Standards
  T1.606: Architectural Framework and Service Description
  T1.617: Signaling Specification for Frame Relay Bearer Service
  T1.618: Core Aspects of Frame Protocol for Use with Frame Relay Bearer Service
ITU-T Recommendations follow ANSI Standards

## Slide 16: Controlling Standards
ITU-T Recommendations
  I.122: Framework for Frame Mode Bearer Services
  I.223: Frame Mode Bearer Service
  I.370: Congestion Management for ISDN Frame Relaying
  I.372: Frame Relay Bearer Service Network-to-Network Interface Requirements
  I.555: Frame Mode Bearer Service Interworkings
  Q.922: ISDN Data Link Layer Specification for Frame Mode Bearer Services
  Q.933: Signaling Specifications for Frame Mode Call Control

## Slide 17: Architecture
Layers and protocols
  Physical Layer -- I.430, I.431 or V.35
  Control plane -- connection establishment and termination
    Q.922 for Data Link, Q.931 for Call Establishment
  User plane -- data transfer between users
    Q.922 core functions for Data Link, User specified terminal functions

## Slide 18: Architecture
Services Provided
  Connection oriented link layer
  Preservation of frame order
  Non-duplication of frames
  Small probability of frame loss
  Errored frames are discarded
  Congestion notification
  Connection number routing

## Slide 19: Data Link Layer
Bit Synchronous Protocol Legacy
IBM SDLC
ANSI ADCCP
ISO HDLC
ITU-T LAP,
LAPB, LAPD,
LAPF, etc.
Vendor
Adaptations
Standards
Adaptations

## Slide 20: Data Link Layer
Bit synchronous frame format
Bit synchronous frame types
  Information
  Supervisory
  Un-numbered
FLAG
ADDR
CNTR
INFO
FCS
FLAG
FLAG 8 bits
ADDR 8*n bits (n = 1, 6)
CNTR 8*m bits (m =1, 2)
INFO 8*r bits (r = 1, R; R configurable)
FCS 8*x bits (x = 1, 4)
FLAG 8 bits

## Slide 21: Data Link Layer
LAPF frame format
LAPF frame types
  User Information: no control field
FLAG
ADDR
INFO
FCS
FLAG
FLAG 8 bits
ADDR 16 bits (default)
CNTR none
INFO 8*r bits (r = 1, R; R configurable)
FCS 16 bits
FLAG 8 bits

## Slide 22: Data Link Layer
LAPF address field format
FLAG
ADDR
INFO
FCS
FLAG
X
0
1
Upper DLCI
Lower DLCI
DLCI Data Link Connection Identifier
X Command/Response Bit
F Forward Explicit Congestion Notification
B Backward Explicit Congestion Notification
D Discard Eligible
D
B
F

## Slide 23: LAPF
Comparison to LAPD and LAPB
  Only 1 frame type
  No control frames (inband signaling)
    No flow control, error control or sequence numbers
I field carries user data
  Default length: 4096 byte
Data link connection identifier
  Maps logical destination to network
  Allows connection multiplexing

## Slide 24: Access Parameters
Committed burst size
  Maximum amount of data network will transfer under normal conditions
Throughput
  Average number of I field bits transferred per second
Minimum acceptable throughput
  Lowest value caller will accept for the call

## Slide 25: Frame Handler
End user is physically connected to a Frame Handler not another end user
Checks FCS field in Incoming Frame
  FCS Good: Route to outgoing interface
  FCS Bad: Discard frame
Routing based on Connection Table
  Use incoming DLCI to identify outgoing DLCI.

## Slide 26: Traffic Management
Joint responsibility of network and user
Network monitors for congestion
User controls congestion
  Limits traffic flow into network
Rule of Thumb: Line > 80% utilized queue becomes unstable

## Slide 27: Traffic Management
Network of network queues
Frame arrival rate (line utilization) increases
  Queue size increases
  Transport delay increases
Frame departure rate increases
  Queue size decreases
  Transport delay decreases

## Slide 28: Traffic Management
Saturation point reached
  Number of incoming frames > number of outgoing frames
  All buffers become filled
  Discard incoming frames
    Requires retransmission
    Self defeating - increases congestion
  Restrict incoming frames
    Flow control of neighboring nodes
    Limits user traffic - avoid throughput collapse

## Slide 29: Congestion Control Strategy
Congestion avoidance used at onset of congestion to minimize effect on network
Explicit signaling -- network mechanism to trigger congestion avoidance
  Frame handler must not reset bits in forwarded frame
Network response
User response

## Slide 30: Congestion Control Strategy
Congestion recovery used to prevent network collapse in face of severe congestion
Implicit signaling -- signal to higher layer indicating that frames are being dropped
  ANSI standard recommends using an adaptive flow control windowing based management scheme

## Slide 31: Control Mechanisms
Committed information rate (CIR)
Discard eligibility (DE) bit
Explicit congestion notification
  BECN bit
  FECN bit
  CLLM message

## Slide 32: FECN, BECN and DE Bits
FECN bit
  Indicates congestion occurred in “this” direction and user action is required
BECN bit
  Indicates congestion occurred in the “other” direction and user action is required
DE bit
  Indicates that “this” frame is eligible for discard

## Slide 33: CIR, Bc and Be
CIR
  Traffic rate in (bps) the network agrees to transport on a connection
Bc
  Maximum amount of traffic in (bits) the network agrees to transport in time T
Be
  Maximum amount of traffic in (bits) above Bc the network will attempt to transport in period T

## Slide 34: Committed Information Rate
Guaranteed Transmission
Transmit if Possible
Discard all Excess
CIR
Be
Traffic Rate (bps)