## Slide 1: H.323
ITU-T spec for transmitting audio, video and data across an IP network

## Slide 2: H.323 Standard
Used for point-to-point and multipoint conferences
  Addresses call signaling and control
  Multimedia transport and control
  Bandwidth control
Uses multiple features and protocols
  Call Signaling H.225
  Media Control H.245
  Audio Codecs G.711, G.722, G.723, G.728, G.729
  Video Codecs H.261, H.263
  Data Sharing T.120
  Media Transport RTP/RTCP

## Slide 3: Elements
Terminals
  User endpoint devices
    Audio, video and data conferencing
    Point-to-point
    Multipoint
Gateways
  Connection to PSTN or ISDN for interworking
Gatekeepers
  Provide admission control
  Address services
MCU – multipoint control units

## Slide 4: Elements of the Network
H.323
Terminal
H.323
Gatekeeper
H.323
Gateway
H.323
Terminal
H.323
MCU
H.323
Terminal
WAN
(RSVP)
PSTN
V.70
Terminal
H.324
Terminal
Speech
Terminal
H.320
Terminal
Speech
Terminal
ISDN
Scope of H.323
Environment

## Slide 5: Components of a Terminal
System Control Unit – provides H.225 and H.245 call control for proper terminal operation
Media Transmission – Formats media for transmission
Audio Codec – Encodes/decodes audio signal for transmission/reception
Video Codec – Encodes/decodes video signal for transmission/reception
Network Interface – Packet based capable of supporting end-to-end TCP or UDP unicast and multicast services
Data Channel – Provides support for database access, file transfer and audiographics conferencing

## Slide 6: Gateway Functionality
Provides
  Switched Circuit Network (SCN) interface
  H.323 Terminal interface
  Translates between the audio, video and data transmission formats
Not needed if SCN interconnect is not required

## Slide 7: Gatekeeper Functionality
Provides pre-call and call-level control services to H.323 endpoints (Terminals and MCUs)
When multiple gatekeepers are implemented inter-communications is provided in an unspecified manner
Must provide following functions
  Address translation
  Admissions control
  Bandwidth control
  Zone management
May provide
  Call control signaling
  Call authorization
  Bandwidth management
  Call management

## Slide 8: Multipoint Control Unit
Endpoint that supports multipoint conferences
Provides
  Multipoint Controller (MC) – transmits capability set to each endpoint in conference
  Multipoint Processor (MP) – receives audio, video and/or data streams and distributes to endpoints
    Each MP is associated with a different equipment stream

## Slide 9: Proxy Server
Operates at application layer
  Examines packets between two communicating applications
  Determines call destination
  Establishes connection
Key functions
  Negotiate adequate QoS to tunnel across IP network
  Manage QoS using RSVP and/or IP Precedence
  Use application specific routing (ASR) to support routing of H.323 traffic separately from ordinary traffic
  Compatible with NAT
  Provides security for H.323 traffic
    In conjunction with Firewall
    Independent of Firewall

## Slide 10: Protocol Suite
Supports
  Call admission
  Setup
  Status
  Teardown
  Media streams
  Messages
Uses
  Reliable delivery – TCP
  Unreliable delivery - UDP

## Slide 11: Protocol Suite (Continued)
Areas of control
  Registration, Admission and Status (RAS) Signaling - provides pre-call control in gatekeeper-based networks
    RAS channel opened before any other channel
    RAS channel is independent of other channels
    Uses UDP connection
    Gatekeeper discovery
      Manual – endpoints are configured with gatekeeper IP address
      Auto discovery – enables endpoint to discover a gatekeeper using IP address 224.0.1.41, UDP discovery port 1718, UDP registration and status port 1719
  Call Control Signaling - supports connection, call maintenance, and disconnection between endpoints
    Based on H.225 using Q.931 call control messages and Q.932 supplementary services

## Slide 12: Protocol Suite (Continued)
Areas of control (Continued)
  Media Control and Transport - provides reliable H.245 channel for media control messages.
    Media control uses dynamically assigned TCP port
    Media transport (RTP/RTCP) uses UDP data streams
      RTP uses even port numbers
      RTCP uses next highest odd port number