## Slide 1: Chapter 5
Internet Addressing
and
Services
THE Internet
Planet Internet

## Slide 2: What Is the Internet?
Network of networks
Machines
  Computers, routers, switches
Circuits
  Wire and fiber
Information and applications
People

## Slide 3: Why Users Want to Connect
Internet Users Say the Internet and Online Services will Change the Way They:
Source: Yahoo! Online Guide Service, SR International
Communicate 93%
Learn 91%
Work 86%
Entertain Themselves 82%
Spend Free Time 68%
Shop 57%
Meet People 43%

## Slide 4: U.S. Usage of the Internet
Source: U.S. Dept. of Commerce and Forrester Research, Inc.
Total in the Year 2000
(7,500 Companies)
Total in the Year 2000
(93,076 Companies)
Total in the Year 2000
(640,962 Companies)
80
60
40
20
0
100
1995
1996
1997
1998
1999
2000
Large Companies (Over 1,000 Employees)
Medium Companies (100–999 Employees)
Small Companies (20–99 Employees)
Percentage

## Slide 5: Business Value of the Internet
Inter-company communications
  Communication
  Information sharing
  Product upgrades
Commerce
  Transactions
  New advertising
New services
  Voice, fax, videoconference
Security Services
Directory Services
Global Internet
E-Mail News Web Servers
VPNs

## Slide 6: Structure of the Internet
Routers used to build the clouds
42,000 + routes in backbone
Europe
Milnet
Australia
Backbone 1
Backbone 2
Backbone 3
FIX-East
Regional
Network B
NAP
NAP
NAP
CIX
Backbone
4, 5, N
MAF(E/+)-East
FIX-West
Japan
Regional
Network A
* Source: Yankee Group, August 1995

## Slide 7: Internet Service Provider
Basic connections
Network design and maintenance
Address management
WEB development
Servers
Outsourcing
Questions
  24x7 support
  Redundant backbone
  Billing structure
  Cost/MB for web co-location
“POP”
Security Services
Directory Services
Global Internet
E-Mail News Web Servers
VPNs
Other
ISPs

## Slide 8: Internet Connection
Wan Circuit Installation
CSU/DSU or Modem
Router
WAN Circuit Charge
Electricity/Space
}
ISP Provides Some or All
ISP

## Slide 9: Connection Type
Dialup
  Analog modem
  ISDN
Dedicated
  Leased circuit
  Frame relay
  SMDS

## Slide 10: Analog Modem
Mobile Users
Internet
Telecommuters
Available almost everywhere
Cost effective for very small sites, single stations
Cost effective for zero to two hours/day
Tariff management reduces phone charges

## Slide 11: ISDN
Digital dialup, fast connect time
64 Kbps per B channel
Cost effective for small sites, single stations
Cost effective for zero to four hours/day
Use Dial-on-Demand traffic management to reduces connection charges
128 Kbps
64 Kbps
64 Kbps
2B
}
{
Basic Rate Interface (BRI)
16 Kbps
D
Internet

## Slide 12: Leased Line
24-hour, dedicated connection with predictable throughput
One connection per physical interface
Bandwidth: 56 Kbps— 45 Mbps (T3)
Cost effective at more than 4-6 hours daily usage
Flat monthly cost

## Slide 13: Frame Relay
One to many
56 Kbps to 1.54 Mbps (T1/E1)
Throughput varies based on traffic of entire Frame Relay
Cost effective in hub/spoke configuration

## Slide 14: WAN Costs
Dedicated or on demand?
How much bandwidth?
How much help do I need?
Price
Availability
Cost per Month
Hours/Day
Leased Line, T1
Modem/ISDN
Frame Relay
SMDS
155 Mbps ATM
0
2
4

## Slide 15: Connection Size
Speed
Single- User
10-20 Users
21-50 Users
51+
Users
On Demand
Dedicated
Circuit
Analog Modem
ISDN
SMDS
28.8 K
128 K
128 Kpbs
9.6 kbps
1. 54 MB (T1)
45 MB (T3)
56 K
Leased Line
Leased Line
Leased Line
Frame Relay
256 K
ATM
155 MB
*
* Leased Line at 9.6 only Useful for Store and Forward

## Slide 16: The Internet Protocol
TCP/IP only native protocol
IP addressing required
Registered IP addresses to connect
The Internet
Mail Server
FTP Server
Gopher WWW Server
Telnet Server

## Slide 17: Internet Addressing
Internet Addresses
  Network Number, Host Number
  Dotted decimal format (nnn.nnn.nnn.nnn)
  32 bit address length
    Class Range ID Network Host
    A 1 - 127 0 7 bits 24 bits
    B 128 - 191 10 14 bits 16 bits
    C 192 - 223 110 21 bits 8 bits
    D 224 - 239 1110 Multicast
    E 240 - 254 1111 Experimental

## Slide 18: Internet Address Format
Network
Host
32 bits
8 Bits
8 Bits
8 Bits
8 Bits
131
108
122
204
.
.
.
Uses: Dotted decimal notation

## Slide 19: Internet Address Format
N
H
H
H
Class A:
N
N
H
H
Class B:
N
N
N
H
Class C:
N - Network Number, NIC assigned
H - Host Number, Network administrator assigned

## Slide 20: Subnet Address Masking Format
131
108
0
0
Class B
IP Address
255
255
0
0
Class B
Default Mask
255
255
255
0
Class B with
8-Bit Subnet
Mask
Use host bits starting with high
order bit position

## Slide 21: Address Masking Rules
Network administrator decides size of subnet
Subnet masks identify which host bits are used to specify the subnetwork
Subnet mask bit layout
  Binary 1 identifies network bit
  Binary 1 identifies subnet bit
  Binary 0 identifies host bit

## Slide 22: IP Addressing Exercise
ADDRESS
CLASS
NETWORK
HOST
10.2.1.1
128.63.2.100
201.222.5.64
192.6.141.2
130.113.64.16
256.241.201.5

## Slide 23: IP Subnet Addressing Exercise
ADDRESS
CLASS
SUBNET MASK
SUBNET
BITS
131.108.2.10
15.6.24.20
168.124.36.12
128.16.32.13
255.255.255.0
255.255.0.0
255.255.255.0
153.50.6.27
201.222.10.60
255.255.255.252
255.255.255.128
255.255.255.248
B
A
B
B
B
C

## Slide 24: Internet Addressing
Domain Name System
  Top Level Domains
    edu, com, mil, org, net, us, au, de, etc.
  Domain Name Service
    Distributed data base
      Domain name ==> IP address (address resolution)
      IP address ==> domain name (reverse address resolution)
Internet Routing
  Hop by hop

## Slide 25: Internet Addressing
Locating Resources
  protocol://host:port/path/filename
    Uniform Resource Identifier (URI)
    Uniform Resource Number (URN)
    Uniform Resource Locator (URL)

## Slide 26: THE Internet
Orgin of the Internet
  ARPAnet
  NSFnet
Technical Governance
  Internet Society (ISOC)
  Internet Architecture Board (IAB)
    Internet Engineering Task Force (IETF)
    Internet Engineering Steering Group (IESG)
    Internet Assigned Numbers Authority (IANA)

## Slide 27: Internet Services
Network Information Center
  Registration services
  Directory and database services
  Information services
Default Protocol Ports
  protocol,port
    FTP, 21; HTTP, 80; NNTP, 119
    TELNET, 23; NEWS, 144

## Slide 28: Internet Policy Decisions
Establish reasons for connecting
Decide on security policy
Determine parameters and limits

## Slide 29: Security Policy
Determine what data outsiders need
Determine the security requirements
Quantify the security system costs
Evaluate trade offs
  Ease of use
  Configuration
  Security demands
Implement a simple robust design

## Slide 30: Access Policy
Who is allowed to connect in or out?
How do they authenticate themselves?
What are they allowed to connect to?
What protocols are permitted?
How much resources can they use?

## Slide 31: Service Policy
What services are needed?
  Web browsing
  File transfer
  E-mail
  News
  Multimedia
  Others…
What services will be provided?
  Web servers
  Name server
  E-mail server
  FTP server
  Gopher
  Others…