## Slide 1: Chapter 15
LAN Systems

## Slide 2: LAN Backend Networks
“Computer room networks”
Interconnect large systems
  Mainframes
  Supercomputers
Key requirement is high-speed bulk transfer
Usually limited distance, few nodes
Speed more important than cost

## Slide 3: LAN High-Speed Office Networks
Increased processing and transfer requirements in many applications now require significantly higher transfer rates
Typical office LAN runs at 1-20 Mbps, insufficient for graphics-intensive applications
Decreased cost of storage space leads to program and file bloat, increased need for transfer capacity

## Slide 4: LAN Backbone Local Networks
Used instead of single-LAN strategy
Better reliability
Higher capacity
Lower overall cost

## Slide 5: Applications Drive New Technology Usage
Token
Ring
CSMA/CD
Frame Relay
ATM
LAN
Campus
MAN
WAN
Private Line
1000
100
10
FDDI/100BaseT/100BaseVG
Bandwidth (Mbps)
GEN
1

## Slide 6: Applications Demand Bandwidth and Performance
Response Time (secs)
107
106
105
104
103
102
101
100
10-1
10-2
10-3
10-4
RPC
DFS
Voice
Audio
Fax
Msg.
Imaging
100 Gbps
10 Gbps
1 Gbps
100 Mbps
10 Mbps
1 Mbps
MPEG
Px64
Raw
Video
B&W
JPEG
Raw
G3
ADCMP
Raw
ADCMP
Color
OLTP
Paging
Data Volume (Bytes)

## Slide 7: Application Demands
Shared LANs
ATM
  Network Delay-Tolerant Application
Network Delay-Sensitive Application
Network Delay-Intolerant Application
      Switched LANs
Traditional computing
Facsimile
E-mail
Compound document transfer
Videoconferencing
  Local
  Campus
  Wide area
Document imaging
Real-time multimedia playback off network Training videos Audio/video from laser discs, etc.

## Slide 8: 100BaseT Architecture

## Slide 9: Fast Ethernet
Integrates with existing systems
Standard
  IEEE 802.3u
Media types
  100BaseTX: UTP5
  100BaseFX: Fiber optics
Uses star topology
  Broadcast mode - multi-port hub
  Full-duplex mode - switching hub

## Slide 10: Switched Fast Ethernet
Switch
Unshielded twisted pair
Fiber optic cable
Full duplex messaging
100 Mbps link speed
Distributed folded bus topology
Dedicated bandwidth environment
Notes: CSMA/CD media access protocol
10/100 Mbps twisted pair or fiber media
1518 byte maximum link level frame
Full duplex message traffic is possible if the link from the switch to the user is point-to-point

## Slide 11: Value of Fast Ethernet
Same format, MAC as 10Mbps Ethernet
Mature technology = low prices
Can be mixed to provide more aggregate bandwidth but no change on the desktop
Can go up to 200Mbps to servers, graphics workstations, etc.

## Slide 12: Gigabit Ethernet
Standards
  IEEE 802.3ab (twisted pair)
  IEEE 802.3z (fiber)
Designed for upgrade
  CSMA/CD media access
  Ethernet frame format
Provides backbone connectivity
Offers migration strategy

## Slide 13: Gigabit Ethernet
Optical fiber cable
  1000BaseSX (MMF - 500 m)
  1000BaseLX/LH (SMF - 3 Km)
  1000BaseZX (Extended reach SMF)
Twisted pair cable
  Category 5
  Category 5E
  Category 6 (Standard expected in 2001)

## Slide 14: 100VG-AnyLAN
VG = Voice Grade
Medium
  4 pair UTP category 3, 4, and 5
  In the future
    2 pair UTP category 5
    STP
    Fiber optic
MAC - 2 level demand priority
Performance
  Heavy load - token ring
  Light load - CSMA/CD

## Slide 15: Fiber Distributed Data Interface
Multimode/single mode optical fiber
Half duplex messaging
100 Mbps link speed
Dual counter rotating rings
Single/dual station attachment
Shared bandwidth environment
Notes: Dual counter rotating rings with dual attached stations allows for loopback if a node fails
Maximum frame size is 4500 bytes
Token passing media access protocol
Deterministic performance

## Slide 16: Fibre Channel
High speed scalable data transport technology
  Mass storage devices
  Data networking
    Mainframes
    Supercomputers
    Servers
    Workstations
Very fast transfer of large data volumes

## Slide 17: Fibre Channel
Supports data intensive applications
  Medical imaging
  Image based document management systems
  Data warehousing
  Real-time video
  Multimedia and voice processing
  Internet and intranet servers
  CAD/CAM and scientific visualization

## Slide 18: Fibre Channel
Why users want fibre channel
  Connectivity
    Arbitrated loops can support 126 devices
    Switching fabrics can supports 16 million point-to-point connections
    Not a shared resource LAN technology
  Distance
    Copper for up to 25 meters
    Multimode fiber up to 500 meters
    Single mode fiber up to 10 kilometers

## Slide 19: Fibre Channel
Why users want fibre channel
  Performance
    Technology provides from 100 to 800 Mbps of bandwidth capability
    Generally operates at 200 Mbps bandwidth
      Full duplex traffic

## Slide 20: Fibre Channel
User benefits of fibre channel
  Scalability
    Grows with the company
  Reliability
    Continuous availability
  Performance
    Improves application

## Slide 21: ATM LANs
Support multiple classes of service
Support isochronous traffic
Link LAN to WAN without technology change
Scale to higher speeds
Permit desired level of performance to be assigned as needed
Performs like a multi-protocol switch

## Slide 22: ATM Forum LAN Emulation
A MAC (Media Access Control) layer specification, known as LANE 1.0, that allows the ATM fabric to emulate a logical Ethernet or Token Ring segment.
Definitions:
  LAN Emulation User Network Interface - Referred to as “LANE 1.0”. It defines the interface between a legacy LAN attached device and the ATM network.
  LAN Emulation Services - They serve the following functions: initialization , address registration / resolution, and data forwarding. They consist of the LECS, LES, and BUS.

## Slide 23: ATM Forum LAN Emulation
Definitions (continued):
  LAN Emulation Configuration Server (LECS) - Maintains the configuration information for each emulated LAN.
  LAN Emulation Server (LES) - Performs the MAC-to-ATM address resolution functions in an emulated LAN.
  Broadcast Unknown Server (BUS) - Performs the multicast server function and broadcasts packets to multiple LECs.
  LAN Emulation Client (LEC) - Multiple LECs connect to the LANE services. Client functionalities are typically implemented on adapters, routers, and ATM-to-LAN edge devices.

## Slide 24: LAN Emulation
AAL 5 segments data frames into cells
ATM LAN Edge Device implements Proxy LANE Client and MAC Layer LANE
Proxy client forwards unregistered MAC addresses
Legacy LAN Host requires no changes
LANE emulates a bridged LAN segment

## Slide 25: LAN Emulation Protocol Stack
Application
NDIS/ODI Driver
LAN Emulation
AAL5
ATM
Physical
ATM
Physical
Physical
LAN
Emulation
AAL5
ATM
Physical
Application
MAC
Physical
NDIS/ODI
Driver
Physical
MAC
Bridging
Software
ATM Host
LAN Host
ATM LEC
“Edge Device”
ATM Switch

## Slide 26: LANE Network Configuration
UNI 3.0/3.1 Signaling
IISP routing
Static ATM addressing
LANE 1.0 provides LAN connectivity
Switch
IISP
LANE Clients
UNI
Switch
Switch
Switch
Bridge
Bridge
IISP
Bridge
TR Network
Ethernet Network
Ethernet Network
LANE Servers
(LES, BUS)
LANE Clients
(Edge Devices)
Notes: SONET - Layer 1
LANE - Layer 2
* UNI 3.0/3.1 signaling
* IISP (Interim Interswitch Signaling Protocol) uses static table for routing

## Slide 27: RFC 1483
Defines multiprotocol encapsulation for network traffic over ATM AAL 5
  Routed Encapsulation
    Non-VC Multiplexing - protocol families share a VC
    LLC/SNAP Header identifies protocol type
    Used in RFC 1577
  Bridged Encapsulation
    Non-VC Multiplexing used for “Bridging over ATM”
      Used by pre-LANE products
    VC-Multiplexing - Protocol families on separate VCs
      Used by LANE products

## Slide 28: RFC 1577
Classical IP and ARP over ATM
  Defines the ATM address resolution protocol
  Maps IP addresses to ATM addresses within a logical IP subnet.
  A group of IP Hosts on the same subnet are connected to a single ATM Network called a logical IP subnet
  ATM Address Resolution Server
  No Broadcasts
  No Routing

## Slide 29: RFC 1577 vs. LANE 1.0
<footer>
<date/time>
LAN
Emulation
RFC 1577
Route or Bridge
Route
Multiprotocol
IP Only
Data over ATM
Mechanism
Internetworking
Protocol Support
Connection Support
Point-to-Point
Point-to-Multipoint
Point-to-Point
Notes: There are several advantages to LAN Emulation over RFC 1577. However, we will be supporting both for interoperability with all vendors. RFC 1577 was available in early ‘94, and LAN Emulation was not really defined until July ‘94. This may be the reason why many vendors are supporting RFC 1577.
LAN Emulation supports point-to-multipoint which is similar to broadcast. At this time, RFC 1577 does not support point-to-multipoint.
RFC 1577 only supports IP. LAN Emulation supports multiple protocols.
Finally, LAN Emulation supports routing and bridging. RFC 1577 only supports routing.

## Slide 30: Wireless LANs
Infrared transmission
  Data rate < 2Mbps
  Aggregated per channel
Radio transmission
  2.4 Gbps spread spectrum
  Data rate 11 Mbps
IEEE 802.11b compliant
Provides flexible equipment layout