## Slide 1: Chapter 14
Local Area Network
Technology

## Slide 2: LAN versus WAN
Ownership
  WAN
    Either public or private
  LAN
    Usually private
Capacity
  LAN
    Higher capacity
    Carry internal communications load

## Slide 3: Commercially Available LANs
Ethernet
IBM Token Ring
Appletalk
Arcnet
Starlan
MAP and TOP

## Slide 4: Network Operating Systems
Novell -- Netware
Microsoft -- Windows NT Advanced Server, Windows 2000
IBM -- OS/2 LAN Server
Banyan -- VINES
Sun Systems -- Network File System
AT&T -- Netware for Unix

## Slide 5: Why are LANs Popular?
Provide sharable hardware, software, and services
Provide low cost network attachment
Allow local management and control
Usually organized into workgroup
Support client/server computing
Support sharable communications, file, and print servers

## Slide 6: PC LAN Networks
Client/Server Communication
  Shared access: databases and internet
  Shared resources: hardware and software
Peer-to-Peer Communication
  Sharing work load and information within a workgroup
Cost sensitive network attachment

## Slide 7: Baseband Network Configuration

## Slide 8: Tiered LANs
Multiple tiers is an alternative to connecting all devices to a single LAN
Bottom-up strategy
  Departments create independent LANs
  Use backbone to interconnect departments
Top-down strategy
  Management develops an organization-wide networking plan
Cost of attachment increases with data rate

## Slide 9: Tiered LAN Architecture

## Slide 10: LAN Performance
Protocol
Speed of transmission
Amount of traffic
Error rates
Efficiency of software
Speed of server computers and disks

## Slide 11: ISO & IEEE 802 Standards
Describe
  Network topology
  Transmission media
  Signal encoding and decoding
  Bit transmission and reception
  Frame assembly and disassembly
  Transmission media access
  Flow and error control policies

## Slide 12: LAN Technology
Network topology
  Bus, tree, ring, or star
Transmission media
  Twisted pair, coaxial cable, or fiber optic
Cable layout
  Linear or star
Media Access Control (MAC)
  Round robin (Token passing)
  Reservation (TDM)
  Contention (CSMA/CD)

## Slide 13: Corporate Wiring Usage
Source: Telecommunications Magazine, January 1996

## Slide 14: Comparison OSI & IEEE 802

## Slide 15: LANs and the OSI Reference Model
Layer 1 -- Physical configurations
  Media
    Twisted pair
    Coaxial cable
    Fiber optics
    Wireless
  Transmission Techniques
    Baseband
    Broadband

## Slide 16: Bus LAN Topology
Uses a multi-point medium
Stations use a tap to attach to bus (linear media)
Full duplex between station and tap
Transmission from any stations travels entire length of bus (both directions)
Termination required at all bus endpoints

## Slide 17: Bus LAN Diagram

## Slide 18: Tree LAN Topology
Generalization of bus topology
Branching cable with no closed loops
Cable(s) begin at headend, travel to branches which may have branches of their own
Each transmission propagates through network, can be received by any station

## Slide 19: Tree LAN Diagram

## Slide 20: Ring LAN Topology
Repeaters are connected by unidirectional point-to-point links to form a ring
Frames circulate through repeater which
  Checks frame address
  Copies into local buffer if match occurs
  Retransmits all frames
Source repeater removes frame from ring

## Slide 21: Ring LAN Diagram

## Slide 22: Star LAN Topology
Each station directly connected to central node
  Usually with two undirectional links
Central node
  Broadcasts information
  Switches frames between stations

## Slide 23: Star LAN Diagram

## Slide 24: Choosing a Topology
Factors to consider
  Reliability, flexibility, expandability, and performance
Bus or tree is most flexible
Tree easiest to lay out
Ring offers high throughput
  Has reliability problems
Star offers high speed for short distances
  Has limited expandability

## Slide 25: Topology Problems
How do you identify transmission destination?
  Data transmitted in frames
  Each frame has address in header
How do you regulate access?
  Stations take turns sending frames
  Stations monitor control information in frames
How to choose the best media?

## Slide 26: Medium versus Topology

## Slide 27: Selecting a Media
Capacity
  Can media support expected network traffic?
Reliability
  Can media meet availability requirements?
Types of data supported
  Is media well-suited to the applications involved?
Environmental scope
  Can media function in the required environment?

## Slide 28: Transmission Media Options
Twisted pair--digital signaling
Optical fiber--analog signaling
Baseband coax--digital signaling
Broadband coax--analog signaling
  Uses FDM to carry multiple channels
  Supports longer distances
  Unidirectional
    Amplifier limitations

## Slide 29: Structured Cabling System
Cabling scheme for wiring within a building
Includes cabling for all applications
  LANs, voice, video, etc
Vendor and equipment independent
Designed to encompass entire building
  Enhances equipment relocated
Provides guidance for pre-installation
  New and renovated buildings

## Slide 30: Wiring Layouts
Wiring layout is different from topology
Linear layout minimizes amount of cable
Star layout uses individual cable from concentration point to subscribers
  May be used for bus or ring
  Concentration point
    Wiring closet
    Active hub
      Accepts frames and regenerates transmitted signals

## Slide 31: Baseband and Broadband Transmission

## Slide 32: LANs and the OSI Reference Model
Layer 2 -- Data link protocols
  Media access
  Logical link control

## Slide 33: IEEE and ANSI LAN Standards
IEEE 802.2 -- LLC Protocol
IEEE 802.3 -- CSMA/CD Networks
IEEE 802.4 -- Token Bus Networks
IEEE 802.5 -- Token Ring Networks
ANSI X3T9.5 -- FDDI Networks

## Slide 34: Media Access Control
Means to control shared media access
Techniques used
  Contention Mode
    Carrier Sense Multiple Access/Collision Detection
  Token Bus
    Round robin token passing
  Token Ring
    Token passing

## Slide 35: CSMA/CD Operation

## Slide 36: Token Ring Operation

## Slide 37: Practical Considerations
Data rate
Usage
Distance
Number of stations
Existing wiring
Layout and installation
Cost

## Slide 38: Logical Link Control
Specifies method of addressing and controls exchange of data
Independent of topology, media, and media access control
Unacknowledged connectionless service
  Higher layers handle error and flow control
Connection-mode service
  Connection setup before data transfer
Acknowledged connectionless service
  No connection setup

## Slide 39: Internetworking
Intranet
  Connecting subnetwork to subnetwork
Internet
  Connecting network of network
Subnetworks
Internetworking devices
  Bridges, Routers, Switches, and Gateways

## Slide 40: Internetworking Devices
Internetworking devices provide connections between network segments. Several different types of internetworking devices are shown below. Each device provides unique services when used to connect network segments.
Repeaters
Bridges
Routers
Gateways
Switches
AT&T


## Slide 41: Repeater or Hub
Connects segments to extend LAN length
Transmits all received bits with no buffering
Provides signal regeneration
Provides no address isolation
Often called a hub or concentrator
Operates at Physical Layer
Extends a LAN without segment isolation

## Slide 42: Using a Repeater
REPEATER
All devices:
“see” all traffic
share the same bandwidth
1 broadcast domain
1 collision domain

## Slide 43: Using a Hub
All devices:
“see” all traffic
share the same bandwidth
1 broadcast domain
1 collision domain
HUB

## Slide 44: Bridge
Connects network segments that use the same LAN data link protocols
Provides address filtering
Learns device locations
Broadcasts unknown messages to all ports. May cause broadcast storms
Uses physical MAC addresses
Provides transparent or translational connections
Operates at Data Link Layer
Extends a LAN with segment isolation

## Slide 45: Bridge Operation

## Slide 46: Types of Bridging
Transparent
Translated
AT&T

AT&T

Encapsulated
Source Routed

## Slide 47: Router
Connects media independent networks
Provides traffic isolation
Establishes best path between source and destination networks
Provides switching function
Uses network addresses
Provides unreliable delivery
Supports multiple protocols
Operates at Network Layer
Divides a large network into manageable segments

## Slide 48: Using a Router
Devices on individual sub-networks
see all traffic on sub-network
share sub-network bandwidth
3 broadcast domains
3 collision domains
No broadcast propagation
Learn network topology
support multiple interfaces
Use network addresses

## Slide 49: LAN Switch
Permits mixed 10/100 Mbps speed migration
Provides full bandwidth availability per user
Provides address filtering
Discards messages with unknown addresses
Migrate from shared to switched backbone
Operates at Data Link & Network layers
Converts a shared network into a switched network
for optimized client/server performance

## Slide 50: Using Switches with Routers
Switched devices
dedicated bandwidth
see no collisions

## Slide 51: ATM Switch
Supports LAN emulation
Provides virtual channel/virtual path connections
Supports isochronous connections
Supports QoS parameters
Supports multiple traffic types
Uses NSAP addresses
Uses cell switching
Operates at Data Link & Network layers
Provides time critical message delivery in a shared
or switched network environment

## Slide 52: Gateway
Permits protocol stack conversion
  SNA to TCP/IP
  SNA to DECNet
Permits migration strategies to be implemented
Permits enterprise integration
  Address translation
  HTML redirection
  Data encryption
  Firewall
Supports increased performance
Operates at All 7 OSI layers
AT&T


## Slide 53: Switched Internetwork Solutions
Which ONE should I choose?

## Slide 54: Possible Network Problems
LAN Segment Congestion
Protocol Congestion
Backbone Congestion
Too many devices on LAN segment
Backbone capacity is not enough
Too many broadcasts
Different Types of Congestion

## Slide 55: Single Technologies Provide a Partial Solution
Routing solution
  Solves the broadcast and protocol problems
  A router for every port is too expensive
LAN switching solution
  Solves collision/media problems
  Does not scale well
ATM LANE switching solution
  Solves the capacity/transport problem
  “ATM everywhere” is not cost-effective
Routing
ATM Switching
LAN Switching

## Slide 56: Multiple Technologies Provide a Complete Solution
Routing
LAN Switching
ATM Switching
“Instead of choosing between switching
and routing, users must learn how to
effectively combine ... these technologies
in the same network to derive the maximum
benefits in throughput and performance.”
M. LeBaron, Gartner Group, 2/95

## Slide 57: IEEE 802.3 Standard
Nomenclature
  Data rate in Mbps
  Signaling method
  Maximum segment length in 100s of meters
Media specification
  10Base5, 10Base2, 10Broad36, 10BaseT, 10BaseF

## Slide 58: IEEE 802.3 and Ethernet
Coaxial cable
Unshielded twisted pair
10 Mbps link speed
Half duplex messaging
Distributed multipoint bus topology
Shared bandwidth environment
Notes: CSMA/CD media access protocol
10 Mbps coax or twisted pair media
1518 byte maximum link level frame
Half duplex message traffic due to the shared media environment
Probablistic delivery of message to receiving node

## Slide 59: Switched Ethernet
Switch
Unshielded twisted pair
Fiber optic cable
Full duplex messaging
10 Mbps link speed
Distributed folded bus topology
Dedicated bandwidth environment
Notes: CSMA/CD media access protocol
10/100 Mbps twisted pair or fiber media
1518 byte maximum link level frame
Full duplex message traffic is possible if the link from the switch to the user is point-to-point

## Slide 60: IEEE 802.5 and IBM Token Ring
Shielded or unshielded twisted pair
Coaxial cable
Half duplex messaging
4/16 Mbps link speed
Ring is folded star topology
Shared bandwidth environment
Notes: Token passing media access protocol
Unidirectional traffic flow
Maximum frame size is unlimited, but practically is limited to 16 Kbytes
Typically the frame size is 4 Kbytes
Token passing offers a deterministic performance because the time that a message should arrive at the next station can be calculated.

## Slide 61: Switched Token Ring
Shielded or unshielded twisted pair
Half duplex messaging
Capable full duplex messaging
4/16 Mbps link speed
Ring is folded star topology
Dedicated bandwidth environment
Switch
Notes: Token passing media access protocol
Unidirectional traffic flow
Maximum frame size is unlimited, but practically is limited to 16 Kbytes
Typically the frame size is 4 Kbytes
Token passing offers a deterministic performance because the time that a message should arrive at the next station can be calculated.