## Slide 1: Chapter 20
Network Security
Malicious Attacks on
Business
Information
AT&T


## Slide 2: Information Integrity
Computer security
  A collection of tools designed to thwart computer hackers
Network integrity
  Measures that insure computer systems are functioning and performing as intended

## Slide 3: Security Is Not Just A Technology Problem
Many security technologies exist
The challenge - enable the customer to implement a single policy
The approach - enable dynamic links
  Between customer policy
  User or host identity
  Network infrastructure
Notes: Security truly is an enterprise wide issue.
The reason why the security problem is a difficult one is most networks (especially Internet and IP) were designed and optimized for connectivity and scalabiltiy. Networks did not become mostly private until quite recently.
Security technology has evolved piecemeal over time. Each specific issues has developed a specific technology to handle that issue. No where has the integrated whole been worried about.
Cisco has so many security features that it is difficult to catalog all of them.
So, today’s issue is not the need for security, but the need to organize and integrate the disparate security technologies. Cisco’s vision is to integrate current technologies, introduce new technologies when needed and bind them together in a single policy.

## Slide 4: Today’s Security Market
Point Products
Firewalls
Campus Login
Dial-In
Host/ Application
Notes: Today’s security market is a scattered approach in that all four areas solve security issues without interconnecting or relating to each other
Firewalls—Cisco, Checkpoint, Raptor, SCC etc., Ascend
Dial-in—MANY AAA SERVERS,RADIUS, TACACS+, Ascend, Shiva, Cisco
Campus—VLANs or host-based security
Host/application—email login, NetWare login, Kerberos
Will will not fully integrate with host and application.
The main issues for separate solutions are;
  High cost of ownership
  Maintenance

## Slide 5: Aspects of Security
Policy
Firewalls
Access
Management
Host
Security
Encryption
l
l
l
l
Router access
control lists
Mobile user
access
Physical issues
User accounts
Application
Network
Link

## Slide 6: Policy Considerations
What level of security is needed?
What data do outsiders need to reach?
What will policy implementation cost?
Identify the trade offs
  Security requirements
  Ease-of-use and configuration
Implement a simple, robust design
Hire a dedicated security specialist

## Slide 7: One Enterprise, One Policy
Mobility
Firewalls
Campus
Policy Management
Open
Restrictive
Closed
Integrity
UNIVERSAL PASSPORT
Kjkjkjdgdk kjdkjfdkI kdfjkdj
IkejkejKkdkd
fdKKjkdjd
KjkdjfkdKjkd
Kjdkfjkdj Kjdk
USA
************************
************************
Kdkfldkaloee kjfkjajjakjkjkjkajkjfiejijgkd
kdjfkdkdkdkddfkdjfkdjkdkd
kfjdkkdjkfd
kfjdkfjdkjkdjkdjkaj
kjfdkjfkdjkfjkjajjajdjfla
kjdfkjeiieie
fkeieooei
Notes: Cisco’s new approach to looking at security is from the central policy perspective.
  People, not products
  Centralized policy
  Legacy integration
What is new and different about this initiative?
  “Policy-aware infrastructure”
  A vertical integration of installed and emerging security technologies, not a new “magic bullet” protocol
  Corporate policy linked to people through the infrastructure

## Slide 8: The Policy Issues
UNIVERSAL PASSPORT
Kjkjkjdgdk kjdkjfdkI kdfjkdj
IkejkejKkdkd
fdKKjkdjd
KjkdjfkdKjkd
Kjdkfjkdj Kjdk
USA
************************
************************
Kdkfldkaloee kjfkjajjakjkjkjkajkjfiejijgkd
kdjfkdkdkdkddfkdjfkdjkdkd
kfjdkkdjkfd
kfjdkfjdkjkdjkdjkaj
kjfdkjfkdjkfjkjajjajdjfla
kjdfkjeiieie
fkeieooei
What is my policy?
Where are my users?
What are their privileges?
Notes: The way to rationalize all the security technologies is to approach the issue in a new way.
The best way to rationalize Security technologies is to look to the real issues customers face every day. What they really care about is the ability to set a policy (that can be open and permissive or closed).
What customers want to be able to do is have the network infrastructure adhere to a central single policy. To do this we can leverage today’s technology offerings and integrate them with some new services.

## Slide 9: Policy Components
Identity
Integrity
Active Audit
Integrity
UNIVERSAL PASSPORT
Kjkjkjdgdk kjdkjfdkI kdfjkdj
IkejkejKkdkd
fdKKjkdjd
KjkdjfkdKjkd
Kjdkfjkdj Kjdk
USA
************************
************************
Kdkfldkaloee kjfkjajjakjkjkjkajkjfiejijgkd
kdjfkdkdkdkddfkdjfkdjkdkd
kfjdkkdjkfd
kfjdkfjdkjkdjkdjkaj
kjfdkjfkdjkfjkjajjajdjfla
kjdfkjeiieie
fkeieooei
UNIVERSAL PASSPORT
Kjkjkjdgdk kjdkjfdkI kdfjkdj
IkejkejKkdkd
fdKKjkdjd
KjkdjfkdKjkd
Kjdkfjkdj Kjdk
USA
************************
************************
Kdkfldkaloee kjfkjajjakjkjkjkajkjfiejijgkd
kdjfkdkdkdkddfkdjfkdjkdkd
kfjdkkdjkfd
kfjdkfjdkjkdjkdjkaj
kjfdkjfkdjkfjkjajjajdjfla
kjdfkjeiieie
fkeieooei
PASSPORT
Notes: Identity
  Is who you are and what you’re allowed to do.
  You may want just username password, token card, digital certificate up to encrypted data as degrees of trust.
  You identify yourself

## Slide 10: Enterprise Identity
Who are you?
Where are you?
What is permitted?
Provide same privileges from anywhere
UNIVERSAL PASSPORT
Kjkjkjdgdk kjdkjfdkI kdfjkdj
IkejkejKkdkd
fdKKjkdjd
KjkdjfkdKjkd
Kjdkfjkdj Kjdk
USA
************************
************************
Kdkfldkaloee kjfkjajjakjkjkjkajkjfiejijgkd
kdjfkdkdkdkddfkdjfkdjkdkd
kfjdkkdjkfd
kfjdkfjdkjkdjkdjkaj
kjfdkjfkdjkfjkjajjajdjfla
kjdfkjeiieie
fkeieooei
Notes: Identity
  Is who you are and what you’re allowed to do Worldwide—campus, dial in, firewall
You may want just username password, token card, digital certificate up to encrypted data—each can be configured for a policy setting that changes the degree of trust.
TACACS+/RADIUS is an example of dial identity
Identity authorizations can also include a time metric for future time based access capability
Enterprise policy sets same privilege level wherever you are
Any level of granularity
People focused, not device dependent

## Slide 11: Integrity
Physical security
Secure configurations
Secure routing updates
Secure data forwarding
Firewalls
Notes: Physical security: Includes secure ROMs and configurations that delete the OS of the box if attacked at the console. We will write internal standards for Cisco box physical security
Secure configurations :includes levels of access for logging on to a Cisco box, AAA authentication for Telnet access, and Kerberized Telnet to configure a box remotely.
Secure routing updates: MD5route authentication for routes
Secure data forwarding: Encrypted links for WAN (cylink), encrypted GRE tunnels,
IPsec later in 1997
Firewall: Cisco IOS packet filtering and NAT, PIX stateful gateway

## Slide 12: Active Audit
Active audit server
Verify policy
Assurance
Reporting
  Errors
  Misuse
  Anomalies
Reporting
Verification
Audit
UNIVERSAL PASSPORT
Integrity
UNIVERSAL PASSPORT
Kjkjkjdgdk kjdkjfdkI kdfjkdj
IkejkejKkdkd
fdKKjkdjd
KjkdjfkdKjkd
Kjdkfjkdj Kjdk
USA
************************
************************
Kdkfldkaloee kjfkjajjakjkjkjkajkjfiejijgkd
kdjfkdkdkdkddfkdjfkdjkdkd
kfjdkkdjkfd
kfjdkfjdkjkdjkdjkaj
kjfdkjfkdjkfjkjajjajdjfla
kjdfkjeiieie
fkeieooei
Notes: Cisco does not have a server to do active audit today. We will partner with someone for this functionality. NETSYS has some of the audit function today in that it can perform “what if” analysis on access lists. Active audit will do so for live network configurations.
Policy audit and verification
Intrusion and anomaly detection
Reporting—canned reporting will be included

## Slide 13: Open Policy
If access is not expressly denied it is permitted
Easiest policy to configure and use
Notes: In all security solutions, there is a wide range of ways to deploy the technology.
Cisco’s current technology allows network managers to implement almost unlimited degrees in the policy scale.
To help explain this concept, we provide 3 examples of policies and how they can be implemented today with Cisco security technology.
An open policy is what most networks were configured for. Networks that are more interested in sharing information than hiding information may want to deploy an “Open” policy. Examples could be universities This group protects against malicious attacks but is fairly trusting of ordinary users.
* PLEASE NOTE:
DO NOT GUARANTEE SECURITY. CISCO PROVIDES THE TOOLS, BUT AN IMPROPERLY DESIGNED POLICY OR MANY OTHER FACTORS CAN CAUSE SECURITY BREACHES. CISCO ONLY PROVIDES THE TOOLS. CISCO CANNOT GUARANTY 100% SECURITY.

## Slide 14: Restrictive Policy
If access is not expressly permitted it is denied
  More extensive use of firewalls
  May use firewalls between internal groups
  More difficult to configure and use
Notes: The second policy example is what many companies will configure.
The policy implies that users may or may not be trusted.
There is a trade-off between configurability and user ease of access AND the degree of security technologies implemented.
In the restricted example, the users will have a harder time getting the information because of the firewall and explicit deny statements.
Most networks will deploy a combination of easy, restricted, or closed based on the location of users and the general trust of internal users, and outsiders.

## Slide 15: Closed Policy
Stricter implementation of access is denied if it is not expressly permitted
  Uses multilevel security procedures
  Uses infrastructure and application security
  Most difficult to configure and use
Notes: Most companies that transfer funds (Banks, Brokerages, etc.) will likely adopt a more stringent policy.

## Slide 16: 3-Part Firewall
AT&T

Corporate
Network
Internet
Joe Hacker
Demilitarized zone or isolated LAN
IP network visible from Internet
192.31.7.0
131.108.0.0
I cannot
get to
131.108.58.32

## Slide 17: Firewall/Gateway Summary
Firewalls should be simple, well tested
Use access lists
  To block general inbound traffic
  To allow access to specific services
Use single-use passwords
All new outbound TCP sessions only
Use passive FTP for safer file transfer

## Slide 18: Network Security
Security threat
  An action that compromises organizational information security
Security service
  A communications service that counters security threats
Security mechanism
  A communications mechanism that prevents, detects, or recovers from a security threat

## Slide 19: Passive Threat
Source
Destination
Attacker
The monitoring or recording of data being transmitted
over a communications facility.

## Slide 20: Passive Threats
Releasing message contents
  Reading data content of transmitted messages
Performing traffic analysis
  Reading header content of transmitted messages to determine location of hosts
  Observing length and frequency of messages

## Slide 21: Active Threat
Source
Destination
Attacker
The unauthorized altering of data or control signals or
the generation of spurious data or control signals on a
communications system.

## Slide 22: Active Threats
Modifying the message stream
  Selectively modifying, deleting, delaying or duplicating messages
Denying the message service
  Destroying or delaying most messages
Masquerading
  Posing as a real host or switch and communicating with another host or switch to acquire data

## Slide 23: Where Can Security Attacks Occur?
Network
Anywhere in the network

## Slide 24: Encryption—Basic Model
Encryption conceals meaning by changing intelligible messages into unintelligible messages
Decryption restores meaning by changing unintelligible messages into intelligible messages by using a key
Decryption
Encryption
Clear text
Original Clear text
Cipher text
Message
&^$!@#l:{Q
Message
Notes: 10
4
4

## Slide 25: Benefits of Encryption
Provides
  Privacy
  Data integrity
  Non-repudiation
Bank
Customer
Deposit $1000
Deposit $100

## Slide 26: Benefits of Encryption
Enables mobile users
Protects the WAN
  Commerce over the Internet
  Share network with business partners

## Slide 27: Encryption Approaches
Network-Layer Encryption
Application-Layer Encryption
Link-Layer Encryption
Link-Layer Encryption
Application
Layers (5-7)
Transport/ Network
Layers (3-4)
Link/Physical
Layers (1-2)
Notes: Encryption can be performed at the application layer by specific applications at client workstations and serving hosts. This has the advantage of operating on a complete end-to-end basis, but not all applications support encryption and it is usually subject to being evoked by individual users, so it is not reliable from a network administrator’s perspective.
Encryption can also be performed at the network layer by general networking devices for specific protocols. This has the advantage of operating transparently between subnet boundaries and being reliably enforceable from a network administrator’s perspective.
Finally, encryption can be performed at the link layer by specific encryption devices for a given media or interface type. This has the advantage of being protocol independent, but has to be performed on a link-by link basis.
To understand the implications of these characterizations, let’s take a closer look.

## Slide 28: Application Encryption
Encrypts traffic to/from a specific application
Specific to application
All users must have same version of application and associated keys
Network and link independent

## Slide 29: Network Encryption
Encrypts traffic on a flow-by-flow basis—between specific user/application pairs or network subnets
Specific to protocol, but media/interface independent
Does not require intermediate network device support
Topology independent
HR
Server
E-mail
Server
A to HR Server—Encrypted
All Other Traffic—Clear
D
B
A
Notes: By contrast, network encryption encrypts traffic on a flow-by-flow basis between specific source/destination user-application pairs or subnets.
Network encryption encrypts only payload information, leaving network-layer headers in the clear. This makes it transparent to intermediary network-layer devices.
Because it operates at the network layer, network encryption is protocol specific, but media and interface independent
This also makes it topology independent.

## Slide 30: Link Encryption
Encrypts all link traffic
  Including network-layer headers
Specific to media/interface type, but protocol independent
Topology dependent
  Traffic is encrypted/decrypted on link-by link basis
  All alternative paths must be encrypted/decrypted
Notes: Link encryption encrypts all traffic on a given link, including network-layer headers and protocol type information.
This enables it to be protocol independent, but it must be media/interface specific in order to accommodate link-layer variations.
This also means that each link over which the traffic to be encrypted may pass needs to be independently encrypted and decrypted. This is particularly required if the traffic is to pass through intermediary network-layer devices, because link layer encryption makes network layer headers unintelligible.
So the utility of link-layer encryption is extremely dependent on network topology.

## Slide 31: Encryption Methods
Private key method
Public key method

## Slide 32: Private Key Method
Uses a single algorithm to encrypt and decrypt a message using a single private key
Requires a key management policy to protect the security of the private key
Vernan Cipher or DES most commonly used algorithms
Decryption
Encryption
Clear text
Original Clear text
Cipher text
Message
&^$!@#l:{Q
Message
Notes: 10
4
4

## Slide 33: Vernam Cipher
Considered the “perfect” cipher
Key
  Random string of bits
  Length of key = length of plain text
Encryption
  Bit-wise addition using Exclusive-OR operation
  Exclusive-Or (XOR):

## Slide 34: Data Encryption Standard
Most widely used method of encryption
Uses DES adopted by NBS in 1977
  Outcome of IBM ‘Lucifer’ project
  NBS is now National Institute of Standards and Technology, NIST
Encrypts 64 bit data blocks
Uses 56 bit key
Provides 256 = 7.2 x 1016 key combinations

## Slide 35: DES Method
Input
  64-bit data entity string
  64-bit key (56-bit key + 8 parity bits)
Function switch specifying
  Encryption or decryption
Output
  64-bit cipher string created by passing 64 bit input and 56 bit key through the algorithm 16 times.

## Slide 36: DES Method
Key string length is the weakness of DES
Triple DES improves encryption strength
  3 iterations through the algorithm with 3 keys. Effective key length is 168 bits.
Increasing key length increase number of possible outputs, BUT also increases the decryption time. Must have high speed processors to use Triple DES effectively.

## Slide 37: Public Key Method
Uses a single algorithm with a public key to encrypt and a private key to decrypt a message
Does not require a key management policy to protect the security of the private key
Decryption
Encryption
Clear text
Original Clear text
Cipher text
Message
&^$!@#l:{Q
Message
Public key
Private key
Notes: 10
4
4

## Slide 38: Digital Signature
Objectives of digital signature
  Protect against receiver/3rd party forgery
  Protect against sender repudiation
  Provide evidence so that a certificate authority can settle disputes

## Slide 39: Creating a Digital Signature
Reversing roles of public key and private key in public-key encryption method creates a digital signature
  Sender private key used to encrypt message and signature
  Receiver uses sender pubic key used to decrypt message and signature
Decryption
Encryption
Clear text
Original Clear text
Cipher text
Message
&^$!@#l:{Q
Message
Public key
Private key
Notes: 10
4
4

## Slide 40: Digital Certificate
Digital certificate is a signed message that attests to authenticity of the user’s public key
Digital certificate contains
    Serial number of the certificate
    Issuer algorithm information
    Valid from/to date
    User public key information
    Signature of issuing authority
Certificate
Authority
Bob
Bob’s Public Key
Pub
0000123
SHA, DH, 3837829 ...
1/1/97 to 12/31/98
Bob Smith, Acme Corporation
DH, 383710 …
Certificate Authority
SHA, DH, 2393702347 ...
Notes: 27
A digital certificate contains:
  Serial number of the certificate
  Issuer algorithm information (digest/hash, PK type, PK)
  User public key information (PK type, PK)
  Valid to/from date
  Signature of issuing authority

## Slide 41: Certificate Authority
Alice’s Public Number
CA’s Signature
Ca’s Public Number
Bob’s Public Number
CA’s Signature
Ca’s Public Number
Certificate Authority
Bob
Public Number
Certificate
Certificate
Public Number
Alice

## Slide 42: Key Management Issues
Private key must not be compromised
Authentication procedure needed to guarantee sender public key is authentic
Key usage protocol required
Public key certification
Compromised private keys

## Slide 43: Key Exchange Problem
How to provide a secure key
exchange with someone watching…
XB
XA
a , p
Bob
Alice

## Slide 44: Creating Secret Keys Using Public Key Technology
Each device has two keys:
  A private key, generated by each device, which is kept secret and never shared
  A public key, calculated from the private key by each device, which is non-secret
Use Diffie-Hellman procedure
DES
DES
Pri
Pub
Pub
Pri
WAN
Notes: 18

## Slide 45: Diffie-Hellman Key Exchange
By exchanging numbers in the clear, two entities can determine a new unique number known only to them
  Generate as often as needed
  Provides scalable and secure key generation
Result is a shared private key
Bob
Alice
XB
XA
YA = (aXA) mod p
YB= (aXB) mod p
a , p
Z = (YB ) XAmod p
Z = (YA )XB mod p

## Slide 46: Disaster Recovery
Risk assessment
Disaster management policy
Disaster management planning
Identification, assessment, and response
Restoration

## Slide 47: Risk Assessment
Risk assessment is analyzing the interaction of:
  The costs that result from catastrophic events
  The likelihood of a catastrophic event occurring
  The costs of disaster management activities
    To prevent the disaster from occurring
    To respond to the disaster
    To recover from the effects of the disaster

## Slide 48: Risk Assessment
Costs of catastrophic events:
  Direct damage to equipment
  Salaries paid to people who cannot work
  Loss of economic opportunity
    Lost sales
    Halted production
  Expense of legal liabilities

## Slide 49: Risk Assessment
Most difficult parts of risk assessment
  Identifying categories of catastrophic events
  Estimating the probabilities of occurrence
  Determining appropriate measures to use in dealing with potential disasters
  Estimating disaster costs

## Slide 50: Disaster Management
Policy document should identify
  Who is responsible for disaster management planning
  Who is responsible for declaring a disaster has occurred
  Who has operational responsibility if a disaster occurs
  Setting priorities and the general level of protection expected

## Slide 51: Disaster Management
Planning should be broken into three categories
  Planning for activities in advance of a disaster
  Planning for managing the disaster event as it occurs
  Planning for the restoration of normal operation after the disaster event is over

## Slide 52: Disaster Management
Planning, preparation, and prevention
  Power of redundancy
  Avoiding single points of failure
San Francisco
New York
Leased Lines
Dial-up Line

## Slide 53: Identification, Assessment and Response
Defined roles for disaster response
  Leaders know responsibilities
  Workers know who is in charge
Contact lists
  Identify people, their roles, how to contact
Physical security
  Protect personnel
  Protect organizational resources

## Slide 54: Restoration
Maintain a good inventory and configuration database
Maintain good vendor contacts
Provide off-site backup facilities
  Establish reciprocal agreements
  Identify alternate locations within the company
  Identify a commercial disaster recovery site
  Provide a “shell” site
  Maintain a “hot” site

## Slide 55: Final Comment
Plan carefully
Test extensively
Train continuously
Practice periodically