## Slide 1: Quality of Service

## Slide 2: Queuing Strategies
FIFO – First In First Out
  Uses single queue for all traffic
  Traffic sent when bandwidth available
WFQ – Weighted Fair Queuing
  Uses multiple queues
  Divides bandwidth equally among all traffic flows
    Low volume flows given preference
    High volume flows share remaining bandwidth
  When flow ends bandwidth is redistributed

## Slide 3: Queuing Strategies
WFQ (Continued)
  Reduces jitter and enables efficient sharing among all applications
  Weighting is affected by 6 mechanisms
    IP Precedence
      More bandwidth allocated as precedence value increases
    Frame Relay: FECN and BECN
    RSVP
    IP RTP Priority
    IP RTP Reserve

## Slide 4: Queuing Strategies
WFQ Caveats
  Administrator must ensure that weights are properly set
  Not intended for interfaces with clock rates > 2.048 Mbps
CQ - Custom Queuing
  Can have up to 16 queues + 1 queue for system messages
  Users specify % of bandwidth to each queue
  Each queue served sequentially in round robin fashion
  A % of traffic on queue is sent before moving to next queue
  Number of bytes sent depends on interface speed + configured traffic %
CQ Caveats
  Knowledge required of port and traffic types
  High administrative overhead
  Provides a highly granular approach to queuing

## Slide 5: Queuing Strategies
PQ – Priority Queuing
  Uses 4 traffic priorities
    High, normal, medium and low
  High priority queue is always serviced first
  Normal is next, etc
  Must understand traffic flows to avoid starving an application
  Works best when High priority traffic is low
PQ Caveats
  Improperly configured can starve applictions by servicing 1 queue and ignoring others

## Slide 6: Queuing Strategies
CB-WFQ – Class Based Weighted Fair Queuing
  WFQ + administrator defined class base
    Use access lists to define the classes
    Classes determine how packets are grouped on queues
    Can specify amount of bandwidth to allocate to each class
      Supports 64 classes with bandwidth control for each class
      Each class is associated with a separate queue
  Bandwidth allocation does not mean that traffic in a class will experience low delay

## Slide 7: Queuing Strategies
LLQ – Low Latency Queuing
  Uses PQ with CB-WFQ
  Provides absolute priority to voice traffic over all other traffic
  Uses access lists to queue voice traffic to a strict PQ
    Based on fact that voice traffic is well behaved
      Sends packets at regular intervals
  Proven to provide voice traffic with the necessary priority, jitter and latency

## Slide 8: Packet Classification
Used to achieve proper weighting for WFQ
IP Precedence
  Setting of the 3 bits in ToS field of IP header
    See Table 9-2, p 200
  Enables router to group traffic flows
  Acts as an inband QoS mechanism

## Slide 9: Packet Classification
IP Precedence Caveats
  No built-in mechanism to reject incorrect IP Precedence settings
  Administrator must manage settings to insure that applications do not change IP Precedence settings from the planned values
  Can use Policy Routing to reset IP Precedence bits
    Use Cisco IOS to create route-map which will reset the precedence bits to “routine”

## Slide 10: Policy Routing
Allows definition of traffic flow policies so that don’t have to rely completely on routing protocols to determine traffic forwarding
Allows setting of IP Precedence bits to create different classes of service
Policies are based on
  IP address
  Port Numbers
  Protocols
  Packet size
Route maps determine where packets are forwarded
Policy routing is applied to the receive interface not the send interface
Caveats
  Traffic created on the router is not sent through the policy route
  Special attention is required to avoid using the “process-switching” path in Cisco IOS based routers

## Slide 11: RSVP-Resource ReSerVation Protocol
Enables endpoints to signal to the network the QoS needed by a particular application
Administrators do not need to be concerned with IP port numbers because RSVP signals this information during setup
Is an out-of-band, end-to-end signaling protocol
  Requests amount of bandwidth needed and latency permitted with each node that supports the protocol
  Skips nodes that do not support protocol
  Node has option to approve or deny the reservation request based on “load” on interface where service is requested
Applications receive notification on whether their request was approved or denied

## Slide 12: RSVP (Continued)
Characteristics
  Is not a routing protocol
  Does not modify routing tables
  Enables routing protocols to choose the most optimal path
Caveats
  Has 3 drawbacks
    Scalability – not deployed in large networks, used only at edge of backbone network
    Admission control – works only on total size of IP packet, doesn’t consider compression techniques
    Setup time

## Slide 13: IP RTP Reserve
Mechanism for weighting traffic based on packet flow UDP port range
  Acts like “static” RSVP
  When used don’t need IP Precedence or RSVP
Classifies packets based on
  UPD port range
  Allows specification of bandwidth to be prioritized on port range
When “reserved” traffic is not present allows bandwidth to be used by other traffic flows
Caveats
  Not most scalable solution
  Supports only a range of 100 UDP ports
  Does not allow admission control – any packet flows within specified IP RTP Reserve range are weighted

## Slide 14: IP RTP Priority
When configured with WFQ a strict priority queue is created
Voice traffic identified by port numbers can be classified on strict priority queue
  Gives voice precedence over all other traffic
  Recommended for VoIP networks with links of < 768 Kbps

## Slide 15: Traffic Policing
Regulating the amount of traffic an application can send across an interface
CAR – Committed Access Rate
  Rate limiting tool
    Control maximum traffic rate on send/receive interface
    Provide granular control at Layer 3
      Enables IP network to have TDM qualities
  Drops traffic based on policing
  Identifies when traffic exceeds threshold
  Often used in service provider networks to ensure that the subscriber does not exceed bandwidth limits set by contract

## Slide 16: Traffic Policing
CAR (Continued)
  Means of rate limiting traffic
    Precedence
    MAC address
    IP address
    Other parameters
  Does not buffer traffic to smooth out traffic bursts
  Information required to setup CAR
    Packet direction
    Average bit rate – based on long term average
    Burst size – maximum increase before traffic is considered to exceed rate limit
    Excess burst size – traffic in excess of rate limit

## Slide 17: Traffic Policing
GTS – Generic Traffic Shaping (on interface basis)
FRTS – Frame Relay Traffic Shaping (on DLCI basis)
  Traffic shaping tools
  Will buffer excess traffic waiting for an opportunity to send
  Allows control of traffic out an interface to match remote interfaces
    Control usage of available bandwidth
    Establish traffic policies
    Regulate traffic to avoid congestion
  Prevents packet loss
  Manages latency
    Gives priority to real time traffic
    Smooth out traffic patterns

## Slide 18: Traffic Shaping and Queuing
Smoothes traffic by storing traffic that is above the configured rate in a queue
  If queue is empty
    Traffic shaper processes the arriving packet
    Sends packet if possible
    Saves on queue if not possible
  If queue contains packets
    Traffic shaper stores arriving packet on end of queue
    Sends packet at head of queue

## Slide 19: Fragmentation & Blocking
Breaking up large packets into smaller ones
  Reduce serialization time on slow links
  Can be accomplished at either Layer 2 or Layer 3
Blocking is amount of time non-real time traffic consumes WAN bandwidth forcing real time traffic to be queued
  Rule of thumb: blocking delay = 80% voice packet size
  Exact formula: WAN BW * Blocking Delay = Fragment size (bits)