## Slide 1: Redundant Implementation Techniques

## Slide 2: Creating Redundancy
Media redundancy
Network redundancy
  Router to router
  Router to server
Network resilience
  Hot standby router protocol
  Spanning tree

## Slide 3: Redundant Connections?
Network
Network
Maybe!!

## Slide 4: What is the Problem?
Meteorite Taking Out Phone Company Central Office
Backhoe Taking Out Line
Malicious Attack Taking Out Server
Earthquake Taking Out Data Center
AT&T


## Slide 5: WAN Service Connection
Central Office
Customer Premise
Phone Switch
1 Internal premises wiring to phone company demarcation point
2 Demarc to service access pedestal
3 Connection to central office
Local Loop
{
1
2
3

## Slide 6: Parallel and Redundant Network Connections
Spanning tree protocol controls parallel line usage in bridged networks
Use different technologies
Dial-up line used only if leased lines fail
San Francisco
New York
Leased Lines
Dial-up Line

## Slide 7: Provisioning Diverse Paths
Phone Switch
Phone Switch
Denver
Minneapolis
New York
San Francisco
Different carriers may use the same facilities

## Slide 8: Always Remember
“One can never know too much about the physical circuit routing. It will inevitably come back to bite you if believe your provider.”
R.C. 1996

## Slide 9: How Clients Find Routers
AT&T

AT&T


## Slide 10: Client Connection to Router
Address resolution protocol
Explicit configuration
Router discovery protocol
Routing protocol

## Slide 11: Address Resolution Protocol
Workstation sends ARP for all destinations
Routers send a Proxy ARP in reply for remote destinations
Potential convergence time: ARP cache time-out period
ARP
ARP
Router A
Router B
ARP Reply

## Slide 12: Configuration of Default Gateway
Router A
Router B
Workstation configured with address of primary router
  Manual intervention required to re-configure with address of secondary router
  Convergence time: possibly forever (or at least until primary router is back on-line)
Knowledge of network is responsibility of workstation
To Get to the Rest of the World, I Go to Router A
Primary
Secondary
X
Router A failed.
Now what do I do?

## Slide 13: Router Discovery Protocol
ICMP
ICMP
RFC 1256 ICMP Router Discovery Protocol (IRDP)
  Extension of ICMP to enable hosts attached to multi-cast or broadcast networks to discover the IP addresses of their neighboring routers

## Slide 14: Router Discovery Protocol
Convergence time: based on router advertisement interval
Requires workstation to run some sort of router discovery protocol
Automatic re-routing to correct router when back on-line
Router Solicitation
Router Solicitation

## Slide 15: Routing Protocols
Workstation participates in routing protocol exchanges
  Routing Internet Protocol (RIP)
  Open Shortest Path First (OSPF)
Routing Update
Routing Update

## Slide 16: RIP Routing Protocol
Convergence time: 90 seconds on average
Workstation participates in routing exchange
  Workstation knows best routes
  Workstation knows unreachable routes
RIP
RIP

## Slide 17: OSPF Routing Protocol
Convergence time: ~1 second on average
Workstation participates in routing exchange
  Workstation affected by all changes in area
  Workstation knows best routes
  Workstation knows unreachable routes
LSA
LSA

## Slide 18: Default Convergence Times
RIP (90 seconds)
IGRP (270 seconds)
OSPF (~1 second)
EIGRP (~1 second)

## Slide 19: Parallel Routing Paths
Equal cost paths
No convergence time
B
C
A

## Slide 20: Full Meshed Topology
Number of circuits =
Multiple paths
Expensive
n(n-1) 2

## Slide 21: Partial Mesh Topology
Some multiple paths
More cost effective
Potential loss due to failure

## Slide 22: Hot Standby Router Protocol
Cisco proprietary protocol
  Permits network topology changes to be transparent to host systems.
  Secondary router assumes the default gateway functions of primary router.
  Permits re-routing of network traffic within 10 seconds without requiring host changes.
  Works on LANs that run OSPF, IGRP, EIGRP or IS-IS routing protocols.
  Feature of Cisco IOS software

## Slide 23: HSRP Configuration and Normal Operation
Workstation configured with address of virtual Router Z
Router A sends Router B HSRP information and ‘Hellos’
Router A responds when Router Z is addressed
Convergence time: 10 sec, worst case 30 sec
Router A
Router B
To Get to the Rest of the World, I Go to Router Z
Router Z
I Will Answer
as Router Z
HSRP
I Become
Router Z if Router A
Goes Away

## Slide 24: HSRP Failure Operation
Router B takes over when Router A fails
Convergence time: 10 sec, worst case 30 sec
No configuration changes necessary on workstation
Automatic re-direction when Router A is back on-line
Router A
Router B
Router Z
To Get to the Rest of the World, I Go to Router Z
I am Taking Over as Router A
X

## Slide 25: Using HSRP to Create Redundant Server Connection
HSRP feature is
enabled in both
router configurations
AT&T

Router A
Router B
Virtual
Router Z
LAN/WAN
Enterprise

## Slide 26: Spanning Tree Algorithm
Spanning Tree
  Ensures each LAN segment is serviced by only 1 bridge or switch
  Permits existence of redundant physical loops but maintains a loop free logical topology
Data loops cause LAN to become unusable
  Causes SAT corruption by moving source address between ports
  Causes exponential frame propagation
  Causes excess collisions due to retransmission

## Slide 27: Spanning Tree Algorithm
Defined in IEEE 802.1d
Uses a ROOT bridge to determine the active network topology
Once ROOT is selected all other bridges in the PHYSICAL topology span to create the ACTIVE topology
Active topology is a Tree which guarantees that no loops will exist

## Slide 28: Using Spanning Tree
A
B
B1
B2
LAN 1
LAN 2
Physical topology before “Spanning Out”
1
2
1
2

## Slide 29: Using Spanning Tree
A
B
B1
B2
LAN 1
LAN 2
Active topology after “Spanning Out”
Port 2 of Bridge B1 is logically disabled
1
2
1
2
STANDBY

## Slide 30: ATM Forum LAN Emulation
A Media Access Control specification, known as LANE, that allows the ATM fabric to emulate a logical Ethernet or Token Ring segment.
Definitions:
  LAN Emulation User Network Interface - Referred to as “LANE 1.0”. It defines the interface between a legacy LAN attached device and the ATM network.
  LAN Emulation Services - They serve the following functions: initialization , address registration / resolution, and data forwarding. They consist of the LECS, LES, and BUS.

## Slide 31: ATM Forum LAN Emulation
Definitions (continued):
  LAN Emulation Configuration Server, LECS - Maintains the configuration information for each emulated LAN.
  LAN Emulation Server, LES - Performs the MAC-to-ATM address resolution functions in an emulated LAN.
  Broadcast Unknown Server, BUS - Performs the multicast server function and broadcasts packets to multiple LECs.

## Slide 32: ATM Forum LAN Emulation
Definitions (continued):
  LAN Emulation Client, LEC - Multiple LECs connect to the LANE services. Client functionalities are typically implemented on adapters, routers, and ATM-to-LAN edge devices.

## Slide 33: LAN Emulation
Edge Device implements Proxy LANE Client and MAC Layer LANE
Proxy client forwards unregistered MAC addresses
Legacy LAN Host requires no changes
LANE emulates a bridged LAN segment
Uses AAL 5 to segment data frames into cells
LANE 1.0 does not support redundant servers

## Slide 34: LANE Network Configuration
Ethernet Network
LANE
“Edge Device”
Proxy LEC
Switch
PNNI
LANE Clients
LEC
UNI
Switch
Switch
Switch
Bridge
Bridge
Bridge
Token Ring
Network
Ethernet Network
LANE Servers
LECS, LES, BUS

## Slide 35: LANE Protocol Stack
Application
NDIS/ODI Driver
LAN Emulation
AAL5
ATM
Physical
ATM
Physical
Physical
LAN
Emulation
AAL5
ATM
Physical
Application
MAC
Physical
NDIS/ODI
Driver
Physical
MAC
Bridging
Software
ATM Host
LAN Host
ATM LEC
“Edge Device”
ATM Switch