## Slide 1: Calculating Response Time

## Slide 2: Response Time
Response Time, RT
  The time interval (elaspsed time) starting when the SEND key on the remote device is pressed until the last character of the reply is received.
  Composed of seven components

## Slide 3: Elements of Response Time
Htp, Sto, Wto
Terminal
Sti, Wti, TDi, TDo
RT=
Htp+Sto+Wto
+Sti+Wti+TDi+TDo
Tprop

## Slide 4: Elements of Response Time
Input device delay time, TDi
  Delay created by the device in moving the input message from the device output buffer to the communications line
Input wait time, Wti
  Time the input message waits in the device output buffer for acknowledgment from the FEP. Calculation of this value requires the use of queueing theory

## Slide 5: Elements of Response Time
Input service time, Sti
  Time to service an input request. Includes the polling time, connection delay time, and message transmission time
Host processing time, Htp
  Total time spent in the CPU, FEP, and all associated computer elements processing the input message and creating the output message

## Slide 6: Elements of Response Time
Output wait time, Wto
  The time the output message waits at the FEP port before being sent to the communications line. Calculation of this value requires the use of queueing theory
Output service time, Sto
  Time required to service an output request. Primarily the time to transmit the output message to the remote device

## Slide 7: Elements of Response Time
Output device delay time, TDo
  Delay created by the device in moving the output message from the device input buffer to the display medium.
TDi, TDo, and Htp are considered fixed delay times. TDi and TDo are generally small and are often ignored for single function devices.

## Slide 8: Elements of Response Time
Intelligent devices and devices that are connected to controllers will usually have processing and waiting delays.
Controller and intelligent device delays may be ignored if they are small when compared to other circuit delays.

## Slide 9: Elements of Response Time
Host processing delays include all non-network delays associated with the processing of messages.
Host delays may have significant impact on transaction processing.
Host delays are not controllable by the network designer.
Designer must obtain both a mean value and standard deviation for Htp.

## Slide 10: Elements of Response Time
Host delays can be minimized by tuning some system elements.
  Host channel attention delay
  FEP buffer size
  FEP line scheduling
A recommended design approach
  “FOB” the FEP
  Allows Htp to be ignored

## Slide 11: Computing Service Time
Service time is the time required for a line to process a request or a reply
  Stx = Ttx + TCD + TPD
  Ttx - message transmission time
  TCD - input connection delay time
  TPD - input polling delay time
  x - input or output

## Slide 12: Message Transmission Time
Time for the device or the FEP to transmit the message text and protocol overhead

## Slide 13: Calculating Throughput
Calculate text transmission time
Compute throughput

## Slide 14: Connection Delay Time
Time for the FEP to connect to a device so that a transaction can be conducted

## Slide 15: Polling Delay Time
Time spent by FEP finding a device that has input to send. Only applies to multi-drop lines
NEP accounts for average number of unsuccessful polls

## Slide 16: Polling Delay Time
TPD only applies to input messages because the input message address identified the desired output device
Factors that effect NEP
  Number of messages arriving at each device
  Size of polling table used by FEP
  Polling algorithm used by FEP

## Slide 17: Polling Delay Time
Assumptions used in calculating NEP
  Each device is polled equally
  Each device receives same number of messages
  No throttling of high volume devices
  No throttling of inactive devices

## Slide 18: Example Calculations
Determine Tti and throughput for a message containing 80 characters of text and 20 characters of protocol overhead
  Use 10 b/c (8 bits data + 2 bits framing)
  Line speed is 4800 bps
  Result: Tti = 0.2083 sec
Determine Tput for these conditions
  Result: Ttext = 0.133 sec
  Result: Tput = 0.64 or 64%

## Slide 19: Example Calculations
Determine TCD if MTA = 0.0485 sec and 3 line turn arounds are required
  Result: TCD = 0.1455 sec
Determine TPD for a multi-drop line with 7 devices and a 10 character poll message. Other parameter values remain the same
  Result: Tpoll = 0.0208 sec, TPD = 0.2079 sec

## Slide 20: Example Calculations
Calculate the input service time, Sti
  Result: Sti = 0.2083 + 0.1455 + 0.2079 = 0.5617 sec

## Slide 21: Error Retransmission
Service time adjustment to account for the retransmission of errored messages
Bit Error Rate, BER -- rate at which errors are likely to occur
Retransmission probability

## Slide 22: Error Retransmission
Normally 1 >> BER so can use an approximation for the retransmission probability

## Slide 23: Effect on Service Time
Retransmissions due to error affect
  Message transmission time
  Connection delay time
  Polling delay time
Adjust service time to include effects of retransmission

## Slide 24: Example Calculations
Consider BER
  Analog line 1/100000 = 10-5
  Digital line 1/1000000 = 10-6
Calculate RP for previous example using BER = 10-5
  Result: RP = 0.01 or 1%
Determine the adjustment to Ttx
  Result: Ttx = 0.5674 sec, which is a 5.7 msec increase

## Slide 25: Calculating Wait Time
Wait time, Wtx, time a message sits in a queue waiting to be serviced
Calculating Wtx requires the use of queueing theory

## Slide 26: Calculating Wait Time
Formula for Wtx is the full-duplex form
Wtx = 0 for pt-to-pt lines unless remote device is a line controller
Consider 2 special cases for
  constant service time, all messages are the same size
  exponential service time, messages have a random distribution (worst case)

## Slide 27: Example Calculations
Calculate mean input wait time, Wti, for a system if 1200 messages arrive during the busy hour and the mean input service time, Sti, is 0.57 sec.
  Result: Wti = 0.067 sec if = 0
  Result: Wti = 0.134 sec if = 0.325 sec
Observation: Wait time doubles when the message mix is changed

## Slide 28: Example Calculations
Calculate mean output wait time, Wto, for the previous system if the mean output service time, Sto, is 0.75 sec.
  Result: Wto = 0.125 sec if = 0
  Result: Wto = 0.250 sec if = 0.563 sec

## Slide 29: Example Calculations
Calculate response time, RT, if Htp = 0.125 sec and the terminal delays, TDi and TDo are negligible
  Result: For constant distributions
  RT = 0.125 + 0.067 + 0.57 + 0.125 + 0.75
  = 1.637 sec
  Result: For exponential distributions
  RT = 0.125 + 0.134 + 0.57 + 0.25 + 0.75
  = 1.829 sec

## Slide 30: Assumptions
Our calculations assume that
  The circuit is full duplex
  The FEP can simultaneously service input and output
  The link protocol used does not segment messages into packets or frames
At least one of these assumptions is false
Might need to make some adjustments

## Slide 31: Full Duplex Adjustment
Same FEP port handles input and output
  Give output priority
  Adjust input service

## Slide 32: Full Duplex Adjustment
Observation
  As the output line utilization, , increases StiA increases because the percentage of Sto added to Sti approaches Sto
  With heavy load the system behaves in a half duplex manner
  Input is required to wait until output is complete

## Slide 33: Example Calculations
Determine the adjustment for the previous example where
  Sti = 0.57 sec, Sto = 0.75 sec, = 0.25
  Result: StiA = 0.664 sec a 16.5 % increase in the input service time when constant service time distributions exit
  Result: StiA = 0.758 sec a 33% increase in the input service time when exponential service time distributions exit

## Slide 34: Message Segmentation
Improves throughput
Reduces effect of error retransmission
Requires more complex system
Require additional buffers
Segmentation valuable
  Very long message
  Probability of retransmission high
  Reaction time is long

## Slide 35: Message Segmentation
Algorithm computes optimum segment size
  Total message length
  Line BER, line speed
Segment overhead provides
  Sending terminal address
  Number of segments in message
  Number of characters in segment
  Segment position in message
  Error checking data for segment

## Slide 36: Message Segmentation
Consider a system that transmits 64 character segments, 56 data + 8 overhead characters
Lspeed = 2400 bps, b = 8 bits, dint-seg = 8 msec
Compute: Transit time, Ttrans, for a 24X80 = 1920 character CRT screen
  Ncomp-seg = 1920/56 = 34.3 = 34 segments
  Mlast-seg = 1920 - 34*56 = 16 chars
  Tseg = (56 + 8)*8/2400 = 0.213 sec

## Slide 37: Message Segmentation
  Rp-seg = 10-5*64*8 = 0.0052
  Tseg-A = 0.213/(1 - 0.0052) = 0.214 sec
Consider the last segment
  Tlast-seg = (16 + 8)*8/2400 = 0.053 sec
  Rp-last-seg = 10-5*24*8 = 0.0019
  Tlast-seg-A = 0.053/(1 - 0.0019) = 0.053 sec
Compute the total transit time, Ttrans
  Ttrans = Ncomp-seg *(Tseg-A + dint-seg) + Tlast-seg-A
  = 34*(0.214 + 0.008) + 0.053 = 7.60 sec

## Slide 38: Message Segmentation
If transmit as 1 message, then use existing formulas to calculate Ttrans

## Slide 39: Message Segmentation
Transit time is nearly equal
Error rate is lowered
For single message transmission

## Slide 40: Message Segmentation
For segmented message
Value of segmentation is reduction of the error rate which improves throughput

## Slide 41: Propagation Delay
Long distance transmissions have delay caused by transmission of electrical signals at near the speed of light
  Speed of light 186,000 miles/sec
Satellite circuits have a circuit distance of 45,000 miles + modem pair delay
  Satellite propagation delay 0.242 sec + modem pair delay of 0.012 sec each way
Modem pair delay function of modem type

## Slide 42: Propagation Delay
Adjustments for TCD when required
Adjustment for TPD when required

## Slide 43: Response Time
Mean response time may not be sufficient
Often need to know largest value of response time for 95% of observations
Will use element variances to calculate this value of response time
Response Time
Mean
95%

## Slide 44: Response Time
Variance of response time elements
  Message transmission time
  Connection delay time
  Polling delay time
  Wait time
  Host processing time
  Terminal delay times

## Slide 45: Variance of Elements
Message transmission time
  Constant message distribution
    VTtx = 0
  Exponential message distribution
    VTtx = Ttx2
Connection delay time
  Fixed time determined by protocol, modem type, line length
    VTCD = 0

## Slide 46: Variance of Elements
Terminal delay times
  Fixed times established by equipment manufacturer
    VTDx = 0
Polling delay time
  Inquiries only on multidrop lines
  Based on mean number of expected polls

## Slide 47: Variance of Elements
Wait time
  Complex relationships envolving the service time distribution and the line utilization
  Will not consider
Host processing time
  Depends on distribution of processing time
    For constant distribution VHtp = 0
    For exponential distribution VHtp = Htp2

## Slide 48: Response Time Standard Deviation

## Slide 49: Adjusted Response Time
Two standard deviations cover 95% of observations
Another useful value is the 90% range

## Slide 50: Final Comments
Each input output sequence is processed to completion
Response time is affected by variations in
  Volume of messages
  Length of messages
  Distribution of messages
  Line utilization
  Line speed
  Host processing time

## Slide 51: Multiplexors
l
l
l
l
RThs
RTls
RT = RThs + RTls