## Slide 1
Synchronous Optical NETwork
An Introduction to SONET

## Slide 2
What is SONET?
Belcore term for North American version of Synchronous Digital Hierarchy
Transport interface and transmission method that provides
  High speed with low error rate
  Fiber-optic multiplexed transmission
  International standard for interfacing PTTs, IXCs and LECs

## Slide 3
Benefits of SONET
In-band operations
  Lowers transmission costs
  Increases transmission efficiency
Administration
Maintenance
Provisioning

## Slide 4
SONET Characteristics
SONET transfer mode defines aspects of digital transmission protocol
  Switching
    Synchronous Transfer Mode
      Circuit switching
    Asynchronous Transfer Mode
      Cell relay
  Multiplexing
    Fixed frame format
      User data, management, maintenance, and overhead

## Slide 5
Basic SONET Structure
Synchronous Transport Signal level 1 (STS-1)
Optical Carrier Signal (OC-N)
Aggregate 51.84 Mbps STS-1 bit stream becomes 51.84 Mbps OC-1 bit stream when converted from “electrical” to “fiber optic”
  810 byte per frame
  8000 frames per second
DS3 electrical signal = OC-1 optical signal

## Slide 6
SONET Multiplexing
Direct multiplexing into STS-N payload
  SONET speeds
    DS1 to OC-3c
    DS3 to OC-12c
  Asynchronous or synchronous service
Individual signals down to DS1 can be directly accessed without demultiplexing
Stable clock source required
  Stratum 1 preferred
  Stratum 3 acceptable

## Slide 7
SONET Architecture
PATH
LINE
SECTION
PHYSICAL
Transport
Pointer Functions
Manages Interfaces
from Physical Layer
Physical Interface
(Photonic)
Synchronization
Channel Multiplexing
Protection Switching

## Slide 8
Layer Descriptions
Physical Layer - defines physical fiber type, path and characteristics
  1550 nm dispersion-shifted fiber
  1310 nm convention glass fiber
  Includes electrical interfaces that become STS-1 frame virtual channels
Section Layer - builds SONET frames from
  Lower SONET interfaces
  Electrical interfaces

## Slide 9
Layer Descriptions
Line Layer - provides communication channel between line-terminating equipment
  Synchronization
  Channel multiplexing
  Protection switching
Path Layer - provides management of data transfer across SONET network