## Slide 1: Chapter 4
TCP/IP and OSI

## Slide 2: Communication Architectures
Basic concepts and definitions
Simplified three layer model
TCP/IP - The Internet Protocol
Open Systems Interconnection (OSI)

## Slide 3: Definitions
Communications -- a process that allows information to pass between a sender and a receiver
Telecommunications -- communications by electrical or electromagnetic means, usually over a distance
Data communications -- movement of coded information over a distance by electrical or electromagnetic means

## Slide 4: Communication Requisites
Individuals = The communicating users
Information = The application that solves a business problem
Information code = The symbols for representing the business problem
Exchange = The Network provides the mechanism and the medium
Process = The rules for communicating

## Slide 5: Basic Elements of a Telecommunications System
Source
Sink
Medium

## Slide 6: Identifying User Needs
User’s view the network from outside
User’s View
of the
Network

## Slide 7: What Users Want?
An unlimited resource with totally transparent services
Easy to connect and reconfigure
Reliable with good data integrity
High availability, large throughput, and fast response time

## Slide 8: Financial Industry
High availability
High speed LANs
Security
Integrated data centers
Diverse computing requirements
Branch systems
Power users

## Slide 9: Retail Industry
High availability
Diverse computing requirements
Low speed access
High speed core
Security
Low cost

## Slide 10: Communications Industry
Low speed, high concentration
Multimedia services
Metropolitan requirements in cities
Open systems
Bandwidth optimisation
Creating ‘fat pipes’
Internet service provider bundles

## Slide 11: What is a Standard?
A procedure or process established by authority as a rule for the measure of value or quality
A procedure or process established by custom or general consent as a model or example
A structure that serves as a basis for a procedure or process
Webster’s Dictionary

## Slide 12: Why Develop Communication Standards?
To provide a common reference point
To provide mainstream evolution
To allow common product development
To enhance product marketability
To promote interoperability

## Slide 13: What is a Network Architecture?
A formal logical structure of the interactions and functions required to provide communication services to end users.

## Slide 14: What is Open Systems Interconnect?
Standards for the exchange of information among “systems” that are open to one another by virtue of their mutual use of standards.

## Slide 15: The Three-Layer Model
Application layer
  Procedures that solve the user’s business problem
Transport layer
  Common procedures used for reliable transfer of application data
Network access layer
  Physical exchange of data between user and network

## Slide 16: TCP/IP Communications
TCP/IP developed by DARPA
Internet protocols communicated across LANs and WANs
Layer 3/4 protocols plus network applications
TCP/IP

## Slide 17: TCP/IP Standard
Transmission Control Protocol
Internet Protocol
Protocols
  UDP, TCP, IP
  FTP, VT
  SMTP, SNMP

## Slide 18: TCP/IP Architecture
Network access
  Physical connection
Internet protocol
Host-to-host transport
Standard Applications
  Telnet, File transfer, Mail, Network management

## Slide 19: Communications Using TCP/IP Architecture
Operating System
Host
Network
Access
IP
TCP
Appl
Appl
Operating System
Host
Network
Access
IP
TCP
Appl
Appl
NAP
NAP
IP
Router
Subnetwork
Subnetwork

## Slide 20: TCP/IP Internet Protocol
Connectionless service
Uses datagrams
Defines internet addresses
  4 byte length
  Uses dotted decimal format
Provides packet routing

## Slide 21: IP Networking
Addressing permits end station communications
Path choice depends upon location
Each location assigned a unique address

## Slide 22: IP Address Classes
Address
Class
A
B
C
Decimal
Value
1st Byte
1-126
128-191
192-223
High
Order
Bits
0
10
110
Class D: Multicast usage - 224.0.0.0
Class E: Experimental usage - 240.0.0.0

## Slide 23: TCP/IP Transport Protocols
TCP - Transmission Control Protocol
  Connection oriented
  End-to-end
  Service access points
    Ports
    Sockets
UDP - User Datagram Protocol
  Unreliable

## Slide 24: TCP/IP Frame Structure

## Slide 25: ISO Open Systems Interconnect
Interconnects heterogeneous computer systems
Supports a variety of data formats
Defines data exchange protocols
Allows internodal communication
Fosters cooperation

## Slide 26: ISO Reference Model
Provides a layered architecure
Defines a hierarchical structure
Contains set of well defined functions
Creates a framework
  Independent development
  Simultaneous development

## Slide 27: OSI Layers
Application
  Provides services to users of OSI environment
Presentation
  Provides transformations for data
Session
  Provides control structure for communications
Transport
  Provides reliable end-to-end data transfer

## Slide 28: OSI Layers
Network
  Provides independence from transmission and switching technologies
Data link
  Provides reliable data transfer across a physical link
Physical
  Provides for the transmission of unstructured bit streams over physical links

## Slide 29
OSI Environment

## Slide 30: Layer-Specific Functions
Protocol specifications
  Peer-to-peer
Service definitions
  Layer to layer
Addressing
  Service access point (SAP)

## Slide 31: IBM System Network Architecture
First release 1974
Provided hierarchical structure
Defined network addressable units
  SSCP, PU, LU
Multilayer architecture
  Differs from ISO
  Includes management

## Slide 32: SNA Network Devices
LU
LU
LU
PU
SSCP
Host
LU
LU
LU
PU
LU
LU
LU
PU
LU
LU
PU
PU
Communication
Controller
Cluster
Controller
Cluster
Controller
PUT4
PUT2
PUT2.1
PUT2.1
PUT5