## Slide 1: Analog, Digital and IP Telephony
Source:
Cisco Systems Networkers ‘98
Denver, CO
June 1998
Notes: 1
3
3

## Slide 2: Standard Telephone Equipment
Telephone set
Key system
  Optimizes use of telephone sets to lines
  Mechanical to electronic
  2 to 10+ sets typically
PBX (Private Branch Exchange)
  Advanced features and call routing
  10s to 100s of telephone sets
Central office switch
Notes: 3

## Slide 3: Analog Telephony—POTS Basics
Analog voice technology dates back to the 1900’s
Information exchange based on voltage, current flow, grounding, etc.
Tip
Ring
Sleeve

## Slide 4: Telephony - Basic Call Progress
On hook
Off hook - signal switch receive dial tone
Dialing - sending digit string to switch
Switching - routing call to destination
Ringing - signaling remote
Talking - information exchange
On hook - end call

## Slide 5: Off-Hook Signaling
Loop Start (almost all telephones)
  Seizure is detected when current flows through local loop, due to off-hook
Ground Start (PBXs)
  Seizure is detected when one wire is grounded
  Seizure can be initiated in both directions
Switch
Switch
Notes: 12

## Slide 6: E&M Signaling
PBXs, switches
  Separate signaling leads for each direction
  E-Lead (inbound direction)
  M-Lead (outbound direction)
  Allows independent signaling
State
On-Hook
Off-Hook
E-Lead
Open
Ground
M-Lead
Ground
Battery Voltage
Notes: 15

## Slide 7: Call Signaling and Addressing
Analog transmission
“In-Band” signaling
Pulse or tone based
Call progress tones
are network generated
Digital transmission
“Out-of-Band” signaling
Message based
Call progress tones
are locally generated
ISDN
Dial Pulse
DTMF
Notes: 16
Dial Pulse Address Signaling opens and closes the tip and ring connectors at specific intervals interrupting current.
  # of interruptions = digit dialed
  Pulse speed is nominally 10pps +/- 1pps
  Pulse period is nominally 0.1 second (open)
  Interdigit interval is ~700ms
  Dialed Digits toggle the A bit in DS1
Dual Tone Multifrequency Address Signaling uses pairs of frequencies transmitted over the loop. Permits end-to-end signaling after the connection is made, i.e. IVR/Audiotex
60ms Break / 40ms Make
  Tones are digitized and decoded
ISDN signaling is message based

## Slide 8: Pulse Dialing
Make
(Circuit Closed)
Break
(Circuit Open)
Off-Hook
Dialing
Inter-Digit
Next Digit
Pulse Period
(100 ms)
US:60/40 Break/Make
700 ms
Notes: 17

## Slide 9: “Touch” Tone Dialing
1
2
3
A
4
5
6
B
7
8
9
C
*
0
#
D
Dual Tone Multi-frequency (DTMF)
1209
1336
1477
1633
697
770
852
941
Digit Timing:
60 ms Break
40 ms Make
Not part of standard
telephone set
Notes: 18

## Slide 10: Voice Channel Bandwidth
Output
Voltage
or
Energy
Frequency
(K-Hertz)
1
2
3
4
.2
Voice Signal
Voice Channel
Tone Dialing
Signals
Systems Control
Signals
Notes: 20

## Slide 11: Early Switching Systems
Manual control—Switch/cord boards
Patch Cord
Pairs
Off-Hook Indicator
Manual Ring
Tip
Ring
Notes: 22

## Slide 12: Types of Voice Circuits
Serving Area
415-NXX-XXX
Serving Area
510-NXX-XXX
415-577-3800
415-655-1400
FX
Foreign Exchange
415-577-3801
OPX
Off-Premises Ext.
ARD
Auto Ring Down
Class 5
Class 5
Switch
Switch
Notes: 24

## Slide 13: Normal Signal Flow
2-Wire Local Loop
Central Office
Receive
Direction
Transmit
Direction
2- to 4-wire hybrid combines receive and transmit signals over the same pair
2-wire impedance must match 4-wire impedance
Talker or Listener echo may be noticeably present
2w-4w
Hybrid
Notes: 26

## Slide 14: How Does Echo Happen?
Central Office
2w-4w
Hybrid
Echo is due to a reflection
Impedance Mismatch at the 2w-4w Hybrid
Is the Most Common Reason for Echo
Receive
Direction
Transmit
Direction
Rx and Tx
superimposed
2-Wire Local Loop
Notes: 27

## Slide 15: Echo Is Always Present
Echo as a problem is a function of the echo delay, and the magnitude of the echo
(dB)
Echo Path Loss
Echo Path Delay (ms)
Echo Is Unnoticeable
Echo Is a Problem
Notes: 28

## Slide 16: Ways to Defeat Echo
Increase the loss in the echo path
  Can often be the solution
  Disadvantage: Static setting, reduces the signal strength of the speaker
Echo suppresser
  Acts like a noise gate, effectively making communications half-duplex
Notes: 29

## Slide 17: Digital Telephony
Backbone to largest interoperable network in the world
Signaling information exchange based on ~30 year old concepts
  Twiddling bits based on ~100-year old signaling
Analog telephony emulation
  Voice encoding
  Limited signaling
  Loop consolidation

## Slide 18: Digital Telephony Access
Digital Trunking
Switch
Switch
Analog Loop
Digital Network
POTS
Switch
CB
Digital Loop Digital Network
ISDN
Switch
Notes: 33

## Slide 19: Digital Telephony
= Sample
8 kHz (8,000 Samples/Sec)
Codec Technique
Sampling Stage
Analog Audio Source
Pulse Code Modulation—Nyquist Theorem
Voice Bandwidth =
300 Hz to 3400 Hz
Notes: 34
Analog to Digital Conversion requires three operations:
  Sampling
  Quantizing
  Encoding
Nyquist Theorem—When a signal is sampled instantaneously at the transmitter at regular intervals and at a rate at least twice the highest frequency in the channel, then the samples will contain sufficient information to allow an accurate reconstruction of the signal at the receiver
Filters used to block signals above 4kHz and below 300Hz to avoid a condition called aliasing. Aliasing happens when a digital point can represent more than one signal.

## Slide 20: Pulse Code Modulation: Analog to Digital Conversion
Stage 1
Quantizing Stage
Quantizing Noise
100100111011001
A-Law (Europe)
µ-Law (USA, Japan)
Notes: 35

## Slide 21: Digital Telephony - T1
T1 ITU-T G.733
Sampling Frequency
Channel Bit Rate
Time Slots per Frame
Channels per Frame
Bits per Frame
System Bit Rate
Framing
Signaling
8 kHz
DS0—64 kbps
24
24
24 x 8 + 1 = 193
D4/Super Frame (12)
Extended Super Frame (24)
Framing Indicator
193rd Bit of Frame
8,000 x 193 = 1.544 Mbps
“Robbed Bit” Channel Associated Signaling
D4/Super Frame Extended Super Frame
LSB/Channel LSB/Channel
Frame 6 and 12 Frames 6, 12, 18, 24
Common Channel Signaling - Channel 24

## Slide 22: Digital Signaling Schemes
Bit Frame
A 6th
B 12th
C 18th
D 24th
Extended Super Frame with Channel Associated Signaling
Supervision
On/Off Hook
Address Signaling
(Dial Pulse)
Audio
Address Signaling
(DTMF)
Notes: 40

## Slide 23: Multi-frame Composition
1
8
3 ms
One ESF Multi-frame
1
24
1
24
12
1 Frame, 125us, 193bits 24 Time Slots
12
1 Channel Time Slot, 5.18us
1 Bit time = 648ns
Notes: 43

## Slide 24: Traditional Network Clocking
PBX
PRS
Master Clock
Toll Office
PBX
Stratum
1
2
3
4
Timing
Timing
Timing
Timing
One per LATA
Bits Distribution
.00001ppm
End Office
DCS
End Office
Notes: 44
Just in case you care
  Stratum 1
    Short Term Accuracy = +/-1 x 10 -11
    Long Term Stability = Unquestionable
    LTS is expressed as total over 20yrs free running
    Sources = Atomic Clocks, GPS, Loran-C
  Stratum 2
    STA = +/-1 x 10 -10
    LTS = +/-1.6 x 10 -8
    Must track or lock to any stratum 2 clock
  Stratum 3
    STA = < 256 frame slips/day
    LTS = +/-4.6 x 10 -6
    Must track or lock to any stratum 3 clock
  Stratum 4
    STA = Undefined
    LTS = +/-32 x 10 -6
    Must track or lock to any stratum 4 clock
  Locking all switches to a single clock ensures that they all send and receive bits at the same rate. Accurate synch can reduce buffer sizes, which will reduce jitter.
  page 474 of orange book

## Slide 25: Voice Coding and Compression
Speech coding schemes
Subjective impairment analysis: mean opinion scores
Digitizing voice
Voice compression
  ADPCM
  CELP (LD-CELP and CS-ACELP)
  Silence Removal Techniques (DSI using VAD)

## Slide 26: Voice Compression Technologies
Bandwidth
(Kbps)
Quality
Unacceptable
Business
Quality
Toll
Quality
8
16
32
24
64
0
*
PCM (G.711)
*
ADPCM 32 (G.726)
*
ADPCM 24 (G.726)
*
ADPCM 16 (G.726)
*
LDCELP 16 (G.728)
*
CS-ACELP 8 (G.729)
*
LPC 4.8
(Cellular)
Notes: Digital Voice uncompressed is Pulse Code Modulation (PCM) at 64 Kbps.
Various methods of voice compression have varying bit rates and subjective “qualities”, which are really impairment analysis.
To understand these we need to understand the three main forms of digital speech coding: Waveform, Vocoders and Hybrids.

## Slide 27: Speech Coding Schemes
Waveform coders
  Non-linear approximation of the actual waveform
  Examples: PCM, ADPCM
Vocoders
  Synthesized voice
  Example: LPC
Hybrid coders
  Linear waveform approximation with synthesized voice
  Example: CELP
Notes: LPC = Linear Predictive Coding: Precursor to CELP
Channel = Frequencies divided up into discreet channels, generated at the far end
Phase = Phase structure analyzed, sent and generated at the far end
APC = Adaptive Predictive Coding: Used together with LPC to come up with CELP
CELP = Code Excited Linear Predictive
SELP = Self Excitation
Vocoding schemes are very low bit rates (2.4 is possible) but sound very synthetic, in fact training is necessary to become accustomed to the voice. These are typically military applications where battlefield conditions are unpredictable, yet the synthesized output is always the same. Also, most are half-duplex.
All of the Hybrid coding schemes are part of what’s called Analysis-by-Synthesis coding (AbS), which defines all generally used speech coding techniques in the 4.8 Kbps- 16 Kbps range. Since AbS continuously analyzes and “learns” what to expect a speech waveform should look like in the near term (5 ms) future, it is a much higher quality than simple Analysis-and-synthesis. It’s the feedback loop which allows the codebook to continuously learn.

## Slide 28: Mean Opinion Score
Source
Impairment
Channel Simulation
“Nowadays, a chicken leg is a rare dish.”
1
2
3
4
5
1
2
3
4
5
Rating Speech Quality Level of Distortion
5 Excellent Imperceptible
4 Good Just perceptible, not annoying
3 Fair Perceptible, slightly annoying
2 Poor Annoying but not objectionable
1 Unsatisfactory Very annoying, objectionable
MOS of 4.0 = Toll Quality
Codec ‘X’

## Slide 29: Subjective Impairment Analysis
5
4
3
2
1
2
4
8
16
32
64
Kbps
Subjective Quality (MOS)
Hybrid Coders
Vocoders
Waveform Coders
Score
Quality
Description of Impairment
5
4
3
2
1
Excellent
Good
Fair
Poor
Bad
Imperceptible
Just Perceptible, not Annoying
Perceptible and Slightly Annoying
Annoying but not Objectionable
Very Annoying and Objectionable

## Slide 30: Digitizing Voice: Using PCM Waveform Encoding
Nyquist Theorem: sample at twice the highest frequency
  Voice frequency range: 300-3400 Hz
  Sampling frequency = 8000/sec (every 125us)
  Bit rate: (2 x 4 Khz) x 8 bits per sample
  = 64,000 bits per second (DS0)
By far the most commonly used method
CODEC
PCM
64 Kbps
= DS0

## Slide 31: Companding
Linear coding to digital results in small amplitude signals having poorer resolution than larger amplitude signals
u-Law and A-Law coding uses more bits for smaller amplitude signals
Result: uniform SQR (signal to noise quantization ratio) across input range

## Slide 32: Non-Linear vs. Linear Encoding
Non- Linear Encoding
Closely Follows Human Voice Characteristics
High Amplitude signals have more quantization distortion
Input
Output
Linear Encoding
Relatively easy to analyze, synthesize and regenerate
All amplitudes have roughly equal quantization distortion
Input
Output

## Slide 33: Waveform Coders
Sampling
Filtering
Encoding
Quantizing
1110010010010110
Waveform
ENCODER
Waveform
DECODER

## Slide 34: Voice Compression
Objective: reduce bandwidth consumption
  Compression algorithms are optimized for voice
  Unlike data compression: these are “loose”
Drawbacks/tradeoffs
  Quantization distortion
  Tandem switching degradation
  Delay (echo)

## Slide 35: Voice Compression: Using ADPCM
Adaptive Differential Pulse Code Modulation
  Waveform coding scheme
  Adaptive: automatic companding
  Differential: encode the changes between samples only
  Rates and bits per sample:
    32 Kbps = 8 Kbps x 4 bits/sample
    24 Kbps = 8 Kbps x 3 bits/sample
    16 Kbps = 8 Kbps x 2 bits/sample

## Slide 36: Voice Compression: Using CELP
Code excited linear predictive
  Hybrid coding scheme
Very high voice quality at low bit rates, processor intensive, use of DSPs
G.728: LD-CELP - 16 Kbps
G.729: CS-ACELP - 8 Kbps
  G.729a variant— “stripped down” 8 kbps (with a noticeable quality difference) to reduce processing load, allows two voice channels encoded per DSP

## Slide 37: Code Excited Linear Predictive
Input to coder is converted from 8 bit PCM to 16 bit linear PCM sample
Coder employs a codebook which uses feedback to continuously analyze, “learn” and predict the voice waveform
Coder is “excited” by a white noise generator
Mathematical result (recipe) is sent to far end decoder for synthesis and generation of voice waveform

## Slide 38: Conjugate Structure Algebraic CELP
CS-ACELP requires use of digital signal processors
80 sample frames (10ms) of 16-bit linear PCM data into 10 8-bit codewords
A “look-ahead” of 5 ms is added
Noise reduction and pitch-synthesis filtering adds to processing requirements
8 Kbps data rate
Notes: The TI chip was chosen because it has 64Kx32 SRAM, FPGA Dynamic Gate Array, and a bus driver/transceiver (channelized interface at up to 2.048 Mbps, to support T1 or E1 interfaces). The CELP functions are performed on the TI chip.
Also, the TI chip is used for echo cancellation and fax detection. It is capable of 4 channels of PCM w/ echo cancellation/fax detection, 2 channels of ADPCM with echo cancellation/fax detection, or one channel of LD-CELP or CSA-CELP with echo cancellation/fax detection.

## Slide 39: Packetized Voice Is Tolerant of “Occasional” Packet Loss
missing packet
G.729 vocoder algorithm
The friendly “retransmission” is of no use in the Voice world… late is as good as never
Complex “concealment strategy” in algorithm interpolates lost packets based on context

## Slide 40: Consecutive Packet Losses Degrades Voice Quality
Consecutive
Frames Lost: 1 2 3 4 5
M.O.S. : 4.2 3.2 2.4 2.1 1.7
“G.729 Error Recovery for Internet Telephony”,
Jonathan Rosenberg, Lucent Technology and Columbia University
V.O.N. Conference 9/97

## Slide 41: Low Delay CELP
Similar to CS-ACELP, except LD-CELP uses smaller codebook and operates at 16Kbps to minimize delay to between 2-5 ms (no “look-ahead”)
10-bit codeword is produced from every five samples of speech from the 8 Khz input
Four of these 10-bit codewords are called a “subframe” which takes approximately 2.5 ms to encode
2 of these “subframes” are combined into a 5 ms block for transmission

## Slide 42: Voice CODECs
PCM
Encoder
111001001001011
Human
Speech Model
Analysis
VocalCords
Throat
Nose
Mouth
Model
Parameters
10110010
Sample
Frames
Parameters
Model
Parameters
Synthesis
PCM
Decoder
Sampling
Filtering
Encoding
Quantizing

## Slide 43: Digital Speech Interpolation
Voice Activity Detection (VAD)
  Removal of voice silence
  Examines voice for power, change of power, frequency and change of frequency
  All factors must indicate voice “fits into the window” before cells are constructed
  Automatically disabled for fax/modem
Notes: Very effective in real-time bandwidth efficiencies
VAD removes ~ 60% of cells, renders a full-duplex conversation half-duplex as far as the network is concerned
All unused bandwidth is made available to other bursty applications

## Slide 44: Voice Activity Detection
Voice “Spurt”
Silence
Pink Noise
Time
Voice
Activity
(Power
Level)
SID Buffer
SID
Hang Timer
No Voice
Traffic Sent
B/W Saved
- 54 dbm
- 31 dbm
Voice “Spurt”

## Slide 45: Bandwidth Requirements
Voice Band Traffic
Encoding/
Compression
Result
Bit Rate
G.711 PCM
A-Law/u-Law
64 kbps (DS0)
G.726 ADPCM
16, 24, 32, 40 kbps
G.729 CS-ACELP
8 kbps
G.728 LD-CELP
16 kbps
G.723.1 CELP
6.3/5.3 kbps
Variable

## Slide 46: Voice Quality
Compression Method
MOS Score
Delay (msec)
64K PCM (G.711)
4.4
0.75
32K ADPCM (G.726)
4.2
1
16K LD-CELP (G.728)
8K CS-ACELP (G.729)
4.2
15
8K CS-ACELP (G.729a)
15
3–5
4.2
3.6
Anything Above an MOS of 4.0 Is “Toll” Quality

## Slide 47: Voice Network Transport
Typically TDM circuit-based:
  T1/E1
  DS3/E3
  SONET (OC3, OC12, etc.)
But can also be packet-based:
  ATM
  Frame Relay
  IP

## Slide 48: Overall Delay
First Bit Transmitted
Last Bit Received
Network
A
A
Sender
Receiver
t
PBX
PBX
Network Transit Delay
Processing
Delay
Processing
Delay
End-to-End Delay
(Goal: < 150 msec)

## Slide 49: Delay Variation: “Jitter”
t
t
Sender Transmits
Sink Receives
A
B
C
A
B
C
D1
D2 = D1
Sender
Receiver
Network
D3 = D2

## Slide 50: Adaptive Clocking
In-Bound Cells
Outbound
Frames
Transmit Clock
Reassembly FIFO Queue
Transport Network
PBX1
PBX2

## Slide 51: VoIP Gateway Applications
PSTN gateway service
Route replacement/toll bypass
  Most common application
PBX OPX “extension”
H.323 interoperability
  Supports voice-enabled Web applications

## Slide 52: Internet Telephony Service Provider
POP (i)
Authentication, Call Routing, Billing and Settlement Server
Settlement Provider
(Trusted 3rd Party)
ISP “B”
ISP “A”
ISP “B”
Backbone
V
ISP “A”
Backbone
POP (ii)
V
QoS
Interconnect
(or Internet)
V
Local
PSTN
Local
PSTN
Local
PSTN

## Slide 53: Route Replacement
Branch Office
PSTN
Main Office
T1,E1
QoS
WAN
(Intranet/Internet)
V
V
Telco
Switch
PBX
PBX
Benefit is to reduce monthly changes
Notes: Works with exsisting telephony architecture
Passes office to office telephone and fax calls across data network significantly reducing toll’s.

## Slide 54: PBX Off Premise EXchange
PSTN
Branch Office
Main Office
4 to 12 Analog
Voice Enabled
Router
QoS
WAN
(Intranet/Internet)
V
V
Telco
Switch
PBX

## Slide 55: H.323 Infrastructure
Intranet
Real-Time Network
Telephone Network
Gatekeeper
H.323 Terminal
Router
Proxy
Gateway
H.320 (Over ISDN)
H.324 (Over POTs)
Speech Only
(PSTN)
Corp LAN
H.323 VoIP Local Loop Bypass
Integrated Messaging: Email, VMail, FaxMail
Interoperability with NetMeeting type programs
H.323

## Slide 56: PBX to Router VoIP Signaling
Corporate Intranet
Switch
Analog Signaling
FXO/FXS
5278305
H.323 Gateway
H.225 (Q.931)
Digital Trunk Signaling
CAS:
E&M
CCS:
Q.931/PRI
5278305
1
2
3
V

## Slide 57: RTP/RTCP: RFC’s 1889/1890
End-to-end network transport function
  Payload type identification
  Sequence numbering
  Timestamping
  Delivery monitoring
RTCP (Real-Time Control Protocol) provides feedback on the quality of the distribution
RTP does not address: Resource reservation or guaranteed quality of service
Notes: RTP Services
  Payload Type ID
  Sequence Numbering
  Timestamp
  Delivery Monitoring
  Synch. Source ID (end point ID not dependent on Net ID.)
RTCP
  Quality Monitoring
Header Compression is used to keep payload to header ratio high for efficiency
  20ms @ 8kbs = 20byte payload
  RTP + UDP + IP = 12 + 8 + 20 (bytes) = 40byte Header 2x Payload!
Fragmentation and Interleave of large packets reduces residency on slow links
  1500 Byte MTU Takes 215Ms to Transmit on 56Kb Link
  MLPPP on single interface at frag level
  IETF Draft memo - draft-ietf-issll-isslow-mcml-01.txt

## Slide 58: L3/L2 Transport Characteristics
L3—VoIP
  Flexible—IP is ubiquitous
  “Soft” form of QoS
  IP/UDP/RTP overhead (RTP compression)
  Quickly emerging technology
  Standards-based H.323
L2—VoFR, VoATM
  “Hard” QoS
  Infrastructure can be rigid
  Standards-based
  Better suited for high volume bulk voice

## Slide 59: Bandwidth Requirements
Voice Band Traffic
Encoding/
Compression
Result
Bit Rate
G.711 PCM
A-Law/u-Law
64 kbps (DS0)
G.726 ADPCM
16, 24, 32, 40 kbps
G.727 E-ADPCM
G.729 CS-ACELP
8 kbps
G.728 LD-CELP
16 kbps
G.723.1 CELP
6.3/5.3 kbps
Variable
16, 24, 32, 40 kbps
Notes: Dick Tracy Decoder Ring so you look smart:
PCM = Pulse Code Modulation
ADPCM = Adaptive Delta PCM
CS-ACELP = Conjugate-Structure Linear-Predictive Coding
LD-CELP = Low Delay CELP
CELP = Code Excited Linear Prediction
ACELP = Algebraic CELP

## Slide 60: Voice Transport Requirements
Subjective quality
  MOS
Delay and delay variation
Echo cancellation
Background noise
Silence suppression
  Comfort noise
Language sensitivity
Loss
Bandwidth
Delay
Delay Variation (Jitter)
VoIP Challenges in the WAN
(Amplified with Coexistence of Voice and Data)

## Slide 61: Delay Budget: Network Elements
Input queuing
Jitter buffer
CODEC
Access (up) link transmission
Backbone network transmission
Access (down) link transmission
CODEC
Packetization
Output queuing

## Slide 62: Fixed Delay Components
Propagation—six microseconds per kilometer
Serialization
Processing
  Coding/compression/decompression/decoding
  Packetization
Processing Delay
Propagation Delay
Serialization Delay— Buffer to Serial Link

## Slide 63: Variable Delay Components
Queuing delay
Dejitter buffers
Variable packet sizes
Dejitter Buffer
Queuing Delay
Queuing Delay
Queuing Delay

## Slide 64: Identifying VoIP Delay Budget
Coder Delay 25 ms
Queuing Delay 6 ms
Serialization Delay 3 ms
Dejitter Buffer
50 ms
Los
Angeles
Munich
Propagation
Delay—32 ms
(Private Line Network)
Total
110 msec
Dejitter Buffer
50 msec
32 msec
Network Delay (e.g.,Public Frame Relay Svc)
Serialization Delay 64 kbps Trunk
3 msec
6 msec
Queuing Delay 64 kbps Trunk
5 msec
Packetization Delay—Included in Coder Delay
Coder Delay G.729 (5 msec look ahead)
Propagation Delay (Private Lines)
Fixed Delay
Variable Delay
Coder Delay G.729 (10 msec per frame)
20 msec

## Slide 65: Voice Delay: How Much Is Allowed?
Cumulative Transmission Path Delay
Time (msec)
0
100
200
300
400
CB Zone
Satellite Quality
Fax Relay, Broadcast
High Quality
Delay Target
500
600
700
800
ITU’s G.114 Recommendation = 0 – 150msec 1-way delay

## Slide 66: Enterprise Network Infrastructure
Core Layer
(Higher Bandwidth
and Lower Delay)
Distribution Layer
Access Layer
(Lower Bandwidth and
Higher Delay)
Access Layer:
Area of Most Challenge
for VoIP Networking
Loss (Bandwidth/Congestion)
Delay (Serialization/Propagation)
Jitter (Varying Packet Sizes)
Access Layer/Small-Mid
Tier Size Network
Frame Relay
ATM, SMDS, VSAT
Pt-to-Pt
Frame Relay
ATM, SMDS, VSAT
Pt-to-Pt
Frame Relay
ATM, SMDS, VSAT
Pt-to-Pt
Frame Relay
ATM, SMDS, VSAT
Pt-to-Pt

## Slide 67: Access Layer Issues
Equally as Important
in the Design Process!
But Not Discussed Here
Router Egress
Dropped Packets—Serial Interface Congestion
Serialization Delay—Voice Packet Behind “Jumbogram”
Varying Packet Sizes—Coexistence of Voice + Data
Small PBX,
Keyset
or POTS
Unless Pt-to-Pt:
Dropped Packets—CIR Rates, ATM QoS
Delay—NBMA Delays, VSAT Delays
Jitter—Shared Transport with Other Customers
WAN Transport QoS
Causes of packet loss, packet delay and packet jitter
Note: These issues exist in the
Core layer but are dampened
with higher bandwidth
Frame Relay
ATM, SMDS, VSAT Pt-to-Pt
PBX

## Slide 68: IP Precedence
Set IP Precedence higher on VoIP
  Result = Isolated WFQ queue from Best Effort traffic
  Set at: Endpoint, proxy, or statically through router
May scale better than RSVP in SOME networks
  Bulk QoS by customer or network
Warning: No admission control

## Slide 69: Resource reSerVation Protocol
IETF signaling protocol
  Reservation of bandwidth and delay
Dynamic end-to-end “access lists”
  Programs queuing policy
Flow can be signaled by end station or by router (static reservation)
QoS services
  Guaranteed - queueing delay and bandwidth
  Controlled loss - no loss for specific bit rate

## Slide 70: Uses of IP Precedence or RSVP
IP Precedence
  Network telephony
  Audio/whiteboard conferencing
RSVP
  Videoconferencing
Either
  Interactive applications
  Transaction applications
  SNA in TCP/IP
Notes: Note: L3 Qos only assures Qos OUT the interface
Once in “WAN cloud” must rely on L2 Qos

## Slide 71: Traffic Engineering Fundamentals
Grade of service
  % of calls blocked
Traffic load
  quantity of traffic during BH
Quantity of circuits
  Traffic tables