## Slide 1
VoIP Networking
Notes: 3
3

## Slide 2
Agenda
Possible VoIP Applications
VoIP Introduction
Packet Networking Challenges

## Slide 3
PSTN gateway service
Route replacement/toll bypass
  Most common application
PBX OPX “extension”
H.323 interoperability
  Supports voice-enabled Web applications
VoIP Gateway Applications

## Slide 4
Internet Telephony Service Provider
POP (i)
Authentication, Call Routing, Billing and Settlement Server
Settlement Provider
(Trusted 3rd Party)
ISP “B”
ISP “A”
ISP “B”
Backbone
V
ISP “A”
Backbone
POP (ii)
V
QoS
Interconnect
(or Internet)
V
Local
PSTN
Local
PSTN
Local
PSTN

## Slide 5
Branch Office
PSTN
Main Office
T1,E1
Route Replacement
QoS
WAN
(Intranet/Internet)
V
V
Telco
Switch
PBX
PBX
Notes: Works with exsisting telephony architecture
Passes office to office telephone and fax calls across data network significantly reducing toll’s.

## Slide 6
Route Replacement
Usage/Billing Cycle (Hours/Month)
Billing Cycle Cost ($)
5
10
15
20
25
30
35
Tie Trunk
DDD
“A” Plan
IP Bandwidth

## Slide 7
PSTN
Branch Office
Main Office
4 to 12 Analog
PBX OPX Transport
Voice Enabled
Router
QoS
WAN
(Intranet/Internet)
V
V
Telco
Switch
PBX

## Slide 8
POP
I-Phone
H.323 S/W
PBX
Router
+ VoIP
Business
I-Phone
H.323 S/W
I-Phone
H.323 S/W
xDSL
Modem
2nd Line
Phone
Residential
Residential
DSLAM
H.323 Interoperability
Main Office
H.323 VoIP Local Loop Bypass
Integrated Messaging: Email, VMail, FaxMail
Interoperability with NetMeeting type programs
QoS
WAN
PSTN
xDSL
Local
PSTN
Internet
V
V
PBX

## Slide 9
Network Convergence
Service
Adaptation
L1
L2
F-T1
DS1 DS3
Sonet
OC3 - OCn
Campus
802.N
Frame
Relay
ATM
L3
IP
Applications
PPP
WAN
IP

## Slide 10
L3/L2 Transport Characteristics
L3—VoIP
  Flexible—IP is ubiquitous
  “Soft” form of QoS
  IP/UDP/RTP overhead (RTP compression)
  Quickly emerging technology
  Standards-based H.323
L2—VoFR, VoATM
  “Hard” QoS
  Infrastructure can be rigid
  Standards-based
  Better suited for high volume bulk voice

## Slide 11
Presentation
Session
Transport
Network
Link
Physical
G.729(A)/G.723(.1)/G.711
H.323/H.323Gateway
RTP/UDP/RSVP
IP/WFQ/IP-prec
MLPPP/FR/ATM AAL1
– – –
Voice over IP Protocols

## Slide 12
H.323 Infrastructure
Intranet
Real-Time Network
Telephone Network
Gatekeeper
H.323 Terminal
Router
Proxy
Gateway
H.320 (Over ISDN)
H.324 (Over POTs)
Speech Only
(PSTN)
H.323
Corp LAN
Internet Phone/I-Fax (VOIP)
Data Conferencing (T.120)
Video Conferencing
Typical H.323 Applications

## Slide 13
PBX to Router VoIP Signaling
Corporate Intranet
Switch
Analog Signaling
FXO/FXS
5278305
H.323 Gateway
H.225 (Q.931)
Digital Trunk Signaling
CAS:
E&M
CCS:
Q.931/PRI
5278305
1
2
3
V

## Slide 14
RTP/RTCP—RFCs 1889/1890
End-to-end network transport function
  Payload type identification
  Sequence numbering
  Timestamping
  Delivery monitoring
RTCP (Real-Time Control Protocol) provides feedback on the quality of the distribution
RTP does not address: Resource reservation or guaranteed quality of service
Notes: RTP Services
  Payload Type ID
  Sequence Numbering
  Timestamp
  Delivery Monitoring
  Synch. Source ID (end point ID not dependent on Net ID.)
RTCP
  Quality Monitoring
Header Compression is used to keep payload to header ratio high for efficiency
  20ms @ 8kbs = 20byte payload
  RTP + UDP + IP = 12 + 8 + 20 (bytes) = 40byte Header 2x Payload!
Fragmentation and Interleave of large packets reduces residency on slow links
  1500 Byte MTU Takes 215Ms to Transmit on 56Kb Link
  MLPPP on single interface at frag level
  IETF Draft memo - draft-ietf-issll-isslow-mcml-01.txt

## Slide 15
Bandwidth Requirements
Voice Band Traffic
Encoding/
Compression
Result
Bit Rate
G.711 PCM
A-Law/u-Law
64 kbps (DS0)
G.726 ADPCM
16, 24, 32, 40 kbps
G.727 E-ADPCM
G.729 CS-ACELP
8 kbps
G.728 LD-CELP
16 kbps
G.723.1 CELP
6.3/5.3 kbps
Variable
16, 24, 32, 40 kbps
Notes: Dick Tracy Decoder Ring so you look smart:
PCM = Pulse Code Modulation
ADPCM = Adaptive Delta PCM
CS-ACELP = Conjugate-Structure Linear-Predictive Coding
LD-CELP = Low Delay CELP
CELP = Code Excited Linear Prediction
ACELP = Algebraic CELP

## Slide 16
Voice Transport Requirements
Subjective quality
  MOS
Delay and delay variation
Echo cancellation
Background noise
Silence suppression
  Comfort noise
Language sensitivity
Loss
Bandwidth
Delay
Delay Variation (Jitter)
VoIP Challenges in the WAN
(Amplified with Coexistence of Voice and Data)

## Slide 17
Delay Budgeting— Networked End Points
Input queuing
Jitter buffer
CODEC
Access (up) link transmission
Backbone network transmission
Access (down) link transmission
CODEC
Packetization
Output queuing

## Slide 18
Delay—How Much Is Too Much?
Cumulative Transmission Path Delay
Time (msec)
0
100
200
300
400
CB Zone
Satellite Quality
Fax Relay, Broadcast
High Quality
Delay Target
500
600
700
800
ITU’s G.114 Recommendation = 0 – 150msec 1-way delay

## Slide 19
Fixed Delay Components
Propagation—six microseconds per kilometer
Serialization
Processing
  Coding/compression/decompression/decoding
  Packetization
Processing Delay
Propagation Delay
Serialization Delay— Buffer to Serial Link

## Slide 20
Variable Delay Components
Queuing delay
Dejitter buffers
Variable packet sizes
Dejitter Buffer
Queuing Delay
Queuing Delay
Queuing Delay

## Slide 21
64kb WAN
Large Packets “Freeze Out” Voice
Large packets can cause playback buffer underrun, resulting in slight voice degradation
Jitter or playback buffer can accommodate some delay/delay variation
~214ms Serialization Delay
10mbps Ethernet
10mbps Ethernet
Voice Packet
60 bytes
Every 20ms
Voice
1500 bytes of Data
Voice
Voice Packet
60 bytes
Every >214ms
Voice Packet
60 bytes
Every >214ms
Voice
1500 bytes of Data
Voice
Voice
1500 bytes of Data
Voice

## Slide 22
Calculate Delay Budget
Coder Delay 25 ms
Queuing Delay 6 ms
Serialization Delay 3 ms
Dejitter Buffer
50 ms
Los
Angeles
Munich
Propagation
Delay—32 ms
(Private Line Network)
Total
110 msec
Dejitter Buffer
50 msec
32 msec
Network Delay (e.g.,Public Frame Relay Svc)
Serialization Delay 64 kbps Trunk
3 msec
6 msec
Queuing Delay 64 kbps Trunk
5 msec
Packetization Delay—Included in Coder Delay
Coder Delay G.729 (5 msec look ahead)
Propagation Delay (Private Lines)
Fixed Delay
Variable Delay
Coder Delay G.729 (10 msec per frame)
20 msec

## Slide 23
Typical Enterprise Network Infrastructure
Core Layer
(Higher Bandwidth
and Lower Delay)
Distribution Layer
Access Layer
(Lower Bandwidth and
Higher Delay)
Access Layer:
Area of Most Challenge
for VoIP Networking
Loss (Bandwidth/Congestion)
Delay (Serialization/Propagation)
Jitter (Varying Packet Sizes)
Access Layer/Small-Mid
Tier Size Network
Frame Relay
ATM, SMDS, VSAT
Pt-to-Pt
Frame Relay
ATM, SMDS, VSAT
Pt-to-Pt
Frame Relay
ATM, SMDS, VSAT
Pt-to-Pt
Frame Relay
ATM, SMDS, VSAT
Pt-to-Pt

## Slide 24
Access Layer Issues
Equally as Important
in the Design Process!
But Not Discussed Here
Cisco’s QoS Toolkit can help here!
Router Egress
Dropped Packets—Serial Interface Congestion
Serialization Delay—Voice Packet Behind “Jumbogram”
Varying Packet Sizes—Coexistence of Voice + Data
Small PBX,
Keyset
or POTS
Unless Pt-to-Pt:
Dropped Packets—CIR Rates, ATM QoS
Delay—NBMA Delays, VSAT Delays
Jitter—Shared Transport with Other Customers
WAN Transport QoS
Loss, Delay and Jitter
Note: These issues exist in the
Core layer but are dampened
with higher bandwidth
Frame Relay
ATM, SMDS, VSAT Pt-to-Pt
PBX

## Slide 25
IP Precedence
Set IP Precedence higher on VoIP
  Result = Isolated WFQ queue from Best Effort traffic
  Set at: Endpoint, proxy, or statically through router
May scale better than RSVP in SOME networks
  Bulk QoS by customer or network
Warning: No admission control

## Slide 26
RSVP - Resource reSerVation Protocol
IETF signaling protocol
  Reservation of bandwidth and delay
Dynamic end-to-end “access lists”
  Programs queuing policy
Flow can be signaled by end station or by router (static reservation)
QoS services
  Guaranteed - queueing delay and bandwidth
  Controlled loss - no loss for specific bit rate

## Slide 27
Other Techniques
Weighted Random Early Detection (W-RED)
  Congestion avoidance
Multilink PPP with fragmentation and interleave
  Prevent voice packet starvation
RTP header compression
  Reduce IP header from 40 bytes to 4 bytes

## Slide 28
Suggestions for Use?
IP precedence
  Network telephony
  Audio/whiteboard conferencing
RSVP
  Videoconferencing
Either
  Interactive applications
  Transaction applications
  SNA in TCP/IP
Notes: Note: L3 Qos only assures Qos OUT the interface
Once in “WAN cloud” must rely on L2 Qos