## Slide 1: Chapter 12
Wide-Area Networks
“Keeping Up With Technology”

## Slide 2: Frame Relay
Next Generation Packet Switching
Streamlined Protocols
High Bandwidth
Minimal Error Checking

## Slide 3: Why Frame Relay?
X.25 Approach to Packet Switching
  Call setup carried on same virtual circuit as data
  Layer 3 provides logical channel multiplexing
  Layer 2 and 3 provide flow and error control
  Designed for low data rates (64 Kbps or less)
Frame Relay Approach to Packet Switching
  Call setup carried on separate logical connection from data
  Layer 2 provides multiplexing and switching
  Layer 2 does not provide flow and error control
  Streamlined version of X.25 for high data rates (> 2 Mbps)

## Slide 4: Frame Relay Concepts
Access Rate
Committed Information Rate
Data Link Connection Identifier
Explicit Congestion Notification
Discard Eligibility
Notes: In order to discuss frame relay, let’s get some concepts clearly understood. The physical speed of the connection between the user device and the network providing the frame relay service is known as the ‘Access Rate’. This is an upper limit on the performance of the virtual circuits. Let us assume that this router has an access rate of 512 Kbps.
There will probably be many virtual circuits supported by the physical interface. Each virtual circuit is supposed to be guaranteed to be able to transmit at a certain minimum level. This guaranteed amount is called the ‘Committed Information Rate’. Each of the 3 virtual circuits shown may have a different CIR. Obviously, the CIR cannot be greater than the Access Rate.
Since there are multiple virtual circuits on one interface, there has to be some way for the network and the user (router) to identify the proper one. This is the purpose of the DLCI (Data Link Connection Identifier). Every virtual circuit on a frame relay interface has a unique DLCI. The DLCI has local significance only. That DLCI can be reused at other ports. The same virtual circuit can have different DLCIs at each end; the network would translate the values.
If there is congestion within the network, the FECN and BECN (Forward and Backward Explicit

## Slide 5: Frame Relay
Differences from X.25
  No frame, flow or error control
  High access circuit bandwidth
    1.544 Mbps (T-1) is most common
    Fractional T-1 is available
    44.7 Mbps (T-3) is available
  Multiplex channel
    Data link connections
  Only uses PVC’s

## Slide 6: Frame Relay Features
Scalable speed
National and global implementation
Handles bursty traffic
Cost competitive
Frame Relay

## Slide 7: Frame Relay Costs
Access port cost
PVC cost
Committed information rate cost
CSU/DSU cost

## Slide 8: Frame Relay Issues
Broadcast packet replication
Congestion management
Network hops = network latency
Frame Relay

## Slide 9: Frame Relay Terminology
DLCI 21
DLCI 23
DLCI 22
DLCI 31
DLCI 32
DLCI 33
Frame Relay
Switch
SDLC
FRAD
Router
Router
Definitions
DLCI: Data Link Connection Identifier
CIR : Committed Information Rate
Bc : Committed burst in bits
Be : Excess Burst in bits
FECN: Forward Explicit Congestion Notify
BECN: Backward Explicit Congestion Notify
DE: Discard Eligible
Frame Relay Switch
Maps DLCIs to form a PVC
Controls each PVC’s CIR, Bc, Be
Congestion Notification: FECN, BECN
Provides Accounting and Monitoring

## Slide 10: Committed Information Rate
Guaranteed
Transmission
Transmit if
Possible
Discard all
Excess
Bc
Be
CIR : Committed Information Rate
Bc : Committed burst in bits
Be : Excess Burst in bits
CIR

## Slide 11: Frame Relay Connections
Local congestion possible
Use CIR to limit PVCs
Remote
128Kb
64Kb
64Kb
64Kb
Local
Remote
Remote
= VC
= Access Link
= Trunk Link

## Slide 12: Asynchronous Transfer Mode
Cell switching
No error or flow control
Connection oriented
Most common cell rate is 155 Mbps
SONET OC-3c transmission format

## Slide 13: ATM Interfaces
User Network Interface (UNI)
ATM router interfaces
ATM work stations
Private ATM Network
ATM
Switch
ATM
Router
UNI
UNI
PNNI
UNI
Public ATM Network
Public
NNI
Public UNI
ATM
Switch
Public UNI
ATM
Switch
ATM
Switch
Network to Network Interface (NNI)
ATM switch to switch interfaces

## Slide 14: ATM Description
Customer Premises
Central Office
Workgroup
Desktop
ATM
WAN Access
ATM
WAN Backbone
ATM
Enterprise
Building/Campus
Backbone
ATM is fast, flexible, but inefficient
ATM is being deployed by Service Providers
ATM is expensive, complete technology change

## Slide 15: ATM Connection

## Slide 16: VP and VC Characteristics
Quality of service
Switched and semipermenant connections
Cell sequencing integrity
Traffic parameter negotiation
Usage monitoring

## Slide 17: ATM Virtual Path
Bundle of virtual channels
Simplifies service provider architecture
  Increased performance and reliability
  Reduced processing and connection time
  Enhanced services

## Slide 18: ATM Virtual Channel
User to user connection
Variable bit rate
Fixed cell size
Full duplex
Supports all signaling protocols
  User to network signaling
  Network to network signaling
    Network management
    Routing

## Slide 19: PVC vs. SVC
Permanent Virtual Circuit (PVC)
  Connectivity is statically configured in the switches and end stations.
  Similar to leased line.
Switched Virtual Circuit (SVC)
  Created dynamically for each transmission.
  Similar to a dial-up telephone call.
Notes: Permanent Virtual Circuits are permanent connections between two network nodes and operate like a dedicated physical line. In a PVC implementation, network connectivity between two nodes is statically configured in the switch(es), and the PVC Virtual Circuit Identifier (VCI) for each remote node is configured on each endstation.
Switched Virtual Circuits (SVCs) are created dynamically for each transmission. Switched Virtual Circuits are similar to a voice telephone network, where connections between any two endpoints on the network are created dynamically for each transmission. SVCs attempt to determine the shortest available route from source to destination.

## Slide 20: Permanent Virtual Connections
Long setup time
Connections are left active for long periods of time
VPI/VCI tables setup in terminals and switches
Network
Management System
Switch
Switch
VPI/VCI
VPI/VCI
VPI/VCI
VPI/VCI

## Slide 21: Switched Virtual Connections
Switch and terminal exchange signaling messages using the signaling channel, VPI/VCI = 0/5.
VPI/VCI = 0/16, Interim Local Management Interface
VPI/VCIs 0/0-31 are reserved
Switch
Signaling Channel:
VPI/VCI = 0/5
Signaling Channel:
VPI/VCI = 0/5

## Slide 22: UNI and NNI Signaling
UNI Signaling
  UNI 3.0 and 3.1 are not interoperable but provide similar functionality
    UNI 3.0 is aligned with ATM Forum
    UNI 3.1 is aligned with ITU-T standard
  UNI 4.0 is backward compatible with UNI 3.1
NNI Signaling
  IISP uses static ATM routing
  PNNI provides dynamic ATM routing

## Slide 23: UNI and NNI
User-to-Network Interface (UNI)
Network-to-Network Interface (NNI)
Interim Interswitch Protocol (IISP)
Switch
Switch
NNI / IISP
UNI
UNI
UNI

## Slide 24: Local Management
ILMI is ATM Forum standard for network management
  Monitors transfers between switch and nodes
  Reports CRC error rates
  Tracks performance dips
  Provides address registration
    Used during station attachment to the ATM network
    Used during LANE initialization

## Slide 25: How ATM Works
All data is converted into 53 byte cells prior to transmission
  Cells streams can be multiplexed together
Switching is simplified because only cells are supported
  Hardware switching permits lower processing overhead
ATM benefits from both circuit and packet switching technologies

## Slide 26: ATM and the OSI RM
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
ATM Adaptation Layer
(AAL)
(Convergence SubLayer)
(Segmentation and Reassembly)
ATM Layer
(VPI & VCI Translation)
(Cell Header Generate/Extract)
Physical Layer
(Transmission Convergence)
(Physical Medium)

## Slide 27: ATM Addressing
Byte 1 - Authority & Format Identifier
  Identifies address format
Bytes 2-13 - Network Prefix
  3 Formats - (DCC, ICD, E.164)
Bytes 14-19 - End Station Identifier
  Equivalent to MAC address
Byte 20 - Selector
  Not used by network
Network Prefix
ESI
Sel
AFI

## Slide 28: ATM Cell Characteristics
53 byte cell
  5 byte header
  48 byte payload
Header types
  User to network (UNI)
  Network to network (NNI)

## Slide 29: ATM Cell Structure
BYTE
8 7 6 5
4 3 2 1
BIT
1
2
3
4
5
6
...
53
Generic Flow Control
Virtual Path Identifier
Virtual Path Identifier
Virtual Channel Identifier
Virtual Channel Identifier
Virtual Channel Identifier
Payload Type
CLP
Header Error Control
Cell Payload
48 bytes
NNI - Generic Flow Control not used, field extends
size of Virtual Path Identifier to 12 bits.
Notes: This is a picture of an AAL 5 cell. The 5-byte header is used for connection identification, flow control, routing, and error control. The cell payload is 48 bytes.

## Slide 30: ATM Adaptation Layer
Adapts protocol frames to ATM cells
  PCM, LAPF, HDLC are examples
Provides segmentation & reassembly
Manages transmission errors
Managers lost and misinserted cells
Supports flow control
Supports timing control

## Slide 31: ATM Adaptation Layer
AAL provides 4 packet-to-cell conversions
  Different data types require different conversions
AAL performs Segmentation & Reassembly
  Provided by adapter hardware
AAL maintains cell sequencing
Only 2 types are widely supported
  AAL 1 and AAL 5

## Slide 32: ATM Adaptation Layer
AAL 1 - Supports Constant Bit Rate (isochronous) traffic for voice or video traffic
AAL 2 - Supports Variable Bit Rate data traffic that requires end-to-end timing
AAL 3/4 - Supports connection or connectless Variable Bit Rate data traffic generated at irregular intervals as short highly bursty sequences
AAL 5 - Most efficient way to support data traffic

## Slide 33: ATM Quality of Service Classes
Constant Bit Rate - guaranteed bandwidth for connection duration
Variable Bit Rate - guaranteed bandwidth for connection duration with a peak maximum burst size
Available Bit Rate - uses all bandwidth that is available at any instant
Unspecified Bit Rate - best effort delivery with no guarantee

## Slide 34: ATM Network Environments
Service Provider
Enterprise WAN
Campus
PNNI
Public UNI
Public UNI
PNNI
Notes: There are emerging several distinct segments to the ATM market. Each has its own requirements
ATM LAN and Campus. This market is LANE, SVC and cost per port focussed.
Broadband Enterprise: This market requires voice/data/video/LAN integration. Bandwidth efficiency is not critical. Data performance nad hence buffering are very important.
Narrowband Enterprise: This market is concerned about TDM replacement is is focussed on WAN costs and hence voice compression and switching.
Carrier/Service Provider. This market is focused on large scale service provision, reliability and on traffic management to ensure QoS for end users..

## Slide 35: What Users Really Want
Reduce WAN bandwidth cost
Improve performance
Improve uptime
Is your company Interested in deploying an ATM WAN?
No 22%
Don’t Know 4%
Yes 74%
Source: “ATM in the Long Haul” Forrester Research, 1995
50 Fortune 1,000 companies interviewed

## Slide 36: Reduce WAN Bandwidth Cost
Voice compression
Silence suppression
Repetitive pattern suppression
Dynamic bandwidth allocation

## Slide 37: Improve Uptime
High availability and reliability - 99.99%
Highly redundant systems
  Processors
  Port and trunk interfaces
  Power supplies
Rapid reroute around failed trunks

## Slide 38: Improved Performance
Typical benefits obtained
  30% bandwidth savings
  50% performance improvement
  50–70% reduction in management costs
  Reduced downtime

## Slide 39: ATM Service Costs
Service installation costs
  One time
Facility access and network port costs
  Monthly recurring
  Depends on type of access and port
    ATM T1, ATM T3, OC-3, OC-12 are examples