## Slide 1: Chapter 20
Access Network Design
Access
Access
Access
Backbone

## Slide 2: Hierarchical Design
Hierarchical design
  User layer
  Access layer
  Backbone layer
Cisco design
  Access layer
  Distribution layer
  Core layer

## Slide 3: The Three Network Layers
Access Layer
Backbone
Layer
User (Application) Layer
Ethernet
AT&T

Servers
Work Stations

## Slide 4: Hierarchical Network Example
DEVICE ISSUES:
Queueing Delay
Routing Delay
FACILITY ISSUES:
Serial Line Overhead
Propagation Delay
Error Rates
Line Turnaround
OPERATIONAL ISSUES
Nodal Delay
Switching
Routing
Call Setup Delay
Multiprotocol
Router
AT&T

AT&T

Customer Premise
Access
Network
Backbone Network
(Common Carrier)

## Slide 5: User Layer
Physical interfaces
  Workstations and Servers
    Serial adapters
    Ethernet adapters
    Token ring adapters
  Front End Processors
Few if any network services

## Slide 6: User Layer
Diversity of
  Interfaces
  Protocols
  Architectures
  Technologies
  Network layer standards
Design based on protocols
  That access data
  That transport data across network
  Are session-oriented

## Slide 7: User Access Wiring
RJ-45
Wall
66
Block
Patch
Panel
HUB
WAN
Wiring Closet

## Slide 8: Access Requirements
What are the access requirements?
  Based on traffic analysis
  Based on capacity plan
  Based on coalescing user requirements onto common platform that defines
    Interfaces and protocols
    Architecture and technology
    Features, functions, and services

## Slide 9: Access Network Topologies
Direct connect to backbone nodes without direct trunking between access nodes
Direct connect to backbone nodes with direct trunking between access nodes
Ring connected to backbone node

## Slide 10: Access Network Topologies
Trees with root connected to backbone node
Multipoint with bus connected to backbone node
Star with hub connected to backbone node
  Hybrid meshed configuration

## Slide 11: Access Network
May include data transport to backbone
Define capacity of total access network
Define capacity of each access device
Network topology accommodates
  Applications
  Devices
  Circuits
  Interfaces

## Slide 12: Access Network
Access design focus
  Physical layer
  Data link layer
  Network layer
  Transport layer (some functions)
Applications support functions from
  Session layer
  Presentation layer
  Application services layer

## Slide 13: Access Layer
Defines entry points into network
Typical devices
  Routers
  Switches
  PBXs
Focal point for standardization

## Slide 14: Access Layer
Standardization
  Architectures
    TCP/IP
  Technologies
    Circuit switching
    Packet switching
    Cell switching
  Protocols
    Physical
    Data link
    Network
Standardization
  Interfaces
    Serial lines
    Ethernet
    Token ring
  Services
    Switched data services
    Wide area networks
  Features/Functions
    DTE terminate data
    DCE pass through/modify data

## Slide 15: Physical Connectivity
Dictated by network service
Point-to-point circuits
Type of media
  Twisted pair (shielded/unshielded)
  Coaxial cable (thick/thin)
  Fiber optic cable (multimode/single mode)

## Slide 16: Physical Interfaces
EIA 232
  25 pin cable, line speeds < 20 Kbps
EIA 449
  37 pin cable, line speeds < 10 Mbps
V.35
  34 pin cable, line speeds < 2 Mbps
Commonly used connectors
  DB-25, DB-37, M-34, RJ-45, RJ-11

## Slide 17: Protocols Characteristics
Which protocols are supported?
  Characteristics
    Syntax
    Semantics
    Implementation
    Idiosyncrasies
Which interfaces are being used?
How are protocols being supported?
  Routed
  Switched
  Bridged
  Encapsulated
  Tunneled
  Translated
  Passed transparently
  Converted by network

## Slide 18: Access Port Utilization
Backbone
Network
Access
Network
User Data: 950 GB/day
User Ports: 2000
Daily Average
Utilization/Port = 2.85%
Peak Hour
Utilization/Port = 13.7%

## Slide 19: Access Node Design
Access Ports
pi = port of type i
si = speed of pi
ui = % utilization of pi
Output Trunks, T
Output Trunks
Tj = trunk of type j
Sj = speed of Tj
Uj = % utilization of Tj
General Relationship:
Access Ports, p

## Slide 20: Access Node Trunk Failure Utilization Design
Output Trunks, TN
Output Trunks
Lf = loading factor per trunk
TjN = number of trunks of speed j
= maximum % loading of Tj
General Relationship:
Access Ports

## Slide 21: Hierarchical vs. Ubiquitous Design
Provides cost-efficient use of network media
Keeps performance from degrading
Protects from broadcast storms
Allows for hierarchical address schemes
Uses access control filters in routers
Eases security administration
Eases isolation and diagnosis of problems

## Slide 22: Ubiquitous Access using Hubs, Bridges or Switches
Creates a flat network => 1 Broadcast domain, multiple collision domains

## Slide 23: Hierarchical Access using Routers
Creates multiple subnetworks => Multiple broadcast and collision domains

## Slide 24: Access Circuit Design
Shortest path
Minimum cost
Minimum congestion
Minimum delay
Minimum loss
Maximum throughput
Best utilization
Minimum hop count