## Slide 1
Internetworking Hardware
“Choosing the Right Stuff”

## Slide 2
OSI Reference Model
Provides a layered architecure
Defines a hierarchical structure
Contains sets of well defined functions
Creates a framework
  Independent development
  Simultaneous development

## Slide 3
OSI Architecture
Application
Presentation
Session
Transport
Network
Data Link
Physical
User of Network
Service
Provider of
Network Service
Network Interface
Defines services, functions, and protocols
Notes: EACH LAYER OF THE ARCHITECTURE CONTAINS SPECIFIC FUNCTIONS, PROVIDES SPECIFIC SERVICES, COMMUNICATES USING PRIMITIVES AND PARAMENTERS TO ITS ADJACENT NEIGHBORS, AND ESTABLISHES PEER RELATIONSHIPS WITH REMOTE PARTNERS.
APPLICATION: SUPPORTS THE USER ENVIRONMENT, FTP, NETWORK MANAGEMENT, TRANSACTION SERVER.
PRESENTATION: SUPPORTS DATA TRANSFORMATIONS, ENCRYPTION, TEXT COMPRESSION, FORMATING.
SESSION: ESTABLISHED, MANAGES, AND TERMINATES CONNECTIONS BETWEEN CO-OPERATING END USERS.
TRANSPORT: PROVIDES END-TO-END FLOW CONTROL, ERROR RECOVERY, TRANSPARENT DATA TRANSFER.
NETWORK: PROVIDES UPPER LAYERS INDEPENDENCE FROM DATA TRANSMISSION, SWITCHING TECHNOLOGIES. ESTABLISHES, MAINTAINS, AND TERMINATES CONNECTIONS.
DATA LINK: PROVIDES RELIABLE TRANSFER OF DATA ACROSS PHYSICAL LINKS. MANAGES FLOW AND ERROR CONTROL.
PHYSICAL: PROVIDES TRANSMISSION OF BIT STREAMS, DEALS WITH ELECTRICAL, MECHANICAL, AND PROCEDUREAL CHARACTERISTICS.

## Slide 4
OSI Layer Services
Application
  Provides services to users of OSI environment
Presentation
  Provides transformations for data
Session
  Provides control structure for communications
Transport
  Provides reliable end-to-end data transfer

## Slide 5
OSI Layer Services
Network
  Provides independence from transmission and switching technologies
Data link
  Provides reliable data transfer across a physical link
Physical
  Provides for the transmission of unstructured bit streams over physical links

## Slide 6
Internetworking Terms
Internet
  Connecting networks together
Intranet
  Connecting sub-network together
Sub-networks
  Connected internetworking devices
Internetworking devices
  Repeaters, Hubs, Bridges, Routers, Switches, and Gateways

## Slide 7
Internetwork Solutions
Which ONE should I choose?

## Slide 8
Possible Network Problems
LAN Segment Congestion
Protocol Congestion
Backbone Congestion
Too many devices on LAN segment
Backbone capacity is not enough
Too many broadcasts
Different Types of Congestion

## Slide 9
Single Technologies Provide a Partial Solution
Routing solution
  Solves the broadcast and protocol problems
  A router for every port is too expensive
LAN switching solution
  Solves collision/media problems
  Does not scale well
ATM LANE switching solution
  Solves the capacity/transport problem
  Is not cost-effective
Routing
ATM Switching
LAN Switching

## Slide 10
Multiple Technologies Provide a Complete Solution
Routing
LAN Switching
ATM Switching
“Instead of choosing between switching
and routing, users must learn how to
effectively combine ... these technologies
in the same network to derive the maximum
benefits in throughput and performance.”
M. LeBaron, Gartner Group, 2/95

## Slide 11
Internetworking Technologies
What does each ONE provide?
FDDI
Token
Ring
Ethernet
ATM

## Slide 12
Ethernet
Shared or dedicated bandwidth environment
10/100/1000 Mbps link speed
Uses multiple media types
  UTP5 - 10/100/1000 Mbps only
  Single or multi-mode fiber
  Thick/thin coax
Switch

## Slide 13
Ethernet
Probabilistic message delivery
  half duplex - shared
  full duplex - switched
IEEE 802.3, IEEE 802.3i, IEEE 802.3u, IEEE 802.3z and IEEE 802.3ab standards
CSMA/CD media access
Switch

## Slide 14
Token Ring
Shared or dedicated bandwidth environment
Supports multiple media types
  Shielded/unshielded twisted pair
  Single/multi-mode fiber
Supported link speeds
  4/16 Mbps - half duplex
  32 Mbps - full duplex
TR Switch

## Slide 15
Token Ring
Token passing media access
Deterministic message delivery
  half duplex - shared
  full duplex - switched
IEEE 802.5, IEEE 802.5r, IBM standards
TR Switch

## Slide 16
Fiber Distributed Data Interface
Shared bandwidth environment
Supports single/multi-mode fiber
100 Mbps link speed
Dual counter-rotating rings
  Fault tolerant
  Self healing

## Slide 17
Fiber Distributed Data Interface
Station attachment method
  Dual or single attach
Uses token passing media access
Deterministic half duplex message delivery
ANSI X3T9.5 standard

## Slide 18
ATM - Asynchronous Transfer Mode
A switched, connection oriented virtual circuit network technology
  Uses 53 byte cell switching
  Provides virtual connections to support
    PVC - statically configured for contracted period
    SVC - dynamically configured for period of call duration
Supports voice, video, image, and data transport over the same network with highly efficient bandwidth utilization

## Slide 19
ATM - Asynchronous Transfer Mode
Supports class of service and quality of service
Supports multiple link speeds
  25Mbps, 155Mbps (OC-3), 622Mbps (OC-12), 1.2Gbps (OC-48), …
Provides a common technology for implementing both local and wide area networks

## Slide 20
ATM Virtual Connections
ATM virtual path
  Contains a group of virtual channels
  Provides a simplified switching architecture
  Increases performance and reliability
  Reduces processing and connection time
  Enhances provider services

## Slide 21
ATM Virtual Connections
ATM virtual channel
  Provides full duplex user to user connections
  Supports user to network signaling
    Between user devices and ATM switches
  Supports network to network signaling
    Between ATM switches
  Supports variable traffic rates

## Slide 22
ATM Adaptation Layer
Adapts packet protocols for ATM cell transport
  Provides packet-to-cell conversions required by different traffic types
    AAL 1 - Supports CBR (isochronous) traffic used for voice or video
    AAL 2 - Supports rt-VBR traffic that requires the transfer of timing between end points
    AAL 3/4 - Supports nrt-VBR traffic which provides short, highly bursty data at irregular intervals
    AAL 5 - Most efficient way to support both voice and data traffic

## Slide 23
ATM Adaptation Layer
AAL 1 and 5 are the most commonly used adaption layers
Provides frame segmentation and re-assembly
Manages frame transmission errors and cell sequencing
Supports flow and timing control

## Slide 24
ATM Classes of Service
Constant Bit Rate - guaranteed bandwidth for connection duration
Variable Bit Rate - guaranteed bandwidth for connection duration with a peak maximum burst size
Available Bit Rate - uses all bandwidth that is available at any instant
Unspecified Bit Rate - best effort delivery with no guarantee

## Slide 25
LANE - LAN Emulation
ATM Forum MAC layer specification that allows the ATM fabric to emulate a logical Ethernet or Token Ring segment.
Uses AAL 5 adaption to segment data frames into cells
Implements proxy client to forward unregistered MAC addresses for legacy LAN hosts
LANE emulates a bridged LAN segment

## Slide 26
LANE - LAN Emulation
LANE supported elements
  LECS - Maintains the configuration information for each emulated LAN.
  LES - Performs the MAC-to-ATM address resolution functions in an emulated LAN.
  BUS - Performs the multicast server function and broadcasts packets to multiple LECs.
  LEC - Performs client services
    Normally implemented on adapters, routers, and ATM-to-LAN edge devices.

## Slide 27
Internetworking Devices
Internetworking devices provide connections between network segments. Each type of device provides unique services for the interconnected segments.
Repeaters
and
Hubs
Bridges
Routers
Switches
Gateways
AT&T
✿

## Slide 28
Repeater and Hub
Connects segments to extend LAN length
Transmits all received bits with no buffering
Provides signal regeneration
Provides no address isolation
Multi-port repeater called a hub or concentrator
Operates at Physical layer
Extends a LAN without segment isolation
HUB
REPEATER

## Slide 29
Using a Repeater
REPEATER
All devices:
“see” all traffic
share the same bandwidth
1 broadcast domain
1 collision domain

## Slide 30
Using a Hub
All devices:
“see” all traffic
share the same bandwidth
1 broadcast domain
1 collision domain
HUB

## Slide 31
Bridge
Connects network segments that use the same LAN data link protocols
Provides address filtering
Learns device locations
Broadcasts unknown messages to all ports. May cause broadcast storms
Uses physical MAC addresses
May provide transparent, translated or encapsulated connections
Operates at Data Link layer
Extends a LAN with segment isolation

## Slide 32
Types of Bridging
Transparent
Translated
AT&T
✿
AT&T
✿
Encapsulated
Source Routed

## Slide 33
Using a Bridge
Devices on individual segment
see all traffic on segment
share segment bandwidth
1 broadcast domain
3 collision domains
Broadcast unknown addresses
Use data link addresses

## Slide 34
Router
Connects media independent networks
Provides traffic isolation
Establishes best path between source and destination networks
Provides switching function
Uses network addresses
Provides “unreliable” delivery
Supports multiple protocols
Operates at Network layer
Divides a large network into manageable segments

## Slide 35
FDDI Dual Ring
Router Interfaces
Provider
Network
Router translates Network (IP) Address to Data Link (MAC) Address for Next Hop
X.25, FR, Leased,
Dial-Up, ISDN

## Slide 36
Using a Router
Devices on individual sub-networks
see all traffic on sub-network
share sub-network bandwidth
3 broadcast domains
3 collision domains
No broadcast propagation
Learn network topology
support multiple interfaces
Use network addresses

## Slide 37
LAN Switch
Permits mixed 10/100 Mbps speed migration
Provides full bandwidth availability per user
Provides address filtering
Discards messages with unknown addresses
Migrate from shared to switched backbone
Operates at Data Link & Network layers
Converts a shared network into a switched network
for optimized client/server performance

## Slide 38
FDDI Dual Ring
LAN Switch Interfaces
Switch uses Data Link (MAC) Address to deliver message
Supports Virtual LANs (VLANs)

## Slide 39
Using Switches with Routers
Switched devices
dedicated bandwidth
see no collisions

## Slide 40
ATM Switch
Supports LAN emulation
Provides virtual connections
  Virtual path
  Virtual channel
Supports multiple traffic types
  Voice, video, image and data
Uses NSAP addresses with QoS
Uses cell switching
Operates at Data Link & Network layers
Provides time critical message delivery in a shared
or switched network environment

## Slide 41
Gateway
Permits protocol stack conversion
  SNA to TCP/IP
  SNA to DECNet
Permits migration strategies to be implemented
Permits enterprise integration
  Address translation
  HTML redirection
  Data encryption
  Firewall security
Supports increased performance
Operates at All 7 OSI layers
AT&T
✿

## Slide 42
A Final Thought
Switch if you can
Route if you can’t
Bridge if you must
From a “wise” network sage