## Slide 1
Chapter 8
Sections 8.1 - 8.3
Bridging & Routing Protocols
The Internet Protocol

## Slide 2
Bridge Loops
Downside
  Bridge loops corrupt Source Address Tables
  Exponentially propagates frames from LAN to LAN
    1 frame becomes 2; 2 frames become 4; etc
  Eventually all attached LANs are unusable due to corrupt SATs and excess collisions
Upside
  Bridge loops provide redundancy when Spanning Tree Algorithm is used

## Slide 3
Problem with Bridge Loops
A
B
B1
B2
Station A transmits a frame to Station B
Frame traverses entire LAN 1
Updates Bridges B1& B2 SATs
LAN 1
LAN 2
Bridges know location of Station A
but not Station B
1
2
1
2

## Slide 4
Problem with Bridge Loops
A
B
B1
B2
Bridge B1 receives frame first (closer to Station A)
Doesn’t know where Station B is located so broadcasts
frame on LAN 2
LAN 1
LAN 2
Station B receives and processes the frame
Bridge B2 receives frame and updates its SAT
(now has 2 entries - original and copy from B1)
“I got it!”
1
2
1
2

## Slide 5
Problem with Bridge Loops
A
B
B1
B2
Bridge B2 deferred to B1 due to CSMA/CD access
B2 doesn’t know where Station B is located so broadcasts
frame on LAN 2
LAN 1
LAN 2
Station B receives and processes the frame AGAIN
Bridge B1 receives frame and updates its SAT
(now has 2 entries - original and copy from B2)
“I got it!
..AGAIN??”
1
2
1
2

## Slide 6
Effect of Bridge Loops
Bridges keep moving the source address from port 1 to port 2
  Causes exponential frame propagation
  Causes SAT corruption
  Causes excess collisions due to retransmission
LAN becomes unusable
What is the Solution?

## Slide 7
Spanning Tree Algorithm
Resolves data loops
Ensures each LAN segment is serviced by only 1 bridge
Permits existence of redundant physical loops but maintains a loop free logical topology

## Slide 8
Using Spanning Tree
A
B
B1
B2
LAN 1
LAN 2
Physical topology before “Spanning Out”
1
2
1
2

## Slide 9
Using Spanning Tree
A
B
B1
B2
LAN 1
LAN 2
Active topology after “Spanning Out”
Port 2 of Bridge B1 is logically disabled
1
2
1
2
STANDBY

## Slide 10
Spanning Tree Algorithm
Defined in IEEE 802.1d
Uses a ROOT bridge to determine the active network topology
Once ROOT is selected all other bridges in the PHYSICAL topology span to create the ACTIVE topology
Active topology is a Tree which guarantees that no loops will exist

## Slide 11
Architectural Comparison
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Transport
Internet
Network
Access
OSI Reference Model
TCP/IP Layers
Network Access supports all standard Physical and
Data Link Layer protocols

## Slide 12
Routing Protocols
Routing protocols provide router-to-router communications between like routers using routing tables
Communications are
  Between autonomous system
  Within autonomous system

## Slide 13
Internet Routing Protocols
Application
Transport
Internet
Network
Access
Routing Information
Protocol (RIP)
Open Shortest Path First
Protocol (OSPF)
Interior Gateway Routing
Protocol (IGRP)
Enhanced IGRP
RIP - Standard distance vector routing protocol
OSPF - Standard link-state routing protocol
IGRP - Cisco distance vector routing protocol
EIGRP - Cisco link-state routing protocol

## Slide 14
Interior & Exterior Routing Protocols
Autonomous System X
Autonomous System Y
Exterior Routing
Protocols
- BGP
Interior Routing
Protocols
- RIP
- OSPF
Interior routing protocols route within an Autonomous System
Exterior routing protocols route between Autonomous Systems

## Slide 15
Routing Protocols
Router determines best way to reach an address through a network of nodes
Routers exchange topology information
  What links are connected
  What is the associated cost
Method of information exchange
  Distance vector
  Link state

## Slide 16
Routing Protocol Definitions
Convergence
  Time required to reach a common view of the network
Hop count
  Distance between users

## Slide 17
Distance Vector Method
Advantage
  Simple to implement
  Bases forwarding only on hop count
Disadvantage
  Large networks create large update messages
  Slow convergence
  Routing Information Protocol (RIP)
    Routing table updates every 30 seconds
    Maximum hop count is 16

## Slide 18
Distance Vector Method
Routers and neighbors periodically exchange (scheduled basis) vectors of the distance to every destination in the network
Each router builds a table of its direct connections and send the table to its neighbors
Over time all locations agree on what the network topology looks like

## Slide 19
Distance Vector Exchange
A
B
C
D
E
F
G

## Slide 20
Link State Method
Routing table changes are flooded throughout the network in tree fashion
All routers quickly agree on network topology
Each router builds its own forwarding table
Link state method is complex and processor intensive
  Uses Dijkstra algorithm

## Slide 21
Link State Method
Advantage
  Small update messages
  Understands path metrics
  Rapid convergence
Disadvantage
  Processor intensive

## Slide 22
TCP/IP Communications
TCP/IP developed by DARPA
Internet protocols communicated across LANs and WANs
Layer 3/4 protocols plus network applications
TCP/IP

## Slide 23
Application Layer
Application
Transport
Internet
Network
Access
File Transfer
- FTP
- NFS
- TFTP
E-Mail
- SMTP
Remote Login
- Telnet
- Rlogin
Network Management
- SNMP
TFTP, Telnet, and SNMP are used in router management

## Slide 24
Transport Layer
Application
Transport
Internet
Network
Access
Transmission Control
Protocol (TCP)
User Datagram
Protocol (UDP)
TCP - connection oriented, reliable, virtual circuit service
UDP - connectionless, unreliable, no delivery validation

## Slide 25
TCP Segment Fields
Source port
Destination port
Sequence number
Acknowledgment number
Header length
Reserved
Code bits
Window
Checksum
Urgent pointer
Option
Data
Calling port address
Called port address
Ensures correct sequence of data
Next expected TCP byte
Size of header in 32-bit words
Set to zero
Control functions
Number bytes sender will accept
Calculated over header and data
Identifies end of urgent data
Maximum TCP segment size
User data
Field Name Field Purpose

## Slide 26
Port Numbers
TCP ports
  FTP -- 21
  Telnet -- 23
  SMTP -- 25
RFC 1700 defines well known port numbers
End systems use port numbers to select proper application
Ports 1024 and greater dynamically assigned by sender at start of session
UDP ports
  DNS -- 53
  TFTP -- 69
  SNMP -- 161

## Slide 27
Using TCP Port Numbers
1028
23
………...
A
Z
Telnet Z
DP = 23, Send
to Telnet Appl.
SP DP

## Slide 28
TCP Open Connection Three Way Handshake
A
B
S_SYN (seq=x)
R_SYN (seq=x)
S_SYN (seq=y, ack=x+1)
S_ACK (ack=y+1)
R_SYN (seq=y, ack=x+1)
R_ACK (ack=y+1)
S_ - Send
R_ - Receive

## Slide 29
TCP Acknowledgment (Window size = 1)
A
B
S_DATA (seq=1)
R_DATA (seq=1)
S_ACK (ack=2)
S_DATA (seq=2)
R_ACK (ack=2)
R_DATA (seq=2)
S_ - Send
R_ - Receive
S_ACK (ack=3)

## Slide 30
TCP Acknowledgment (Window size = 3)
A
B
S_DATA (seq=1)
R_DATA (seq=1)
S_ACK (ack=4)
S_DATA (seq=4)
R_ACK (ack=4)
R_DATA (seq=4)
S_ - Send
R_ - Receive
R_DATA (seq=2)
R_DATA (seq=3)
S_DATA (seq=2)
S_DATA (seq=3)
R_DATA (seq=5)
R_DATA (seq=6)
S_DATA (seq=4)
S_DATA (seq=4)

## Slide 31
TCP Sequence and Acknowledge Numbers
A
Z
Sent 10
1028
23
SP DP
Seq
Ack
10
1
1028
23
SP DP
Seq
Ack
11
2
23
1028
SP DP
Seq
Ack
1
11
Received 10
Ask for 11
……...
……...
………..

## Slide 32
UDP Segment Fields
Source port
Destination port
Length
Checksum
Data
No sequence or acknowledgement fields
Applications layer provides for reliability
Used by TFTP, SNMP, NFS, DNS
Calling port address
Called port address
Number of bytes of data
Validates segment transmission
User data
Field Name Field Purpose

## Slide 33
Internet Layer
Application
Transport
Internet
Network
Access
Internet Protocol (IP)
Address Resolution
Protocol (ARP)
Reverse Address
Resolution Protocol (RARP)
Internet Control
Message Protocol (ICMP)
IP- Provides connectionless, best effort datagram delivery
ARP - Determines data link address for known IP address
RARP - Determines IP address for known data link address
ICMP - Provides control and messaging capabilities

## Slide 34
IP Datagram
Version number
Header length
Type of service
Total length
Identification
Flags
Flag offset
Time to live
Protocol
Header checksum
Source IP address
Destination IP address
IP options
Data
IP version number
Header length in 32-bit words
How to handle this datagram
Length of header + data
Provide fragmentation of datagrams, allow different MTUs in the Internet
How long to keep datagram active
Layer 4 protocol (TCP, UDP)
Header integrity check
32-bit IP address of source location
32-bit IP address of destination
Testing, debugging, security, etc
User data
Field Name Field Purpose

## Slide 35
Internet Control Message Protocol
Application
Transport
Internet
Network
Access
Destination Unreachable
Time Exceeded
Echo
Echo Reply
Information Request
Information Reply
Address Request
Address Reply
Others ...
ICMP - Carried in IP datagrams, send error and control
messages
ICMP

## Slide 36
ICMP Echo/Echo Reply
A
Z
Is Z reachable?
Yes, I’m here
ICMP Echo
ICMP Echo Reply
The Echo/Echo Reply messages are generated by the
PING command

## Slide 37
Address Resolution Protocol
131.108.3.1
131.108.3.2
IP: 131.108.3.2
Ethernet: =
IP: 131.108.3.2
Ethernet: 0800.0020.1111
Requestor checks for local subnet before sending ARP
request
I need the
Ethernet address
of 131.108.3.2
I heard the
broadcast, that’s me
Here is my
Ethernet address