## Slide 1
Network Service Definitions

## Slide 2
Connection Oriented Network Services (CONS)
States
  Establish circuit path
  Transfer data over established circuit path
  Terminate circuit path

## Slide 3
Connection Oriented Network Services (CONS)
Types of connections
  Circuit switching - physical path
    Leased circuit
      Manual setup by administrator
      Duration based on contract
    Switched circuit
      Dynamic setup by network
        Requires setup protocol
      Duration based on length of call
        Requires teardown protocol

## Slide 4
Connection Oriented Network Services (CONS)
Types of connections (Continued)
  Packet switching - logical path
    Permanent virtual circuit (PVC)
      Manual setup by administrator
      Duration based on contract
    Switched virtual circuit (SVC)
      Dynamic setup by network
        Requires setup protocol
      Duration based on length of call
        Requires teardown protocol

## Slide 5
Connection Oriented Network Services (CONS)
Technologies that use CONS
  POTS
  ISDN
  X.25 Virtual Circuits
  Frame Relay
  ATM

## Slide 6
Connectionless Network Service (CLNS)
States
  None
Transfer data
  Use dynamically created path

## Slide 7
Connectionless Network Service (CLNS)
Types of connections
  Packet switching - logical path
    Datagrams
      Dynamic setup by network
        Requires routing algorithm
      Path may change with each packet

## Slide 8
Connectionless Network Service (CLNS)
Technologies that use CLNS
  X.25 Datagrams
  SMDS
  Ethernet
  Token Ring
  FDDI
  Internet Protocol